## Slide 1: Topology Enhancements and Rel-19
RP-232444
3GPP TSG RAN #101 Bangalore, India, 11-15 September 2023
Source: Ericsson, Deutsche Telekom, China Unicom Agenda Item: 8A.2.14.1 Document for: Discussion

## Slide 2: Summary
Considerations on potential IAB evolutions
Considerations on femtos
Considerations on local breakout
Conclusions, proposals

## Slide 3: Considerations on potential IAB evolutions (1)
Some proposals seen in previous discussions (in no particular order):
  Wireless access and backhaul on UAVs (“IAB based on full gNB”)…
    Only missing piece seems to be local breakout
  gNB+UPF for local services…
  IAB for UAV, multi-hop mIAB (public safety), enhancing measurements for positioning…
  Mesh IAB for emergency cases…

## Slide 4: Considerations on potential IAB evolutions (2)
We have been building IAB for 3 releases, even adding some mobility
  Very powerful toolbox
    (Side effect: Network Controlled Repeaters)
Any functionality really missing from IAB? I.e., any missing functionality foreseen from real deployments?
  Opportunity to let ecosystem catch up; any missing features could be handled as TEI?
Proposal 1: No further work on IAB until missing features, if any, preventing the support of credible use-cases (e.g. emergency) are clearly identified

## Slide 5: Considerations on femtos (1)
Rel-8 3G/4G | Rel-18 5G
“Macro network is monolithic; RAN architecture is not flexible” | Split NG-RAN (CU-DU; CP-UP)
“CN cannot cope with femto traffic; concentration/aggregation stage is needed” | - CN, RAN are virtualized - No hard limit on n. of CP connections / cells - CU-DU split may be leveraged for CP concentration if needed
Indoor coverage problematic with early UMTS bands | Many different bands
No tools to extend/tailor coverage | - IAB - NCR - MIMO - …
No support for closed user groups | CAG, NPN

## Slide 6: Considerations on femtos (2)
Introduced in Rel-9, fully specified in Rel-12
  Specific architecture; dedicated GW, security GW, management system
  Closed/open/hybrid access and mobility added over several releases
    Membership verification in CN
  Dedicated air interface additions
  Limited functionality
    e.g. no S1-flex, X2 mobility limitations, …
  Specific local breakout (LIPA) added later
Cannot really “seamlessly migrate” this architecture to NG-RAN
Source | Target | Notes
eNB or any HeNB | open access HeNB | 
eNB, or any HeNB | hybrid access HeNB | 
hybrid access HeNB or closed access HeNB | closed access HeNB | Only applies for same CSG ID and PLMN, and if the UE is a member of the CSG cell.
Any HeNB | eNB | 
X2 handover support (Rel-12)
3GPP TS 36.300

## Slide 7: Considerations on femtos (3)
Femtos in NG-RAN are supported
  Local Area BS class applicable to femtos (R4-220263, agreed 11/2022)
    Operators may deploy femtos accordingly
Proposal 2: Pragmatic approach for femtos: start from operator requirements and consider available NG-RAN toolbox rather than pre-5G solutions

## Slide 8: Considerations on Local Breakout
Strong commonality among topology enhancement proposals
Further consideration may be justified, but:
4 “flavors” of local breakout were available in E-UTRAN:
  LIPA (only works for femtos)
  SIPTO@LN with co-located GW (also ported to UTRAN)
  SIPTO with stand-alone GW
  SIPTO above RAN (CN functionality)
Current NG-RAN, 5GC functionality allow to relocate UPF anywhere on the fly (supported by in-band signaling)
Proposal 3: For local breakout, identify gaps (if any) in available functionality; if further specification work is needed, work on a common solution to avoid multiple “flavors”

## Slide 9: Conclusions, Proposals
Consider the current stage in NG-RAN architecture lifecycle (i.e., fairly late)
Proposal 1: No further work on IAB until missing features, if any, preventing the support of credible use-cases (e.g. emergency) are clearly identified
Proposal 2: Pragmatic approach for femtos: start from operator requirements and consider available NG-RAN toolbox rather than pre-5G solutions
Proposal 3: For local breakout, identify gaps (if any) in available functionality; if further specification work is needed, work on a common solution to avoid multiple “flavors”

## Slide 10
https://www.ericsson.com/en/5g