## Slide 1: Inmarsat-Viasat operator priorities for NTN Evolution in Release 19
RP-232468, RAN4-led items
11-15th Sept 2023, 3GPP TSG RAN#101, Bangalore

## Slide 2: Introduction and General Views
NTN is a reality now, with networks being deployed as we speak.
Initial focus of deployments and product has been NB-IoT NTN in FR1, but system will evolve in time
Devices are being released to the market, even before the Release 17 and 18 work has been fully finalized
  NB-IoT NTN was arguably rushed to market with a shorter Work Item phase in R17, this meant some aspects were missed.
We must focus on:
  Features that ensure better system efficiency based on learnings from field
  Features that facilitate deployment and ROI
Release 19 is likely the last chance to improve what’s missing before too many products are already on the market.

## Slide 3: Overall Key Priorities (RAN123 and 4)
IoT NTN (specifically NB-IoT NTN)
  Network Capacity Enhancements – NB-IoT NTN Deployments are capacity limited, severely limited by the DL signalling overhead. Improving system capacity via reduced DL signalling and techniques such as CBS PUR and OCC is critical to meet the capacity demands and ensure economic viability.
  UE Location Reporting for NB-IoT - The lack of support of UE location reporting for NB-IoT NTN is a significant limitation of Rel-17 & 18 for IoT NTN that was missed in Rel-17 due to wrong assumptions. All satellite operators deploying NB-IoT NTN would need this critical feature for mobility and resource management.
  HPUE - For all FR1 IoT NTN bands including especially for NB-IoT NTN, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm).
NR NTN
  NR less than 5 MHz – At least enabling support for 3 MHz channel BW and 12 PRB transmission, as already specified by RP-232467also for NTN bands. This is critical to enable NR NTN deployments within the context of existing non-3GPP services, as well as to support EIRP limited satellites and maximize frequency reuse efficiency.
  UL Capacity/Throughput enhancements – NR NTN deployments will be severely UL limited, Rel-18 focused on UL Coverage enhancements using repetitions. Use of PRB sharing and OCC can lead to huge capacity increase whilst maintaining coverage gains. This is crucial to make NR NTN economically viable.
  HPUE – For all FR1 NTN bands, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm), reusing existing TN assumptions for FDD HPUE

## Slide 4: RAN4 Priorities
IoT NTN
HPUE - For all FR1 IoT NTN bands including especially for NB-IoT NTN, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm).
  Duty-cycle and SAR related aspects may need to be considered. FFS whether some effort is required in RAN1.
NR NTN:
NR less than 5 MHz – At least enabling support for 3 MHz channel BW and 12 PRB transmission, as already specified by RP-232467also for NTN bands. This is critical to enable NR NTN deployments within the context of existing non-3GPP services, as well as to support EIRP limited satellites and maximize frequency reuse efficiency.
HPUE – For all FR1 NTN bands, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm), reusing existing TN assumptions for FDD HPUE
DL Coverage Enhancements – Specifically focused at supporting more flexible Beam Hopping across cells and deep coverage UE Paging

## Slide 5: NR NTN less than 5 MHz
Initial NR NTN deployments will have to coexist with existing non-3GPP satellite services
Furthermore, satellites will still have limited power and will be largely EIRP-limited
Reduction of the minimum BW required can facilitate with:
  Early NR NTN deployment around existing services
  Support of EIRP-limited satellite assets
  Easier frequency resource management and reuse
As a minimum, reuse existing TN assumption of support down to 12 PRB with no impact to PSS/SSS and PBCH puncturing.
If further puncturing of PSS/SSS could be considered to achieve further minimum BW reduction, this may be very beneficial to flexibility of initial deployments
If assumptions are reused from TN (no PSS/SSS puncturing, no PBCH re-design), from our perspective, this could be handled as a normal Spectrum Related WI, as Basket WI (new channel bandwidths for existing NTN bands), entirely within RAN4.

## Slide 6: Thank You!