## Slide 1: Clarification on Carrier Re-configuration for NB-IoT NTN
RP-232532
11-15th Sept 2023, 3GPP TSG RAN#101, Bangalore

## Slide 2: Background
NB-IoT NTN is being deployed commercially as we speak
Satellite and satellite beam coverage areas are very large, with different beam sizes or tiers and will very likely include multiple NB-IoT NTN cells deployed as different carreirs in the same footprint
There are very common situations in which the network may need to move one or more UE between NB-IoT NTN carriers for load-balancing or frequency management purposes
There are also very common situations in which the network may want to instruct one or more UE to move between beams for mobility, coverage, frequency or load-balancing purposes
NB-IoT currently does not support CONNECTED_MODE mobility or any kind of Network-controlled mobility
A combination of multiple NB-IoT NTN Anchor and Non-anchor carriers may be deployed within any given satellite beam coverage area
NTN operators may have a constraint of being able to deploy only Anchor carriers in adjacent beams or within the same beam
Moreover, it is likely expected that additional Non-Anchor carriers associated with a given Anchor carrier are only deployed within the same beam, and that adjacent beams will mostly be associated with different Anchor carriers

## Slide 3: Question for clarification
It is well-understood in the specification that the UE Dedicated RRC signalling CarrierConfigDedicated-NB can be used to specify a new Non-Anchor Carrier for the UE to switch to
During Release-14, CR 2927 to TS 36.331 (R2-1705756) was approved, removing the specific restriction of the CarrierConfigDedicated-NB to “Non-Anchor” carrier
  The Following Reason for Change is provided in the referenced CR:
In principle, the mechanism provided by CarrierConfigDedicated-NB could be overloaded to be used as a means for the NTN to move UE between carriers within a beam (intra-beam load management) and between adjacent beams (inter-beam mobility). However, the usability for both load balancing and inter-beam mobility is conditional to the ability for the Network to move UE not only to a different Non-Anchor carrier, but also between different Anchor carriers.
Once the UE is assigned to a new Anchor carrier, it is expected to read the new Anchor carrier’s NPSS/NSSS/NPBCH/SIB1-NB during the next UL-to-DL gap.
However, it is not clear whether the dedicated UE signalling CarrierConfigDedicated-NB can be used to specify the UE to switch to a new arbitrary Anchor carrier that is different from the original Anchor carrier (different NB-IoT PCI) where the UE performed initial cell selection (NPSS/NSSS/NPBCH/SIB1-NB) and possibly initial access.
  Without this clarification, it’s unclear how the Network should expect the UE to behave when instructed to switch to a new Anchor carrier which has a PCI that does not correspond to the PCI of the initial Anchor Carrier, and which may assume the UE to read the new SIB1 with a new set of parameters.
Reason for change: | In Rel-13 NB-IoT, CarrierConfigDedicated-NB is used to specify a non-anchor carrier for load balance in multi-carrier cell. In Rel-14 NB-IoT, PRACH can be performed on non-anchor carrier. There may be the case that eNB wants to assign the UE to the anchor carrier by CarrierConfigDedicated-NB. So the restriction to non-anchor carrier in the description of CarrierConfigDedicated-NB is not needed.

## Slide 4: Proposal
Proposal 1: RAN2 to clarify that, at least for NB-IoT NTN from Release-17, CarrierConfigDedicated-NB can be used by the network to arbitrarily specify a new Anchor carrier for the UE to switch to, that is different from the Anchor or Non-Anchor carrier where the UE performed its initial access.

## Slide 5: Thank You!