## Slide 1: 4G Timing as a Service in Rel 19
Source: Vodafone
Agenda Item: 8A.2.15
RP-232550
3GPP TSG RAN #101, Bangalore, India
September 11-15, 2023

## Slide 2
A surprising number of services use “accurate time” as a key component.
Many “users of accurate time” are unknown to 3GPP
Most “users of accurate time” use clocks derived from GPS
Many users now realise that GPS signals can be blocked or spoofed
3GPP release 18 supports the use of 5GC-NR to provide “time as a service”
  It allows the RAN to tell the UE the accuracy of the cell’s broadcast time
  Provision of this information is subject to a subscription
As with most ‘machine’ type services, full national coverage is very useful
  At least in developing markets (e.g. Africa) full national coverage of NR is not imminent
  Support on both LTE and NR could enable full coverage
  Without full coverage, potential customers will adopt non-3GPP solutions
Rollout of some NR-TDD, and provision of back up to GPS timing, encourages operators to enable both LTE FDD and NR cells to be time synchronised.

## Slide 3
Release 11, LTE SIB 16 can broadcast time to a fine granularity – but unknown accuracy
SIB 16 indicates the time of the SFN boundary  in combination with “accuracy”, the time signal could be better than 1ms. This is suitable for applications required by e.g. electricity generators.
EPC-LTE “timing as a service” could be provided by:
  Dedicated mode RRC signalling to convey the accuracy of the cell’s timing to the UE
  S1-AP signalling from the MME to the RAN to control whether the eNB provides the accuracy information to the UE.
  No new radio reference signals are needed.
  EPC changes (e.g. HSS to MME signalling) can be copied from 5GC design
SA2 discussion has indicated concerns on RAN workload
 TSG RAN should indicate to SA that this work can be conducted as either TEI-19 or “SA alignment” in Rel 19.

## Slide 4: Thank you