## Slide 1: Discussion on security for UE configuration provided by DU
3GPP TSG RAN #101 RP-232552
Bangalore, India, 11th – 15th September 2023
Agenda Item: 8A.2.15
Source: Intel Corporation
Document for: Discussion

## Slide 2: Motivation/limitations of current architecture
Current RAN architecture prevents fast, secure and reliable control signalling to the UE
Current architecture creates additional security risk by increasing use of MAC CEs
  MAC CEs now carry information that can be considered sensitive
  Use of MAC CEs primarily to avoid delays from using RRC delay
  Security risks already being raised by SA3 and academia
Current architecture has unnecessary signalling delay and dependency between DU and CU for lower layer configuration
  DU generated RRC signalling to control L1 and L2 are sent to CU for security and encapsulation in RRC Reconfiguration message
  Larger RRC processing delay of RRC Reconfiguration message
Configuration information from DU delivered to UE by MAC-CEs less reliable than that delivered by RRC (HARQ only, no RLC)

## Slide 3: Proposed objective
Objective: Specify security for DU generated signalling
  Suggested architectural changes
    Support PDCP termination at DU for security.
    Support direct transfer of RRC messages generated at DU to the UE
      Allow DU to generate RRC messages for DU configuration (e.g. CellGroupConfig) and send directly to UE without transferring to CU
    Reduced RRC processing delay
      Introduce “simpler” RRC messages (similar configuration contents as MAC CEs) generated at DU
  Possible specification approach
    New RRC message to encapsulate RRC-DU and MAC-CE like control information
    Define new SRBx for RRC-DU directly from DU to UE
    PDCP for SRBx at DU with DU specific security keys
    Security for MAC CE
      Encapsulate MAC CE in DU-RRC
      Define simple RRC message containing same information as MAC CE

## Slide 4: Summary: Motivation and objective
Motivation
  Current RAN architecture prevents fast, secure and reliable signalling of lower layer configurations
    Security risk from using MAC CEs to avoid RRC delay
    Longer delay in configuration by DU generated signalling sent via CU
    Less reliable transmission (no RLC) for MAC CEs
Objective: Specify security for UE configuration provided by DU