## Slide 1: Discussion on Rel-19 Mobility enhancements
3GPP TSG RAN #101 RP-232553
Bangalore, India, 11th – 15th September 2023
Agenda Item: 8A.2.6
Source: Intel Corporation
Document for: Discussion

## Slide 2: NR Mobility RAN2
R15
Basic mobility support, e.g., handover between NR cells, handover between LTE and NR cells
R16
0ms interruption handover, i.e., DAPS (Dual Active Protocol Stack)
High reliability handover, i.e., CHO (Conditional Handover)
R17
CPA, i.e., Conditional PSCell Addition
MN initiated and SN initiated inter-SN CPC
Intra-SN CPC, i.e., intra-SN conditional PSCell change without MN involvement
Dual connectivity, e.g., EN-DC and NR-DC
Activation/deactivation of SCG for power saving
R18
Mobility latency reduction (LTM)
Optimize MR-DC mobility using CHO (CHO including target MCG and candidate SCGs)
Mobility enhancement in the case of frequent SCG changes when operating FR2 (selective activation of SCG)
Fast Scell activation based on temporary RS
LTE eNB or 5G NR gNB
5G NR gNB
simultaneous connection
  LTE-NR/NR-NR Dual connectivity
  NR mobility evolving roadmap
  Characteristics of conditional handover/ PSCell change, i.e., multiple candidate cells and condition evaluation
There are still some leftovers to consider for R19

## Slide 3: Rel-19 mobility enhancements: Motivation and objectives (1/2)
Overall motivation:
  R18 mobility enhancements brought new mechanisms such LTM, selective activation, RACHless HO
    Only limited scenarios were considered in the initial release
  Solutions should be extended to cover other scenarios in Rel-19
  But contain the overall work scope to scenarios that were discussed
Specific objectives:
  LTM for PCell in R18 is not expected to be applicable with SCG configuration
    NR-DC is an important feature for NR
    Releasing and subsequent addition of SCG during PCell LTM switch can severely impact throughput and increases signalling
    Objective: Support LTM for PCell with SCG configuration
  LTM for Rel-18 is supported only for intra-CU scenario
    UEs at inter-CU border cannot benefit from LTM
    Objective: Support inter-CU LTM

## Slide 4: Rel-19 mobility enhancements: Motivation and objectives (2/2)
Specific objectives (contd.)
  LTM for Rel-18 does not support CHO like operation
    CHO is considered a useful feature for L3 mobility for HO performance improvement
    Objective: Introduce CHO for LTM
  HARQ is reset during LTM operation
    Continuation of HARQ will avoid data interruption
    Objective: Support HARQ continuation during LTM operation
  Extend RACHless operation
    RACHless operation can reduce interruption during HO
    Supported in Rel-18 for limited scenarios for L3 mobility when TA in target is same as source or 0
    LTM supports early TA and RACHless
    Early TA with RACHless HO can be extended also for L3 HO
    Objective: Support LTM based Early TA and RACHless also for L3 HO
  Rel-18 supports selective activation only for SCG
    During initial Rel-18 WID discussion, there was support for also for selective activation of the MCG
    Objective: Support selective activation of the MCG

## Slide 5: Summary of objectives for Rel-19 Mobility enhancements
Proposed objectives for Rel-19 mobility enhancements
  Support LTM for PCell with SCG configuration
  Support inter-CU LTM
  Introduce CHO for LTM
  Support HARQ continuation during LTM operation
  Support LTM based Early TA and RACHless also for L3 HO
  Support selective activation of the MCG
  Selected leftovers from Rel-18 feMOB WI scope that could not be completed