## Slide 1: Discussion on Rel-19 XR enhancements
3GPP TSG RAN #101 RP-232554
Bangalore, India, September 11th – 15th 2023
Agenda Item: 8A.2.8
Source: Intel Corporation
Document for: Discussion

## Slide 2: End-to-end 5G system for XR use cases in Rel-19
NOTE: Coordination expected with SA4, SA2, e.g., to identify additional XR traffic characteristics to consider and new target use cases/requirements of interest
3GPP continues enhancements of 5G system (UE/NG-RAN & 5G-CN) considering XR-specific characteristics:
XR specific traffic in DL and UL with 1 or more streams e.g.
I and P streams
Video and audio/data streams
FOV + omnidirectional view
Pose/control traffic
Multiple devices associated to one or multiple user(s) in same or different locations
Differentiation of XR packets or group of XR packets (i.e. “PDU set”)
Enhancements to NG-RAN and 5G CN to better support XR traffic characteristics not covered in Rel-18 XR e.g.
Multi-modality
Inter-PDU set dependency
Enhance XR operation when operating with 5G features of interest, such as, URLLC, positioning, sidelink (as studied by SA1 in Rel-19 Metaverse)

## Slide 3: Summary on enhancements to XR operation
In Rel-18, RAN and UE are enhanced to consider XR specific information although some topics of interest were not pursued due to lack of time/interest or foreseen impacts. SA1 Rel-19 TR 22.856 captures Metaverse use cases (which are a super set of XR).
C-DRX support of XR traffic with non-integer periodicities
Multiple CG PUSCH transmission occasions in a period of a CG PUSCH configuration
BSR enhancements considering XR characteristics and including delay reporting of UL buffered data
Discard operation for intra-PDU set
Support of Multi-Modal XR data (i.e., different streams of an application) e.g., synchronization of related streams, multiple C-DRX active simultaneously
Measurement gap enhancements to mitigate the impact on the XR traffic
Differentiated handling (e.g., reliability, prioritization) of different PDU set importance in a given QoS flow
PDU set discard enhancements due to inter-PDU set dependencies
Rel-18
Rel-19
Retransmission-less CG enhancement for XR

## Slide 4: XR Traffic with Multi-modal Data
Motivation:
In Rel-17, SA WGs defined Multi-modal Data as data coming from different kinds of devices or sensors to one or different kinds of destinations (i.e., one or more UEs) that are required for the same task or application. ​
  Multi-modal data refers to data from some advanced XR applications which generates multiple types of traffic flows (e.g., video/audio stream, as well as sensor data for more immersive experience)
However, RAN WGs have not enabled optimizations targeting this operation
Proposed WI Objective:
Enable RAN/UE enhancements targeting XR traffic with Multi-modal Data (i.e., different/multiple data streams of one XR application) including the study of:
  Synchronized or coordinated transmissions
  Multiple active C-DRX configurations simultaneously
  UE assistance/feedback information

## Slide 5: Differentiated PDU Set Handling in a QoS Flow
Motivation:
Rel-18 introduced enhanced discard mechanism (based on PSI and congestion), triggers based on exceeding tolerable delay but does not make differentiation on the reason why a packet fails (e.g., bad radio signal conditions, collision, congestion).
From system performance perspective, it is better for RAN enhancements to focus on ensuring packets are delivered successfully to the receiver end point (rather than the mechanism to discard them in case delivery is unsuccessful).
  PDUs with higher importance could be provided with higher reliability or more robust mechanism over the radio. This could be enabled or selectively applied (e.g., based on radio conditions or PSER or PSDB).
Proposed WI Objective:
Differentiated handling (including e.g., reliability, prioritization) of PDU sets with different importance (i.e., PSI) in a given QoS flow , considering the study of:
  RLC bearer switching (i.e., Single PDCP entity mapped to multiple RLC AM bearers)
  Selective duplication (i.e., Multiple RLC UM bearers as required to support different handling of the PDUs with different PDU set importance)

## Slide 6: Further Enhancements associated with PDU Sets
Motivation:
PSIHI (PDU Set Integrated Handling Information) indicates whether all PDUs of the PDU Set are needed by the application layer in the receiver side
In Release 18, discard is enhanced for intra-PDU set with the understanding that a PDU Set is considered as successfully delivered only when all PDUs of a PDU Set are delivered successfully.
Inter-PDU set discard can be used when all the PDUs of the dependent PDU sets are needed by the application layer in the receiver
  if a related packet from any of the PDU sets is discarded, the remaining PDUs of all the dependent PDU sets can be discarded
Proposed WI Objective:
PDU set discard enhancements for inter-PDU Set dependencies

## Slide 7: Measurement gap for XR
Motivation:
To minimize impact of measurements to XR traffic while also reducing the scheduling restrictions (e.g., to reduce delay and discard of packets), as initially discussed in Rel-18 XR.
  NOTE-1: This area of enhancement is not XR specific.
  NOTE-2: RAN4 Rel-19 material (RWS-230460) also includes measurement gap related enhancement for time-sensitive or reliability-sensitive types of services which could apply to XR.
Proposed WI Objective:
Measurement gap enhancements to mitigate the impact on the XR traffic
  Note: This objective can also be addressed in the RAN4 led WI on measurement gap enhancements

## Slide 8: Proposed WI Objectives on Rel-19 XR
Enable RAN/UE enhancements targeting XR traffic with Multi-modal Data (i.e., different/multiple data streams of one XR application) including the study of:
  Synchronized or coordinated transmissions
  Multiple active C-DRX configurations simultaneously
  UE assistance/feedback information
Differentiated handling (including e.g., reliability, prioritization) of PDU set with different importance (i.e., PSI) in a given QoS flow , considering the study of:
  RLC bearer switching (i.e., Single PDCP entity mapped to multiple RLC AM bearers)
  Selective duplication (i.e., Multiple RLC UM bearers as required to support different handling of the PDUs with different PDU set importance)
PDU set discard enhancements for inter-PDU Set dependencies
Measurement gap enhancements to mitigate the impact on the XR traffic
  Note: Could be addressed in RAN4 led WI on measurement gap enhancements
-