## Slide 1: Discussion on Rel-19 AIML for NG-RAN and mobility
3GPP TSG RAN #101 RP-232555
Bangalore, India, September 11th – 15th 2023
Agenda Item: 8A.2.9
Source: Intel Corporation
Document for: Discussion

## Slide 2: Objectives for AI/ML NG-RAN Rel-19
OBJ1: Support AI/ML in NG-RAN for NR-DC
OBJ2: Support model inference at gNB-DU
OBJ3: Model/Model Info sharing among NG-RANs
OBJ4: R18 leftover and new NG-RAN use cases

## Slide 3: OBJ1: Support AI/ML in NG-RAN for NR-DC
Motivation:
  During Release 18 work item, RAN3 mainly focused on standalone (SA). However, NR-DC is an important commercial deployment scenario for 5G network, supporting AI/ML NG-RAN in NR-DC is important.
Objective: Support AI/ML in NG-RAN for NR-DC
  Study and specify signaling support for use cases including (but not limit to): NWES, load balancing, mobility optimization

## Slide 4: OBJ2: Support model inference at gNB-DU
Motivation:
  Model inference is not considered to be deployed in gNB-DU during Release 18. Expanding model inference in gNB-DU brings more flexibility for resource optimization.
Objective: Support model inference at gNB-DU
  Study and specify signaling support for use cases include (but not limit to): NWES, load balancing, mobility enhancement (LTM/L1/L2)

## Slide 5: OBJ3: Model/Model Info sharing among NG-RANs
Motivation
  During Release 18, AI/ML models are separately trained in different network entities. More accurate/precise decisions can be obtained by updating ML model to a general model with more data and model information across multiple NG-RANs.
  During Rel-18 SA2 Enablers for Network Automation for 5G phase 3 WI, ML model sharing between different vendors are supported. For example, introducing interoperability indicator, ML model interoperability information, etc in Analytics ID for ML model sharing, federated learning between NWDAFs, etc.

## Slide 6: OBJ3: Model/Model Info sharing among NG-RANs
Motivation (Cont.)
  Optimizing UE performance feedback Collection
    Reducing the amount of signaling for performance feedback collection, e.g. massive reporting of UE’s performance by utilizing model/model information sharing
      In Rel-18, periodic and one time UE performance feedback reporting are supported to collect the performance feedback of impacted UEs (by AI/ML actions). The UE may be configured with different reporting periodicity or reporting time, which may lead to massive messages for reporting UE performance feedback and/or UE trajectory information.
    Reflecting the performance of both handed-over UEs and existing UEs’ performance at the impacted target NG-RAN node
      In Rel-18, the target NG-RAN node will only report the performance of impacted UEs (handed-over UEs). However, this AI/ML action may also impact the existing UEs at the target NG-RAN node, which is not expected to be negative. Such performance information is not acknowledged by the source NG-RAN node who initiates impacted UEs’ handover (caused by AI/ML prediction).
      Introducing signaling(s) to exchange the existing UEs’ performance at the target NG-RAN node is complex and burdensome.
    Instead of using massive signaling to exchange UE performance feedback and/or UE trajectory, NG-RAN node can simply exchange model/model information to synchronize the trained model, which implicitly includes all UEs’ performance at neighbouring NG-RAN node. The source NG-RAN node can replace/update the model accordingly.

## Slide 7: OBJ3: Model/Model Info sharing among NG-RANs
Motivation (Cont.)
  Improve prediction accuracy by overcoming unavailability of predicted information from neighbouring NG-RAN node
    In Rel-18, different failure cause values are introduced to indicate failure cause of not reporting the requested predicted information, e.g. due to timing issue, etc. Prediction at source NG-RAN node may not be accurate/optimized due to missing some predicted information at neighbouring NG-RAN node.
    Exchanging model/model information has no time constraint. It can help to avoid collecting detailed predicted information which may be temporarily unavailable, and further improve prediction accuracy at the source NG-RAN node.
  To improve regional performance optimization
    With data/model sharing across NG-RAN nodes, distributed/federated learning may be used to improve AI/ML model at each specific NG-RAN nodes by jointly considering regional environment.
  Sharing optimized AI/ML model from neighbouring NG-RAN nodes
    Model sharing or transfer learning for new deployed NG-RAN node;
    Model sharing if the neighbouring NG-RAN node is leak of model training capacity due to high workload
    Depending on the progress of AI/ML for air interface, if model transfer/delivery is supported and gNB is the termination of model transfer/delivery, model sharing between NG-RAN nodes is needed to support UE mobility

## Slide 8: OBJ3: Model/Model Info sharing among NG-RANs
Objectives: Model/Model Info sharing among NG-RANs over Xn interface
  Distributed model/model information sharing between NG-RANs for federated/distributed learning, e.g. for new deployed NG-RAN nodes
  Support interoperability, e.g. for NG-RAN nodes with high workload which lack resource for model training
  Joint network optimization between NG-RANs for regional environment
Fig. AI/ML model coordination/sharing across NG-RANs

## Slide 9: OBJ3: Model/Model Info sharing among NG-RANs
Potential specification impact: Exchange model/model information over Xn interface, including
  New procedure for model sharing, including request, response, update, etc
  Model Interoperability information
  Vendor ID
  Model ID
  Correlation ID for identifying the relative Federated Learning/Distributed Learning procedure
  Model accuracy information
  Model information (e.g. layer number, gradient, etc)

## Slide 10: OBJ4: R18 leftover and new NG-RAN use cases
Potential R18 leftover
  AI/ML support for CP-UP separation scenario
Study potential new use cases and benefits for AI/ML in NG-RAN
  Study AI/ML solutions for below use cases:
    DC mobility enhancement
    Coverage and capacity optimization
    Network slicing
  Study specification impact on data collection and signaling support within existing NG-RAN interfaces and architecture

## Slide 11: Potential New Use Case for Rel-19

## Slide 12: AI/ML for Mobility use case - Motivation
Study benefits of AI/ML on mobility especially considering challenges in HO, e.g.
  Power consumption/signaling overhead due to high quantity of measurements and reporting of neighboring cells
  Increased handover failure/ping-pong ratio/service interruption in very dense/high-frequency deployments
  Early handover command provided to UE in a more stable radio link condition than legacy HO
Fig. AI/ML based Mobility

## Slide 13: AI/ML for Mobility use case – Potential Enhancements
Evaluate performance benefits of AI/ML based algorithms
  AI/ML framework/evaluation methodology from Rel-18 AI/ML SI should be used as a baseline but the mobility specific AI/ML characterization should be studied
  Performance evaluation between network-sided model (i.e. RAN3 Rel-18 AI/ML in NG-RAN enabled mobility optimization) and UE-sided model
  Performance evaluation to focus on HOF rate, ping-pong rate, etc
Potential applications of AI/ML to mobility use case:
  Use AI/ML to predict UE mobility/trajectory/measurements and trigger HO based on predictions
  Use AI/ML to dynamically select the HO parameters based on multiple factors, e.g. UE location, etc.