## Slide 1: Considerations for R19 work on NCR Enhancements
Philips International B.V.

## Slide 2: NCR enhancements
NCR is an important enabler for the provision of fill-in coverage in difficult locations
  Rel-18 work limited the scope to fixed, operator-controlled installations using a common band for backhaul and control paths
NCR should be enhanced to support more flexible operation. By providing swift resolution of coverage problems in ad-hoc deployments, for example, enhanced NCR becomes an important enabler for emergency and public safety applications.
  Self-installation and configuration
  Flexible multi-band operation
  Effective management of link quality in backhaul and access channels

## Slide 3: NCR enhancements
Scope for Enhanced NCR in Rel-19
  multi band operation – it should be possible for the Fwd and control paths to operate in different bands
    For example, the Fwd path might operate in FR2, control in FR1
  Self-installation and configuration – it should be possible for an Enhanced NCR node to find an NCR-ready gNB and negotiate beam settings and other parameters without requiring OAM configuration
  Fwd path monitoring – when the control and backhaul paths use different links, it should be possible for the NCR node to provide the gNB with information on backhaul DL and access UL channel qualities
  Multi-network usage – It should be possible for the Enhanced NCR node to work with multiple networks and, optionally, allow the Fwd path to be shared by multiple networks
The NCR framework could also be used as the basis for RIS operation
  Reflective Intelligent Surfaces have been put forward as a candidate technology for Rel-19
  RIS offers a similar 'on-channel' repeater function
  Reflected signals can also be steered in beams