## Slide 1
0
Considerations on XR enhancement for Rel-19
3GPP TSG RAN RP#101 RP-232598
Bangalore, Sept. 11th-15th, 2023
Agenda Item: | 8A.2.8
Source: | CMCC
Document for: | Discussion

## Slide 2
Motivation
R18 SI/WI leftover
  Enhancement for XR capacity
R19 XR feature
  Support for Multi-modal traffic flows
Content

## Slide 3
Motivation
General observations
Rel-18 SI/WI leftover： Rel-18 XR capacity improvement enhancement focuses on video traffic. However, the statistical characteristics of video packet has not been fully exploited in BSR. Rel-19 XR feature: Research on synchronization and coordination for multi-flow of single UE is desired: New traffic flows may be added to XR service ,e.g., haptic data from XR glove, in Rel-19; Multi-modal flows can be transmitted at the same time to one destination for further processing in a coordinated manner, in terms of QoS coordination, traffic synchronization, etc; The growth of XR traffic in the future will impose more stringent requirements on network capacity.

## Slide 4
Rel-18 SI/WI leftover: Capacity
Background
Video packet follows truncated Gaussian distribution and composes the vast majority of XR UL traffic, while current BSR table is exponential. Simulation shows that Gaussian BSR table has the least quantization error compared with linear or exponential table. With delay status reporting mechanism introduced in Rel-18, current MAC scheduler can not perform remaining time based scheduling but only assign physical resource based on LCG priority, causing starving issue for low priority LCG. PUSCH TTI in TDD is not constant even in the same slot format, thus a constant threshold for triggering remaining time reporting is not suitable.
Study further capacity improvement for XR [RAN2] Specify Gaussian BSR table for least quantization error [RAN2]. Specify resource allocation mechanism based on remaining time [RAN2]. e.g., TTI triggered MAC CE containing remaining time and corresponding buffer status for TDD
1080p@60fps, NVENC
Objective

## Slide 5
Rel-19 new feature: Multi-modal flows
Background
For multi-modal flows, inter-flow synchronization and coordination from one UE is necessary due to separate devices connected to one terminal, e.g., separate glove and glass, and multi-camera capture. For single UE, synchronization and coordination of QoS flows is also needed. Can be studied in inter-PDU set dependency.
Study multi-modal related enhancement for XR [RAN2, RAN3] Specify inter-PDU set dependency for integrity scheduling [RAN2] the UE will prioritize multiplexing the data in one PDU set or co-ordinated multiple PDU sets into same MAC PDU(s) the UE will prioritize multiplexing a retransmission and a new transmission of another data of one PDU set or co-ordinated multiple PDU sets into same MAC PDU(s) Specify inter-PDU set dependency for differentiate scheduling [RAN2] Specify L2 architecture enhancement, e.g., splitting RLC for different PDU sets in one QoS flow [RAN2] Specify inter-PDU set discard enhancement Specify inter-flows synchronization and coordination[RAN2] Specify scheduling enhancement for data transmission alignment, e.g. LCP enhancement, DCI shceduling enhancement Specify further assistance information for multi-modal [RAN2, RAN3]
Objective
Multi-modal Data: Multi-modal Data is defined to describe the input data from different kinds of devices/sensors or the output data to different kinds of destinations (e.g. one or more UEs) required for the same task or application. Multi-modal Data consists of more than one Single-modal Data, and there is strong dependency among each Single-modal Data. Single-modal Data can be seen as one type of data.

## Slide 6
Thank you!