## Slide 1
Moderator (Huawei)
Agenda item: 8A.2.4
Summary of Ambient IoT Proposals for Release 19
3GPP TSG RAN Meeting #101 RP-232614
Bangalore, India, September 11-15, 2023

## Slide 2
General overview of RAN#101 contributions on Rel-19 Ambient IoT
28 companies submitted proposals for Ambient IoT in Rel-19 (agenda 8A.2.4). 14 out of 17 companies included Ambient IoT in the package in their Rel-19 overview Tdocs (agenda 8A.2).
RWS-230488 (RAN Chair’s summary of Rel-19 workshop):
  Based on the outcome of the study at RAN, a WG-level study item is expected to continue in Rel-19
    Need to have focused scope on issues such as device type(s), deployment scenario(s), topology option(s), etc. and,
    Need to address cross-TSG-dependencies
  Is there a strong need and is it feasible to convert the study and hence specify ambient IoT in Rel-19?
  In RP-231540, the RAN Chair allocated [3~4] TU in RAN1, [2] TU in RAN2, [2] TU in RAN3.
  It is expected to have impact to RAN4, and to coordinate with the SA project on Ambient IoT.

## Slide 3
Justification for further study/work on Ambient IoT
The justification for a project on Ambient IoT in 3GPP has been made clear already since Rel-18, with studies in both RAN and SA, including the Study on Ambient IoT (Internet of Things) in RAN (FS_Ambient_IoT_RAN) developing TR38.848. Detailed justification for the study can be found in the Rel-18 SID (RP-232404).
Motivation for Rel-19 study/work follows from justification of the study in Rel-18, to provide devices with complexity and power consumption orders of magnitude lower than the existing 3GPP LPWA technologies (e.g. NB-IoT and eMTC), that shall address use cases and scenarios that cannot otherwise be fulfilled based on existing 3GPP LPWA IoT technologies.
Some contributions submitted to RAN#101 emphasized the market urgency and the need for 3GPP to provide normative specifications for Ambient IoT in Rel-19, since existing cellular devices may not work well with energy harvesting due to their peak power consumption of higher than 10mW.

## Slide 4
Summary of the proposals submitted to RAN#101
Discussion on SI vs. SI+WI for Rel-19 is expected at RAN#102
SI-only vs. SI+WI in Rel-19
The views are still split with no overwhelming majority either way. A few companies did not express a clear preference at this time, and suggested that a decision may not be needed at the start of the release.
  Many companies emphasized in their contributions that whether SI-only or SI+WI is decided for Rel-19, the focus should be on a small subset of deployment scenarios and topologies, and possibly also a subset of the device types, defined in TR 38.848.

## Slide 5
Summary of the proposals submitted to RAN#101
Prioritization between Devices A, B and C
The views are roughly equally split
  ~12 companies included Device type A in their priority
  ~15 companies included Device type B in their priority
  ~16 companies included Device type C in their priority
Among those, ~8 companies proposed to include all 3 device types in the scope of Rel-19
Potential prioritization for Rel-19 among the device types can be discussed at RAN#102

## Slide 6
Summary of the proposals submitted to RAN#101
Connectivity topologies and Deployment scenarios
TR38.848 provides a categorization by 5 deployment scenarios incorporating the relevant connectivity topologies. Most companies, however, still expressed their views directly on their preferred prioritization among the connectivity topologies, while a few companies expressed their preferences directly on the deployment scenarios.
Based on the recommendation agreed in TR 38.848, RAN#102 is expected for further down-select among the following:
  Deployment scenario 1 with Topology 1
  Deployment scenario 2 with Topology 1
  Deployment scenario 2 with Topology 2
  Deployment scenario 4 with Topology 1
  Deployment scenario 4 with Topology 3

## Slide 7
Summary of the proposals submitted to RAN#101
Type of spectrum
Not all companies expressed their views in Tdocs submitted to RAN#101, but views were expressed during the Rel-18 RAN SI discussions.
Based on the recommendation agreed in TR 38.848, FR1 licensed spectrum is recommended, and RAN#102 is expected to decide on selection or prioritization between FDD and FDD/TDD
RAN is also recommended to down-select to one or more of:
  Spectrum in-band to NR, in guard-band to LTE/NR, and in standalone band(s)

## Slide 8
Possible list of objectives for a WG-level study item
      Evaluations and remaining feasibility assessments
          Device architecture and characteristics
        Evaluation methodology and assumptions
        Design target evaluations
        Coexistence evaluations
      Physical layer study on:
        Waveform and multiple access
        Frame structure and numerology
        Modulation and channel coding
        Physical layer signals/channels
        Physical layer procedures including initial access and mobility, scheduling, (H)ARQ, power control, etc
      Higher layers study on:
        Compact protocol stack and lightweight signaling procedure, including mobility aspects
          Control plane functionalities, including CN connectivity
          User plane functionalities
          Security aspects (*Note: This does not necessarily mean security has RAN impact)
      RAN3 aspects for study:
        Enabling necessary CN-RAN signalling
        RAN architecture aspects, if any
      RAN4 aspects for study:
        Feasibility study of BS/UE/device architectures
        Link budget study
        Coexistence analysis
        RRM

## Slide 9: References (Tdocs in agenda 8A.2.4)
TDoc | Title | Source
RP-231542 | Rel-19 study on Ambient IoT | Nokia, Nokia Shanghai Bell
RP-231553 | Views on scope for Ambient-IOT in Rel-19 | Qualcomm Incorporated
RP-231574 | Consideration on Rel-19 Ambient IoT | New H3C Technologies Co., Ltd.
RP-231588 | Deutsche Telekom’s Ambient-IoT objectives | Deutsche Telekom AG
RP-231602 | Discussion of R19 work on Ambient IoT | Futurewei
RP-231608 | Views on Ambient IoT for R19 | Xiaomi EV Technology
RP-231626 | On Rel-19 Ambient IoT | Ericsson
RP-231750 | Apple Views on Ambient IoT for Rel-19 | Apple
RP-231774 | Discussion on study of ambient IoT in Rel-19 | OPPO
RP-231792 | Rel-19 Ambient IoT (RAN1-led) | vivo
RP-231847 | Views on Rel-19 Ambient IoT | Haier
RP-231854 | Ambient IoT considerations in Rel-19 | Spreadtrum Communications
RP-231869 | Ambient IoT | NEC
RP-231917 | Motivation of study on Ambient IoT | Kyocera
RP-231985 | On Rel-19 Ambient IoT | InterDigital, Inc.
RP-232024 | Samsung's views on scope of Ambient IoT | Samsung
RP-232064 | Study of Ambient IoT | CATT
RP-232075 | Views on ambient IoT for Rel-19 | NTT DOCOMO, INC.
RP-232120 | Ambient-IoT in Rel-19 | Fujitsu Limited
RP-232160 | Views on Rel-19 Ambient IoT | ZTE, Sanechips
RP-232188 | Views on Ambient IoT for Rel-19 | Lenovo
RP-232195 | Proposals on Ambient IoT in Rel-19 | LG Electronics
RP-232207 | Views on Rel-19 Ambient IoT | China Mobile International Ltd
RP-232294 | Considerations for R19 work on Ambient IoT | Philips International B.V.
RP-232415 | Ambient IoT work in Rel-19 | Huawei, HiSilicon
RP-232419 | Views and considerations for Rel-19 work on Ambient IoT | NOVAMINT
RP-232534 | Views on Ambient IoT in R19 | VODAFONE Group Plc
RP-232579 | Ambient IoT | CEWiT