## Slide 1
Moderator (Huawei)
Agenda item: 8A.2.5
Summary of Network Energy Savings Proposals for Release 19
3GPP TSG RAN Meeting #101 RP-232615
Bangalore, India, September 11-15, 2023

## Slide 2
General overview of RAN#101 contributions on Rel-19 network energy savings
32 companies submitted proposals for further work on network energy savings in Rel-19
15 out of 17 companies included network energy savings in their Rel-19 overview Tdocs (agenda 8A.2)
RWS-230488 (RAN Chair’s summary of Rel-19 workshop):
  Further enhancements of network energy saving (NES) are expected to continue in Rel-19
    If so, the enhancements should be based on the study outcome in Rel-18
    Need to focus on areas which can provide significant power savings with reasonable standardization efforts

## Slide 3
Justification for further work on network energy savings
Proposals on further work on network energy savings were motivated by the proponents with the following justifications:
  Many techniques evaluated in TR 38.864 were shown to bring substantial NES gains, but were not included in Rel-18 due to limited time and capacity in RAN WGs.
  Rel-18 has focused primarily on RRC Connected, user specific signals and channels, and low load scenarios.
  Rel-19 could address network energy savings in different deployment scenarios and operating points of the system than specified in Rel-18.
    E.g. Rel-18 NES limits SSB-less operation for SCell(s) to inter-band cases for FR1 co-located scenarios.

## Slide 4
Summary of the main directions proposed at RAN#101
One direction was proposed by almost all sources, with a few open questions
  On-demand SSB transmission and on-demand SIB1 transmission (documented in TR38.864)
    Focus:
      On-demand SIB1/[SSB] for idle UEs
      On-demand SSB ([and possibly other DL signals]) for Scell for connected UEs
    Possible triggering methods to be considered:
      Based on UE uplink wake-up-signal (e.g. non-CA case), if so whether the WUS can be based on an existing signal (as a starting point, if possible) or a new signal
      Based on cell on/off indication via backhaul
      Based on Scell activation/deactivation signaling
    Whether to target the design of a simplified SSB

## Slide 5
Summary of the main directions proposed at RAN#101
Another group (G1) of proposals were contributed by nearly half of the sources (12~13)
  [SSB]/SIB1-less operation in multi-carrier scenario for (documented in TR38.864)
    [SSB]/SIB1-less for non-anchor NES cell for UEs in IDLE/INACTIVE state, where it is assumed that another carrier (an anchor cell) is available for the UE
    Some discussion may be useful for the schemes when compared with on-demand SSB/SIB transmission, in terms of targeting scenarios, benefits etc.
    Some concerns were expressed on this proposal in the offline drafting session
  Adaptation of common signal/channel transmissions (documented in TR38.864)
    Proposals are fragmented between skipping transmission occasions, adapting periodicities/patterns, simplified/compact design of some channels
    Proposals are fragmented on channels to target (e.g. SSB, SIB1, common PDCCH, paging, PRACH occasions)
    Proposals are fragmented between dynamic or semi-static adaptation

## Slide 6
Summary of the main directions proposed at RAN#101
  A second group (G2) of proposals was contributed by 5~10 sources
  Cell DRX/DTX for UEs in idle/inactive modes (as an extension of Rel-18 cell DRX/DTX)
    Only 2 sources proposed to further identify additional physical channels to be turned off during non-active time of cell DTX/DRX in RRC Connected mode
    Only 2 sources proposed dynamic switching among multiple cell DTX/DRX configurations. Note that there are still on-going Rel-18 discussion on this aspects.
    Some concerns were expressed on this proposal in the offline drafting session
  Multi-TRP adaptation mechanisms
    Proposals are fragmented and the scope could be very broad
    Details could include measurements, CSI feedback, power control, PDCCH/PUCCH/PUSCH/PDSCH repetition, single-DCI based scheduling, multi-DCI based scheduling, SRS transmission, TCI configuration, beam management, beam failure recovery, radio link monitoring, cell (re)selection, handover, initial access, etc.
  Aspects discussed but not specified in Rel-18
    Proposals are fragmented and very generic, including BM/TCI enhancements, UE complexity/CSI payload reduction, PUCCH resource adaptation

## Slide 7
Summary of other directions proposed at RAN#101
  A third group (G3) of proposals was contributed by just one or two sources, in many cases such techniques were not studied in Rel-18:
    UE group-common or cell-specific BWP configuration, adaptation and/or switching.
    Group cell switch
    Power domains studied in R18 (techniques D-2 ~ D-5)
    Low-power SSB/SIB1/Paging
    Extension of spatial and power domain techniques in 1) high load scenarios 2) Type-II codebook types
    Semi-static beam-specific broadcast channel configuration
    Scenario 2a for SSB-less
    It was also mentioned that some proposals for multi-carrier enhancements may be beneficial for network energy savings (e.g. cross-carrier HARQ, fast DL carrier switch, multi-carrier CSI)
    Extensions to network-controlled repeaters (NCR), e.g. backhaul/control link behavior for efficient interaction between NES-capable gNB and associated NCR, to consider the case where the gNB would operate with S/P-domain adaptation or cell DTX/DRX adaptation for NW energy saving

## Slide 8
Summary of the RAN3-led directions proposed at RAN#101
  A group (G4) of proposals is looking at network coordination aspects, but proposals are rather fragmented so far (mostly single company proposals). Some proposals may impact RAN2 and RAN1.
  Enable finer control of cell reselection procedures at cell shutdown
  Cell shutdown enhancements that allow for faster cell on/off, e.g. faster power reduction of SSB at cell shutdown
  Further enhancements to gNB/cell sleep to include states during which certain services and/or transmissions can be provided without the gNB/cell being fully functional
  Enhance the inter-node/AMF information exchange
    Enable SSB remapping (i.e., the association between SSB indices and physical beam directions may change)
    Enable restricting paging of pseudo-stationary idle/inactive UEs that may change their camped cell
    NES state coordination between RAN nodes
    AMF awareness of RAN nodes’ availability for paging
  Cell on/off optimization in split gNB deployment, to support gNB-DU assisted/initiated cell (de)activation or gNB-DU autonomy for cell shutdown
  Extensions to access control
Note that discussions on network energy savings as RAN3-led directions are also discussed/proposed for Rel-19 under AI/ML for NG-RAN. At least overlap should be avoided.

## Slide 9
Coordination with SA
  One source proposed to include objectives to address aspects discussed in SA:
  SA work wants to understand energy consumption on a:
    per UE basis
    per UE per PDN connection basis;
    per UE per PDN connection per QoS flow basis.
  As the large majority of energy consumption is in the RAN, early Rel 19 RAN WG co-operation is needed, e.g.
    RAN 1 for guidance on whether reporting can be based on e.g. the sum of number of resource blocks*TTI*transmit power.
    RAN 2 on the (in)feasibility of per PDN, and per PDN per QoS flow reporting for a UE.
    RAN 3 on a reporting framework (e.g similar to “secondary RAT data volume reporting”).
It was not clear to the moderator whether this activity would be triggered by SA, or whether this would be discussed as an independent task for RAN in a RAN-led work item.

## Slide 10: References (Tdocs in agenda 8A.2.5)
TDoc | Title | Source
RP-231554 | Views on scope for NR Network Energy Savings in Rel-19 | Qualcomm Incorporated
RP-231589 | Deutsche Telekom’s Network Energy Saving objectives | Deutsche Telekom AG
RP-231603 | Discussion of R19 work on Network Energy Saving Enhancements | Futurewei
RP-231775 | Discussion on enhancement for network energy saving for Rel-19 | OPPO
RP-231787 | Discussion on Network Energy Saving Enhancements | KDDI Corporation
RP-231793 | Rel-19 Network energy saving enhancements (RAN1-led) | vivo
RP-231870 | Network Energy Saving (NES) enhancement | NEC
RP-231891 | Network Energy Saving Enhancements in Rel-19 | Nokia, Nokia Shanghai Bell
RP-231905 | Network Energy Saving Enhancements for Rel-19 | Spreadtrum Communications
RP-231930 | Network energy savings enhancements in Rel-19 | Huawei, HiSilicon
RP-231942 | On Network Energy Saving Enhancements in Rel-19 | Ericsson
RP-231986 | Network Energy Saving for Rel-19 | InterDigital, Inc.
RP-232036 | Network energy saving enhancements in Rel-19 | Samsung
RP-232063 | Network Energy Saving enhancement | CATT
RP-232076 | Enhancement of Network Energy Saving for NR | NTT DOCOMO, INC.
RP-232095 | Views On Network Energy Saving in R19 | Apple Inc.
RP-232148 | Views on network energy saving enhancements in Rel-19 | Lenovo
RP-232161 | Views on Rel-19 network energy saving enhancements | ZTE, Sanechips
RP-232190 | Network Energy Saving Enhancements in Rel-19 | Fujitsu Limited
RP-232196 | Proposal on network energy saving in Rel-19 | LG Electronics
RP-232208 | Further enhancements on network energy saving | China Mobile International Ltd
RP-232268 | Network energy saving for Rel-19 | China Telecom
RP-232281 | Views on Enhanced Network Energy Saving | Fraunhofer IIS, Fraunhofer HH
RP-232298 | Views on Network Energy Saving (NES) enhancements | Rakuten Mobile, Inc
RP-232327 | [RAN1-led] Network energy saving enhancements | MediaTek Inc.
RP-232535 | Views on Energy Saving work in R19 | VODAFONE Group Plc
RP-232536 | Views on Rel. 19 Network Energy Savings Enhancements | AT&T
RP-232563 | Discussion on Rel-19 Network Energy Saving Enhancements | Intel Corporation
RP-232580 | Network Energy Saving Enhancements | CEWiT

## Slide 11: References (relevant overview papers in agenda 8A.1)
RP-231584 | Things we should not do ! | Deutsche Telekom AG
RP-231749 | Overview on RAN Rel-19 | Apple
RP-231753 | Nokia's views and priorities for Release 19 | Nokia, Nokia Shanghai Bell
RP-231758 | General views on Rel-19 RAN package | Qualcomm India Pvt Ltd
RP-231934 | General views on Rel-19 | Huawei, HiSilicon
RP-231940 | Overview of Rel-19 | Ericsson
RP-231972 | On Rel-19 Package | SHARP Corporation
RP-231981 | Views on Rel-19 RAN scope | InterDigital, Inc.
RP-232042 | Views on Rel-19 RAN scope | Panasonic
RP-232071 | Overview on Release 19 | NTT DOCOMO, INC.
RP-232289 | General view on Rel-19 Handling | Rakuten Mobile, Inc
RP-232297 | Overview of RAN Release 19 | ZTE, Sanechips
RP-232363 | Keysight’s views on 3GPP Rel-19 - unified AI/ML evaluation framework | Keysight Technologies UK Ltd
RP-232533 | General views on R19 scope and size | VODAFONE Group Plc
RP-232556 | Overview of Rel-19 content | Intel Corporation