## Slide 1: Fragmented carriers in the DL A proposal for Rel-19 study item RAN plenary #101
TELUS, Bell Mobility, T-Mobile
RP-232649

## Slide 2: Problem statement
Phone chipsets are limited by the number of supported CA component carriers (CCs)
Signalling associated with multiple CCs is increased
It is not expected that this number of CCs will go up significantly in the coming years (6 or 7 is likely the limit in FR1 range)
Fragmented spectrum in FDD mid-bands contributes to a large number of CCs
In high-bands in FR1, similar fragmentation exists and adding a 200 MHz channel bandwdith would help reduce the fragmentation problem
Some chipset vendors have so far demonstrated that fragmented blocks require the same baseband DLP count as single non-fragmented blocks (e.g., 7A-7A requires single DLP, same as 7A)
3GPP has already a wideband NRU solution where different blocks are treated as part of the same carrier

## Slide 3: Proposal for new Rel-19 items
NR could be modified to make fragmented blocks appear as single CC in mid and high bands in FR1 as long as the intra-band DL bandwidth is narrower than the widest channel bandwidth
We propose a new Rel-19 study item on how to reduce the number of CCs by counting these fragmented blocks as single CCs
For TDD bands (e.g., n77), we propose a Rel-19 work item to introduce a 200 MHz channel profile (with support for 120, 140, ..., 200 channel bandwidths)
We further propose to allow for fragmented blocks within 200 MHz to be part of a single CC (as a part of Rel-19 study item)
CC1
CC2
1 CC

## Slide 4: Example of fragmented blocks in FR1 mid-bands in Canada
PCS (n25) example of fragmented spectrum in Toronto*
BRS (n7) example of fragmented spectrum in Toronto*
AWS1/3/4 (n66) example of fragmented spectrum in Toronto*
*Same colour indicates spectrum access for the same operator

## Slide 5: Example of fragmented blocks being treated as a single CC
There are 189 PRBs in 70 MHz, we need 51 on each side (for 2x20 MHz), thus leaving 87 PRBs that are not used.
PCS is 65 MHz wide, likely a 70 MHz solution would work there too.
AWS1/3/4 is 90 MHz wide, so a 90 MHz profile in FDD is needed.
The alternative is to use 100 MHz channel bandwidth for all and to select properly placed PRBs.
SCS = 30 kHz
70 MHz for n7
A 70 MHz channel can have blank PRBs in the missing portion of the spectrum (where other operators’ blocks are present)

## Slide 6: What needs to be studied?
Currently, the max FDD bandwidth is 50 MHz in the standard; 100 MHz is needed
Backwards compatibility:
  30 kHz subcarrier spacing may not be supported in current devices for FDD bands, and 60 kHz for TDD bands
  Would legacy devices co-exist in some TDM scheduled mode?
The impact on the UE Rx chain design needs to be studied

## Slide 7: THANK YOU