## Slide 1: Summary for discussion [RAN1-R18-ULTxSwitching]
Moderator (NTT DOCOMO, INC.)
3GPP TSG-RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda Item: 9.3.1.2
RP-232658

## Slide 2: Reference
TDoc | Title | Source | Moderator’s comment
RP-231562 | Views on UL Tx switching scope | Qualcomm Incorporated | The proposal in this tdoc is aligned with the intention of proposal for Issue 1 in RP-232090.
RP-231971 | Rescoping Rel-18 UL Tx switching to only up to 3 bands | Apple | The proposal is not fully covered by RP-232090, but whether the most significant issue (Issue 1 in RP-232090) could be solved or not would have an impact to this proposal. So, the proposal in this tdoc can be marked as Issue 4 and can be discussed after Issue 1.
RP-232089 | Status report for WI: Multi-carrier enhancements for NR | NTT DOCOMO, INC. | There has been no flag/concern on the SR.
RP-232090 | Discussion on the supported scenarios for Rel-18 MCE | NTT DOCOMO, INC. | Issue 1, Issue 2 and Issue 3 in this tdoc should be discussed. Issue 1 and 2 in this tdoc can cover RP-231562, RP-232418 and RP-232443.
RP-232418 | CR for 38.101-1: Time mask for switching across three or four uplink bands | China Telecom, Huawei, Hisilicon, CMCC, Xiaomi, China Unicom, vivo, CATT | Whether this CR can be approved or not (i.e., some updates are necessary) depends on the discussion on Issue 1 and Issue 2 in RP-232090.
RP-232443 | On Scope of 3-4 band TX switching scenarios | Ericsson | The proposals in this tdoc would be aligned with the intention of proposal for Issue 1 in RP-232090, and hence they can be covered by Issue 1 and 2 in RP-232090.
RP-232471 | Introduction of Rel-18 - Multi-carrier enhancements | RAN1 | As this CR pack does not include UL Tx switching part, it would not have any issue.

## Slide 3: Issue 1: supported scenarios for Rel-18 UL Tx switching
Background
  At the RAN#96, target scenarios for Rel-18 UL Tx switching were discussed and the proposal in RP-221880 was agreed without changes, where concerned scenarios were captured as below.
  At the RAN#97-e, concerned scenarios were discussed as summarized in RP-222672, but there was no conclusion regarding the scenarios.
  At the RAN#98-e, new WID on NR CA band combo with dual SUL bands was approved in RP-223553.
  At the RAN#99, whether simultaneous configuration of two cells with SUL is allowed or not was discussed due to different understanding on Note 2 in RP-223553, and following was agreed in RP-230810.
  At the RAN#100, RAN4 CR in R4-2310270 was not approved and corresponding discussion was postponed to RAN#101
  Other Further check additional scenarios as below can be discussed in RAN4#104e and RAN#97e, e.g.,
    {SUL band + corresponding NUL band} + {SUL band + corresponding NUL band}
    Simultaneous transmission across 2 bands in {SUL band + corresponding NUL band} + 1 or 2 other NUL band(s) (excluding simultaneous transmission between SUL and corresponding NUL)
Task RAN4 to assess the additional, if any, RAN4 specification impact and UE implementation impact for a UE configured with two serving cells, each with SUL; report to RAN#100 with the goal of striving for potential normative work supporting the case where a UE is configured with two serving cells, each with SUL
  E.g., whether back-to-back transmissions between two SUL carriers and back-to-back transmissions between SUL carrier and non-corresponding NUL carrier could be supported without any switching period, or
  E.g., whether it is only feasible to support such configuration in the UL Tx switching framework with UE capability based switching period
  Example band combinations are referred to in RP-223553 (RP-230719)
  Further check the status in RAN#100

## Slide 4: Issue 1: supported scenarios for Rel-18 UL Tx switching
Discussion
  Regarding the scenario with dual SUL, there is a clear operator’s demand as shown in RP-223553, and RAN4 agreed that “For a UE configured with two serving cells, each with SUL, UL Tx switching between two SUL carriers and between SUL carrier and non-corresponding NUL carrier can be supported with UL Tx switching framework without additional RAN4 spec impact and UE implementation issue”. Therefore, the scenario ({SUL band + corresponding NUL band} + {SUL band + corresponding NUL band}) should be supported at least for the case of switched UL in Rel-18.
  Regarding the dual UL support for the scenario with SUL(s), simultaneous transmission between SUL and SUL or non-corresponding NUL has not been studied/supported in previous releases as well as in Rel-18. We think that the study on such simultaneous transmission between SUL and SUL or non-corresponding NUL is necessary before supporting it.
  On the other hand, simultaneous transmission between NUL and NUL in the scenario with SUL(s) can be supported. In Rel-18 UL Tx switching, switched UL or dual UL can be reported/configured per band pair, and hence supporting dual UL for specific band pair only can be handled.
Proposal
  The scenario {SUL band + corresponding NUL band} + {SUL band + corresponding NUL band} is supported in Rel-18 UL Tx switching framework (no back-to-back transmission), with following restrictions.
    For the band pair between NUL and NUL, “switched UL” or “dual UL” can be reported/configured.
    For any other band pair including SUL, only “switched UL” can be reported/configured in Rel-18.
  The same restrictions are applied to the scenarios {SUL band + corresponding NUL band} + 1 or 2 other NUL band(s).

## Slide 5: Issue 2: how to capture the supported scenarios/restrictions
Background
  In RAN1 specification TS38.214 section 6.1.6 on UL Tx switching, there are three sub-sections i.e., 6.1.6.1 for ENDC case, 6.1.6.2 for CA case and 6.1.6.3 for SUL case in Rel-16/17.
  For Rel-18 TS38.214, the new sub-sub-section 6.1.6.2.2 for UL Tx switching with 3 or 4 UL bands is to be introduced according to the latest draft CR from editor (which was discussed in post-RAN1#113 email discussion but not endorsed due to Issue 1).
  Due to Issue 1, RAN4 CR in R4-2310270 was not approved at RAN#100.
  As proposed for Issue 1, if supported scenarios and restrictions are clarified by RAN, next issue is where/how to capture such supported scenarios and restrictions in the specifications, e.g., whether it should be in RAN4 spec, RAN1 spec or RAN2 spec (such as RRC/UE capability signaling)
Discussion
  In latest CRs for TS38.214 and TS38.101-1, there is no description about the proposed restriction for Issue 1 such as “dual UL is not appliable to any band pair including SUL band”, and there is no restriction on dual SUL bands.
  We think either one of following alternatives (or both) can be selected.
    Alt.1: clarify the restriction according to the Issue 1 discussion in TS38.101-1 e.g., section 5.5C “Configurations for SUL”
    Alt.2: clarify the restriction according to the Issue 1 discussion in TS38.306/331 i.e., UE capability/RRC signaling on switchedUL/dualUL
Proposal
  RAN should provide guidance on where/how to capture the restrictions (if any) according to Issue 1 discussion.

## Slide 6: Issue 3: whether DCI format 0_3/1_3 can request Tx on SUL carrier
Background
  At the RAN#99, it was agreed that UL/SUL indicator field is excluded from a DCI format 0_X.
  RAN1 has been discussing whether DCI format 0_3/1_3 can request/schedule UL transmissions on SUL carrier(s)
    Some company argued that “SUL can be semi-statically configured and used without switching, therefore DCI 0_3 can still be used for scheduling PUSCH on SUL, without UL/SUL indicator”.
      UL/SUL indicator – 0 bit for UEs not configured with supplementaryUplink in ServingCellConfig in the cell or UEs configured with supplementaryUplink in ServingCellConfig in the cell but only one carrier in the cell is configured for PUSCH transmission;
    RAN1 has also been discussing the bit size per cell in the row of the joint SRS request configuration table
      Alt.1: BIT STRING(SIZE(x)), where x=3 for a cell configured with SUL and x=2 for a cell configured without SUL
      Alt.2: BIT STRING(SIZE(2))
Discussion
  UL CA band combination including one or two serving cells each with SUL is possible in Rel-18 (as in Issue 1).
  Although legacy DCI with UL/SUL indicator can be used to dynamically select SUL or NUL for UL transmission, MC-DCI can also be used to schedule/request UL transmissions on set of cells including cell(s) with SUL.
    Due to no UL/SUL indicator field in MC-DCI, pre-defined rule and/or semi-static configuration to determine which carrier is scheduled/requested for UL transmission by MC-DCI is necessary for cell(s) with SUL.
    SRS request can be 2 or 3 bits according to SUL configuration for each serving cell as in legacy DCIs.
  However, as proposed for Issue 1, simultaneous transmission between SUL and SUL or NUL should not be expected.
Proposal
  RAN should provide guidance on whether DCI format 0_3/1_3 can request UL transmissions on cell(s) with SUL.

## Slide 7: Issue 4: whether to exclude 4 bands cases from Rel-18 UL Tx switching (RP-231971)
Observation 1: Up till August RAN4 meeting, there were still many remaining open issues associated with the 4-band configuration which do not seem to have immediate solutions and may hinder the completion of Rel-18 UL Tx switching feature.
  Switching time may be different for the same band pair under different 4-band configurations [5]. For example, switching time could be different for A <-> B and A<-> C between A-B-C-D and A-B-C-E 4-band configurations.
  The switching time for 4-band switching (A-B-C-D) has been assumed by RAN4 as max {Tswitch_A-C, Tswitch_B-D, Tswitch_A-D, Tswitch_B-C} which could be rather inefficient as certain switching pairs may have shorter switching time [5].
  4-band switching involves only 1Tx-1Tx + 1Tx-1Tx where the 1Tx-1Tx switching time could be different from 1Tx-2Tx or 2Tx-2Tx for the same band pair.
  4-band switching time mask has not yet been specified in the recent endorsed RAN4 CR [6].
  Dual-SUL 4-band switching may involve (NUL1+NUL2) to (SUL1+SUL2) switching where NUL1-SUL1 and NUL2-SUL2 switching time can only be 0 μs which however would not be feasible in a 4-band configuration switching.
Observation 2: The dual-SUL 4-band switching feature was causing the disapproval of the endorsed RAN4 CR in June plenary meeting and further controversial views in August RAN4 meeting.
Observation 3: The potential switching scenarios would grow exponentially with the number of bands.
Observation 4: For UL Tx switching among 4 bands, there are potentially total of 57 switching scenarios.
Proposal 1: Limit the scope of Rel-18 UL Tx switching feature to only among 3 bands to avoid the outgrown complexity by introducing 4-band switching in parallel.
Proposal 2: Postpone the 4-band UL Tx switching feature to Rel-19 multi-carrier enhancement WID in order to allow RAN4 more time to sort out the solutions for the remaining open issues.

## Slide 8: Offline agreed WF for Issue 1 and Issue 2
The scenario {SUL band + corresponding NUL band} + {SUL band + corresponding NUL band} is supported in Rel-18 UL Tx switching framework with following restrictions.
  For the band pair between {NUL and NUL}, “switched UL” or “dual UL” can be reported/configured.
  For any other band pair including SUL (between {SUL and another SUL}, between {SUL and corresponding NUL}, and between {SUL and non-corresponding NUL}), only “switched UL” can be reported/configured in Rel-18.
  Back-to-back transmission (i.e., switching without having switching gap) between {SUL and another SUL} and between {SUL and non-corresponding NUL} are not supported in Rel-18.
  Note: this does not prevent a study and normative work to support simultaneous transmission between {SUL and another SUL} and/or between {SUL and non-corresponding NUL} as well as back-to-back transmissions between {SUL and another SUL} and/or between {SUL and non-corresponding NUL} in future release
The same restrictions are applied to the scenarios {SUL band + corresponding NUL band} + 1 or 2 other NUL band(s).
  For band pairs between {SUL and non-corresponding NUL} in this scenario, only “switched UL” can be reported/configured in Rel-18
  Back-to-back transmission (i.e., switching without having switching gap) between {SUL and non-corresponding NUL} in this scenario is not supported in Rel-18
  Note: this does not preclude a possible support based on other UE architecture than Rel-18 UL Tx switching
Clarify the restrictions above at least in TS38.101-1 e.g., section 5.5C “Configurations for SUL”
  Note: TS38.214 may not need to capture the restrictions, and whether/how to capture restrictions in TS38.331/306 can be discussed in Q4 RAN2

## Slide 9: Updated potential WF for Issue 3
The bit size per cell in the row of the joint SRS request configuration table is “BIT STRING(SIZE(2..3))”, where the size is 2 for a cell configured without SUL, and the size is 3 for a cell configured with SUL
  Note that simultaneous transmission between {SUL and SUL} and between {SUL and NUL} is not supported in Rel-18
When a cell configured with SUL is one of co-scheduled cells of DCI format 0_3, UE does not expect that only SUL carrier in the cell is configured for PUSCH transmission on the cell
  PUSCH transmission(s) triggered by DCI format 0_3 is performed only on NUL carrier(s)

## Slide 10: Offline agreed WF for Issue 4
Keep both 3 bands and 4 bands switching cases for Rel-18 UL Tx switching