## Slide 1: Offline discussion summary on Rel-18 NR-NTN PUCCH enhancements for Msg4 HARQ-ACK
NTT DOCOMO
3GPP TSG-RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda Item: 9.3.2.7
RP-232665

## Slide 2: background
Following contributions submitted to RAN#101 discussed whether to support repetition for the PUCCH transmissions when dedicated PUCCH resource configuration is not provided
  Companies are generally fine to support repetition for the PUCCH transmissions when dedicated PUCCH resource configuration is not provided
RP-231818 | Discussions on PUCCH repetition when dedicated PUCCH resource configuration is not provided | vivo
RP-231947 | On PUCCH repetition for NR NTN | Ericsson
RP-232020 | NTN PUCCH repetition for Msg4 HARQ ACK | Panasonic
RP-232039 | On the scope of Rel-18 NR NTN enhancements | Samsung
RP-232091 | Discussion on Rel-18 NR NTN | NTT DOCOMO, INC.
RP-232100 | On R18 NR NTN Coverage Enhancements | Apple Inc.

## Slide 3: Offline discussion
Majority companies are fine with the proposal in RP-232091 during Monday online session.
 Main bullet and 1st sub-bullet of the proposal in next page. The intention is the same as the proposal in RP-232091, while it is revised from WID revision to a simple proposal to clearly agree that repetition is supported for PUCCH transmissions when dedicated PUCCH resource configuration is not provided.
Nokia/NSB showed their great flexibility to support the main bullet with the condition that the behavior written in this sub-bullet is clarified
 2nd sub-bullet of the proposal in next page
Qualcomm showed their concern during Monday online session if separate UE capability is introduced for the repetition of PUCCH transmissions when dedicated PUCCH resource configuration is not provided, in addition to that of Msg4 HARQ-ACK (FG 44-1 in the latest RAN1 UE features list in R1-2308521).
 3rd sub-bullet of the proposal in next page

## Slide 4: Proposal
PUCCH repetition discussed in Rel-18 NR NTN coverage enhancement is supported for the PUCCH transmissions when dedicated PUCCH resource configuration is not provided
  No additional RAN1 work to support this behavior is assumed
  It is confirmed that DAI field for dynamic indication of repetition factor can indicate '1' when multiple values configured by the gNB for repetition factors include '1'
  FG 44-1 is used to indicate the support of this feature

## Slide 5: Ref: FG 44-1 in R1-2308521
Features | Index | Feature group | Components | Prerequisite feature groups | Need for the gNB to know if the feature is supported | Applicable to the capability signalling exchange between UEs (Sidelink WI only)”. | Consequence if the feature is not supported by the UE | Type (the ‘type’ definition from UE features should be based on the granularity of 1) Per UE or 2) Per Band or 3) Per BC or 4) Per FS or 5) Per FSPC) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Capability interpretation for mixture of FDD/TDD and/or FR1/FR2 | Note | Mandatory/Optional
44. NR_NTN_enh | 44-1 | PUCCH repetition for Msg4 HARQ-ACK | 1. Support repetition transmission of PUCCH for Msg4 HARQ-ACK on common PUCCH resource 2. Support receiving repetition factor in system information [3. Support receiving repetition factor in DCI scheduling Msg4 PDSCH] [4. Support Msg3 to transmit information for PUCCH Msg4 HARQ-ACK repetition] [5. Extension of the repetition transmission of PUCCH before dedicated PUCCH resource configuration] 6. Support of RSRP threshold for Msg4 HARQ-ACK repetition | FFS | Yes | No | UE does not support PUCCH repetition for Msg4 HARQ-ACK | Per Band | N/A | N/A | N/A | A UE that includes [RAN2 parameter name] in [RRC Setup Request] must support FG 44-1 [Note: This UE feature group is applicable only for bands in Table 5.2.2-1 in TS 38.101-5 [and HAPS operation bands in Clause 5.2 of TS 38.104] | Optional without capability signaling