## Slide 1: WF on potential RRM objectives for NR-NTN deployment in above 10 GHz (NR-NTN-enh WID)
Source: Thales
3GPP TSG-RAN Meeting #101
Bangalore, India, September 11-15, 2023
Agenda Item: 9.3.2.7
RP-232694

## Slide 2: TDoC considered in the discussion
TDOC | Type | Title | Source | Comments
RP-232039 | discussion | On the scope of Rel-18 NR NTN enhancements | Samsung | Proposal 2 : Including the following as a sub-bullet under objective 4.1.2 “Specify necessary RRM requirements for NR-NTN UEs operating in the NTN example band (i.e. Ka band) based on associated assumptions of the UE architecture (including beam steering capabilities) .”
RP-231533 | LS in | LS on RAN4 RRM work scope for NR NTN Ka band (R4-2314484; to: RAN; cc: -; contact: Thales) | RAN4 | RAN4 discussions are still ongoing on how to define RRM requirements. However, RAN4 RRM is happy to announce that the scope of the work needed to define the RRM requirements (i.e. beam steering related) necessary for NR-NTN UEs operating in the NTN example band (i.e. Ka band) based on associated assumptions of the UE architecture has been identified

## Slide 3: Rel-18 NR-NTN-enh WID: RRM req for Ka band
Proposal 1: As part of the NR-NTN-enh WID, RAN4 shall work on the definition of RRM requirements considering the following
  cases: Case-1: Stationary UE for GSO; Case-2: Stationary UE for LEO; Case-3: Mobile UE for GSO
  UE architectures: Fully electronically-steered beam UEs (Type 1); Fully mechanically-steered beam UEs (Type 2)

## Slide 4: Rel-18 NR-NTN-enh WID: RRM req for Ka band
Proposal 2: RAN recommends RAN4 to define the following RRM requirements for example band (Ka band) in the table below as baseline.
RRM requirements to be defined as part of Rel-18 NR-NTN-enh WID | Electronic steering antenna | Mechanical steering antenna (inter-sat) | Mechanical steering antenna (intra-sat)
 | Terminal Type 1 | Terminal Type 2 | 
UE uplink timing accuracy | Y | Y | Reuse FR1 NTN requirement, except UL uplink timing accuracy
RRC IDLE and INACTIVE mobility | L | N | 
(Conditional/blind) Handover | Y | Y | 
RRC Re-establishment | L | L | 
RRC Connection Release with Redirection | N | N | 
Radio Link Monitoring | Y | Y | 
Link Recovery procedure (BFD/CBD) | N | N | 
Active TCI switching | N | N | 
Measurement Procedure | Y | N | 
(L1/L3 measurement delay and measurement gap, scheduling restriction due to mixed numerologies) | Y | N | 
Measurement Performance | Y | N | 
UL spatial relation switching | N | N | 
Y | Yes (shall to be defined)
N | No (No need to define in Rel-18)
L | Low priority (may be defined if time allows)
The following assumptions (applicable to Type 1 and Type 2 terminals) are used for R18 RRM requirements
  single SAN Tx beam per radio cell in DL
  For inter satellite HO, only blind HO and no neighbor cell measurement
    Blind HO assumption for type 1 UE can be revisited if issue is identified in RAN4
  Intra-sat neighbor cell measurement is needed
  Same UE Rx beam is used for both serving and neighboring cells which belong to the same sat. (i.e. no Rx beam sweeping)