## Slide 1
0
Views on Rel-19 LP-WUS WI
December 2023
3GPP TSG RAN #102 RP-233422
Edinburgh , GB, December 11-15, 2023
Agenda Item: 9.1.1.6
Source: CMCC
Type: Discussion

## Slide 2
LP-WUS SI results (based on TR38.869 v0.4.0)
 | OOK | OFDM | Comment
Power saving gain | 57%~99% (average 80%), PWURON< 1 unit | 29%~95% (average 66%), 5<=PWURON<= 10 unit -79%~86% (average 16%),10<=PWURON<= 20 unit | OOK has better PSG than OFDM, Note: Assuming (PWURON<= 1 unit) for OOK and (PWURON >4) for OFDM by author of this article
Coverage | 0.9~17.28 MHz*Symbol/bit | 0.31~4.32 MHz*Symbol/bit | OFDM has clear advantage over OOK Note: compare to Msg3 single transmission
LLS | Time error: up to 4us Frequency error: 390kHz | Time error: 4us depending on sliding window Frequency error: worse than OOK/FSK | OOK is better than OFDM in time and frequency error tolerance, but much worse in spectrum efficiency.
Active Power | 0.05 ~ 1(8 sources), 4(1 source) | Frequency-domain correlation 4 ~ 10/30 (5 sources) 1 (1 source) Time-domain correlation only 5 ~ 10/30 (5 source) 1 ~5 (1 source) 0.15 (1 source) | Clear differences on active power. OOK has lower active power consumption over OFDM receiver. Only IF/BB receiver for OOK is considered in the table.
LP-SS / SSB | 0.4% for 320ms, 1 slot LP-SS 0.3% for 1.28s, 3 slot LP-SS | Current SSB, no additional overhead | Overhead is marginal
RRM accuracy | X= [-9, -11] dB: AWGN, 90% accuracy of 3 or 5dB, (1 -20) symbols spreading over 1-3 periods is required | X= [-3, -6] dB: AWGN, 90% accuracy of 3dB, 1 OFDMA symbol in 1 period is required | X denotes SNR target
NetPower | (0.06%~3.9%), (0.07%~2.716%), (0.388%~1.076%) for zero load, low load and medium load (1 slot LP-SS, 4 sources) | Current SSB, no additional Power | network power consumption increase is marginal.
Observations 1: OOK and OFDM receiver are tradeoff between power (i.e., active power, power saving gain) and link performance (coverage, measurement accuracy). Network power consumption and overhead is marginal

## Slide 3
LP-WUS SI outcome
PSG | PWURON<= 1 unit | 4<PWURON<=10 | 10 < PWURON <= 30
[8A-3] | 99% | 95%, (5x) * | 
[8A-13] | 66% | 29%, (2.2x) | -79% (5.3x)
[8A-17] | 75% |  | 
[8A-16] | 97% | 76%, (8x) | 86% (4.6x)
[8A-11] | 85% | 64%, (2.4x) | 42% (3.9x)
[8A-12] | 84% |  | 
[8A-4] | 57% |  | 
Note (*): 95% means the power saving gain is 95% compared to legacy, 5x means the power consumption is 5 times compared to PWURON< 1 unit
Power consumption for different PWURON for low traffic arrival rate and FAR (<=0.1%)
Observations 2:
  If assuming (PWURON<= 1 unit) for OOK and (PWURON >4) for OFDM receiver
    Almost all companies show significant power saving gain for OOK and OFDM receiver.
    All companies shows OFDM receiver is 2.2x ~ 8x times power consumption than OOK receiver.
Proposal 1：
  Lower power consumption is essential for IoT devices. At least for IoT devices, OOK receiver should be considered.
  For wearable and smartphone, OFDM receiver can be considered to further improve performance (carrying more information or better coverage) while still bringing large power saving benefits.
For RRC CONNECTED mode
  For FTP/IM
    Trade-off between Power saving gain and UPT for replace DCP
    For the usage of LP-WUS to trigger the UE MR PDCCH monitoring,
      Significant UE power saving gain (up to more than 60%) and moderate UPT improvement (up to more than 10%) when the UE MR enters deep sleep state during LR LP-WUS monitoring
Observation 3: RRC CONNECTED LP-WUS has benefits for power saving.

## Slide 4
RAN#101 outcome for the waveform
RP-232616 Moderator’s summary of Rel-19 LP-WUS WI, Moderator(CMCC)
The most favorite two directions are shown as follows,
Direction 1:
Waveform-option-1: OOK-1 and/or OOK-4, as described in section 7.2.1.1 (A)(D) in TR38.869.
Waveform-option-3: Harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform, i.e., specified overlayed OFDM sequences over OOK symbol
For RRC IDLE/INACTIVE, in addition to existing PSS/SSS, LP-SS (, i.e., OOK-1 and/or OOK-4 waveform with/without overlayed OFDM sequences with potential further down selection in WI phase) for LP-WUR that cannot receive existing PSS/SSS, is supported for synchronization and/or RRM for serving cell.
Direction 2:
Waveform-option-3: Harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform, i.e., specified overlayed OFDM sequences over OOK symbol
For RRC IDLE/INACTIVE, in addition to existing PSS/SSS, LP-SS (, i.e., OOK-1 and/or OOK-4 waveform with/without overlayed OFDM sequences with potential further down selection in WI phase) for LP-WUR that cannot receive existing PSS/SSS, is supported for synchronization and/or RRM for serving cell.
Thus, the 2 directions should be considered to formulate the WID.

## Slide 5
Potential scope for Rel-19 LP-WUS WI
LP-WUR based on waveform consideration
  LP-WUR support OOK only should be considered,
    targeting for low speed and with peak power consumption lower than 1 unit, and IoT traffics. Both duty-cycled and continuously monitoring(can be discussed in WI phase, larger CRC protection is not expected) can be considered.
  LP-WUR supporting both OOK and OFDM can be considered as alternative LP-WUR receiver,
    OFDM sequence(s) can be additionally modulated on top of OOK
    targeting for low speed and with peak power consumption larger than 4 unit and less than [20] unit, both eMBB and IoT traffic can be considered. Only duty-cycled monitoring is supported.
    For wearable and smartphone, OFDM receiver can be considered to further improve performance (carrying more information or better coverage), details can be discussed in WI.
LP-SS based measurement for synchronization and RRM is supported
  MR RRM is further relaxed or offloaded to LP-WUR
  For OOK receiver, same waveform for LP-SS and LP-WUS should be considered.
  For OOK+OFDM receiver, reusing existing PSS/SSS measurement should be considered.
Targeting LP-WUS/LP-SS coverage comparable to NR bottleneck channel, e.g., PUSCH for msg3.
Generation of OOK waveform by existing gNB implementation should be supported. Discuss and decide which OOK alternative is supported in WI.
Necessary L1 and higher layer procedure to activate/deactivate LP-WUS monitoring, LP-SS measurement and wake-up/go-to-sleep MR should be supported.
Forward compatibility to allow wake-up other system should be considered.
Both RRC IDLE/INACTIVE/CONNECTED is considered.

## Slide 6
Thank you!