## Slide 1: Network Energy Saving Enhancements
RP-233505
3GPP TSG RAN Meeting #102 Edinburg, Scotland, December 11-15, 2023
Agenda item: 9.1.1.5
Sourced by: CEWiT, IIT-K, Tejas Networks

## Slide 2
© CEWiT 2022
2
Motivation and State of Art
Adapting the transmission/reception procedures at gNB to reduce energy consumption
  Motivation: is to reduce operational cost and environmental impacts
  Adaptation based on traffic condition, channel, UE feedback/assistance information etc.
  Constraint: Minimum impact on performance, legacy UEs and specification
Rel. 18 studied energy saving techniques in time, frequency, spatial and power domains
  Evaluation metric and KPI
  Energy saving gains
  Specification impact
  Impact on legacy operation
The outcome of the study is captured in TR 38.864

## Slide 3
© CEWiT 2022
3
State of art cont’d…
Rel. 18 WI focused on
  Adaptation of DTX/DRX pattern for gNB (Technique A-4)
    Configuration for DTX/DRX and activation/deactivation of DTX/DRX
    Impact of DTX/DRX pattern on various signals/channels and UE behavior for various conflicts
  Adaptation of spatial elements: Port adaptation and TxRu adaptation (Technique C-1)
    Procedures and Configuration for determining the adaptation pattern
      Impacts on CSI-RS measurement and reporting framework
    Signaling exchanges for spatial adaptation and UE behavior
  Power adaptation (Technique D-1)
    Procedures and Configuration for determining the adaptation pattern
      Impacts on CSI-RS measurement and reporting framework
    Signaling exchanges for power adaptation and UE behavior

## Slide 4
Adaptation of Common Signals/Channels

## Slide 5
© CEWiT 2022
5
Motivation for Adaptation of Common Signals/Channels
Rel. 18 techniques for NES is restricted to UE specific signals/channels
Spatial and power domain adaptations, and Cell DTX/DRX has no impact on common signals/channels
  In NR, transmission of common signals/channels is irrespective of load or network condition and it occupy a certain part of time and frequency resource
  Results in frequent switching, lower inactive period, and limit the energy saving gains
  E.g., if SSB occasion overlaps with inactive period of Cell DTX, then the gNB turns On and transmit SSB
SSB-less SCell operation is limited to certain scenario
  Synchronization relies on measurement of SSB in other cells
  Measurement is applicable only for co-located cells
  Non-co-located cells rely on periodic SSB transmission, where NES techniques are not applicable
Techniques for NES should be extended to common signals/channels and new scenario
  Prioritize techniques based on the outcome of SI phase

## Slide 6
© CEWiT 2022
6
On-demand SSB (Technique A-5-2)
Extension of SSB less operation to non-co-located cells
SSB transmission based on WUS
  Enable longer inactivity period for cell, resulting in energy saving
  Simplified SSB to enable measurement and transmission of WUS by the UE
    As a starting point RACH can be considered as the WUS
  Based on TR 38.864, significant energy saving is observed
Combining simplified SSB with DTX pattern
  Transmit simplified SSB during non-active period of DTX pattern
  Simplified SSB occupy less amount of time and frequency resources
  Increases sleep time and energy saving gains
Fig. 1: On demand SSB framework
Simplified SSB
SSB
SIB1
WUS
DRS
SSB
SSB
Periodic SSB occasions
Active period of DTX pattern
Non-active period of DTX pattern
Fig. 2: Multiplexing On demand SSB with DTX pattern

## Slide 7
© CEWiT 2022
7
On-demand SSB cont’d…
Impact on legacy UE can be overcome/minimized by
  Enabling the technique in a cell without legacy UEs (E.g., FR2)
  Increasing the periodicity of legacy SSB and multiplexing simplified SSB with legacy SSB
Fig. 3: Multiplexing On demand SSB with legacy SSB
Simplified SSB
SSB
SSB
Periodic SSB occasions

## Slide 8
© CEWiT 2022
8
Rel. 19 WI phase should consider on-demand SSB
  Procedures for On-demand SSB
  Design of simplified SSB and WUS
  Multiplexing simplified SSB and DTX pattern
On-demand SSB: Proposal

## Slide 9
Adaptation of Transmission Reception Points

## Slide 10
© CEWiT 2022
10
Adaptation of TRP (Technique C-2)
Motivation
  Rel. 18 spatial adaptation techniques focussed on single TRP operation
  Rel. 18 studied dynamic switching between single TRP and m-TRP operation
    Significant energy saving is observed
    No impact on legacy UE is foreseen, if implemented for UE specific signals/channels
Adapt the number of TRPs transmitting and/or receiving signals and channels
  Adaptation of TRP impacts the TCI state configurations
    Transmission/reception using single/multiple TRP is configured using TCI states
    Current specification has limited flexibility to configure TCI states
  Adaptation of TRP impacts the repetition schemes
    Spatial domain repetition using m-TRP improves reliability of transmission
    Different type of mappings are defined between repetitions and TCI states
    Adaptation reduces the number of repetitions and impacts the mapping with TCI states

## Slide 11
© CEWiT 2022
11
Adaptation of TRP (Technique C-2) : Proposal
The Rel. 19 WI phase should consider following aspects for efficient implementation of TRP adaptation
  Enhancements for TCI framework for m-TRP
  Signalling exchanges for TRP adaptation and defining UE behaviour
  Impacts on repetition schemes/procedures

## Slide 12
Extending NES to Additional Scenario/Deployment

## Slide 13
© CEWiT 2022
13
Extending NES to Network Controlled Repeater
NCR is an advanced repeater
  Capable of receiving/processing side control information from serving gNB
  Capable of adapting the amplify & forwarding operation based on SCI
  Rel. 18 NES adaptations assumed deployment without NCR
NCR should adjust A&F operation based on adaptation at the serving gNB
  Save energy at NCR and minimize interference in system
  NCR behavior should be defined for the scenario when serving gNB is in NES mode
  New SCI neededed to inform NCR about adaptation pattern at gNB

## Slide 14
© CEWiT 2022
14
Extending NES to Network controlled repeater: Proposal
The Rel. 19 WI phase should consider following aspects
  Impact of adaptations for NES at serving gNB on NCR
  Signalling exchanges to inform NCR about the adaptations for NES at serving gNB
  Behaviour of NCR for new scenario/signaling

## Slide 15
Further Enhancements for Rel. 18 NES Features

## Slide 16
© CEWiT 2022
16
  Rel-18 WI on spatial/power adaptation focused on
  Measurement and reporting framework for determining the adaptation pattern
  Adaptations for PDSCH only
  Spatial/power adaptation impacts the beam characteristics and TCI states
  Turning off antenna elements for spatial adaptation can lead to broader beams
  CSI-RS and PDSCH are transmitted using beams with different characteristics
  QCL relation between CSI-RS and PDSCH is impacted due to variation in beam characteristics
  Spatial/power adaptation impacts BFR procedure
  Best beam is selected using measurements on CSI-RS and configured threshold
  PDSCH is to be transmitted using different spatial/power configuration compared to CSI-RS
  Measurements on CSI-RS w/o adaptation satisfy the threshold whereas the PDSCH may not
  Performance of the selected beam may not be the best for PDSCH
Enhancements for Spatial/power domain adaptation

## Slide 17
© CEWiT 2022
17
Rel-18 spatial and power adaptation increases UL resource consumption and UE power consumption
  Transmission of multiple CSI reports corresponding to various adaptation patterns
  UE reports configured CSI report quantity for all adaptation patterns
  Increase the measurement complexity, CSI payload and reporting
Enhancements to simplify CSI report framework
  Configured CSI report quantity can be redundant across the adaptation patterns
  Enhancements to avoid redundancy in reporting
  Rel-18 WI dropped following aspects of spatial and power adaptation due to time constraints
  Enhancements for TCI states and BFR procedure
  Enhancements for CSI report payload reduction
Enhancements for Spatial/power domain adaptation cont’d…

## Slide 18
© CEWiT 2022
18
  Rel. 19 should consider the following enhancements for spatial and power domain adaptations
  Enhancements for TCI state and BFR procedure to support spatial and power domain adaptations
    Dynamic adaptation of the TCI state mapping based on adaptation pattern
    Dynamic adaptation of threshold for beam selection based on adaptation pattern
  Methods to simplify the CSI reporting framework for NES adaptation
    CSI compression using correlation among various CSI report quantities for various adaptation patterns
    Methods to derive CSI report quantities based on the adaptation pattern
Enhancements for Spatial/power domain adaptation: Proposal

## Slide 19
© CEWiT 2022
19
  Rel-18 DTX/DRX adaptation support single configured DTX/DRX pattern, activated by RRC or DCI
  DTX/DRX pattern comprises start time, ON duration and periodicity
  Dynamic adaptation of DTX/DRX pattern based on network condition is essential
  Cell DTX/DRX pattern depends on network condition, which varies dynamically
  DCI based activation/deactivation supports dynamic adaptation
  Single pattern restrict flexibility of dynamic adaptation
  Multiple Cell DTX/DRX patterns is essential to improve flexibility adapt the pattern based on network condition
  RRC configures multiple DTX/DRX pattern
  DCI activate/deactivate cell DTX/DRX and select the pattern
Enhancements for DTX/DRX Adaptation

## Slide 20
© CEWiT 2022
20
  Rel-18 DTX/DRX pattern can be activated DCI
  Failure of DCI activating DTX/DRX adaptation results in uncertainty about DTX/DRX pattern
  Unnecessary transmission/monitoring at UE side for the signals affected by DTX/DRX pattern
  UE skip monitoring/reception of signals affected by DTX/DRX pattern
  Methods to enhance reliability of DCI activating/deactivating DTX/DRX should be considered
  Introducing feedback for the DCI activating/deactivating DTX/DRX
Enhancements for DTX/DRX Adaptation cont’d…

## Slide 21
© CEWiT 2022
21
Enhancements for DTX/DRX Adaptation: Proposal
The Rel. 19 WI phase should consider following enhancements for DTX/DRX mechanism
  Support for multiple DTX/DRX patterns
  Increasing reliability of activation/deactivation of DTX/DRX

## Slide 22
© CEWiT 2022
22
Summary
  On-demand SSB
    Procedures for On-demand SSB
    Design of simplified SSB and WUS
    Multiplexing simplified SSB and DTX pattern
  Adaptation of TRP transmitting and/or receiving signals and channels
    Enhancements for TCI framework for m-TRP
    Impacts on repetition schemes/procedures
    Signalling exchanges for TRP adaptation and defining UE behaviour
  Extending NES enhancements to deployment scenario with NCR
    Side control information to support NES capable gNB
    Signaling mechanism and NCR behavior
Further enhancements for DTX/DRX mechanism
  Support for multiple DTX/DRX patterns
  Increasing reliability of activation/deactivation of DTX/DRX
  Further enhancements for spatial/power adaptation
  Enhancements for TCI state and beam failure recovery procedures
  Enhancements to simplify CSI report framework
Following NES techniques are supported for WI phase in Rel. 19

## Slide 23
© CEWiT 2022
23
Thank You