## Slide 1: Views on Rel-19 LP-WUS
China Telecom
Dec, 2023
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.1.6
Document for: discussion
RP-233572

## Slide 2: Potential objectives
Based on RP-232616 in RAN #101, the following direction can be selected for Rel-19 work:
Direction 1 (Number of supporting companies:13) | Direction 2 (Number of supporting companies:13)
Waveform-option-1: OOK-1 and/or OOK-4, as described in section 7.2.1.1 (A)(D) in TR38.869. Waveform-option-3: Harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform, i.e., specified overlayed OFDM sequences over OOK symbol For RRC IDLE/INACTIVE, in addition to existing PSS/SSS, LP-SS (, i.e., OOK-1 and/or OOK-4 waveform with/without overlayed OFDM sequences with potential further down selection in WI phase) for LP-WUR that cannot receive existing PSS/SSS, is supported for synchronization and/or RRM for serving cell. | Waveform-option-3: Harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform, i.e., specified overlayed OFDM sequences over OOK symbol For RRC IDLE/INACTIVE, in addition to existing PSS/SSS, LP-SS (, i.e., OOK-1 and/or OOK-4 waveform with/without overlayed OFDM sequences with potential further down selection in WI phase) for LP-WUR that cannot receive existing PSS/SSS, is supported for synchronization and/or RRM for serving cell.
Seems that the difference between direction 1 and direction 2 is whether OOK-1 and/or OOK-4 can be separately transmitted with legacy OFDM waveform
UE grouping or sub-grouping management can be simplified for gNB by harmonized design, and less frequency resource will be occupied, which benefits the resource allocation efficiency, so option 3 is preferred
gNB should have implementation flexibility for whether separate or unified transmission is configured
Proposal 1：Direction 1 is preferred for the consideration of gNB implementation flexibility

## Slide 3: Waveform design
The main-lobe of original LP-WUS signal is narrow
Generation effects with whole bandwidth
Generation effects after droping some side-lobe
Same time-domain envelope is generated in different frequency positions
Almost same time domain waveform
Diversity gain
Based on TR 38.869, several generation methods are proposed, and central part repetition scheme need to be further discussed.
For waveform generation the following observations are made - Flat spectrum in frequency domain provides robustness against frequency selective fading compared to concentrated energy in frequency domain. - for OOK-4, sequence before DFT/LS with variation in phase via such as ZC, M-sequence or QAM sequence can achieve more flattened spectrum. Further discuss the following potential observations for waveform generation: - Repetition of a sequence(s) used in LP-WUS generation in frequency can be used to improve diversity for MC-OOK and robustness against frequency offsets for MC-FSK.
Flat spectrum is observed to provide robustness against fading in OOK-4 procedure, which will be further designed for the Rel-19 normative work
Central part repetition scheme is also able to be against the frequency selective fading and should be considered as well
Proposal 2：Support central part repetition scheme as a potential normalized waveform generation procedure

## Slide 4: Coverage target
Based on TR 38.869, the coverage results is listed as follows
The simulation results show the LP-WUS coverage performance is similar to MSG3 PUSCH and worse than PDCCH Considering too many slots are needed for LP-WUS signal to reach an AL16 PDCCH MIL target, comparable with MSG3 coverage performance is more appropriate with reasonable coverage and overhead
RAN1 has carried out coverage evaluation to compare the MIL performance of LP-WUS with that of legacy NR channels (e.g. PUSCH for MSG3, PDCCH for Paging). It is observed that for LP-WUS can achieve comparable MIL performance with that of NR PUSCH MSG3, with the assumed resource for each LP-WUS transmission is as the following, in which RedCap and non-RedCap UE cases are not further distinguished. For Urban scenario and single PUSCH MSG3 transmission For OOK-based LP-WUS, the required resource reported is 0.9~17.28 MHz*Symbol/bit For FSK-based LP-WUS, the required resource reported is 4.32~25.92 MHz*Symbol/bit For OFDM-based LP-WUS, the required resource reported is 0.31~4.32 MHz*Symbol/bit For Urban scenario and PUSCH MSG3 transmission with two retransmissions (one source) For OOK-based LP-WUS, the required resource reported is 241.92 MHz*Symbol/bit For OFDM-based LP-WUS, the required resource reported is 2.16 MHz*Symbol/bit For Rural scenarios and single PUSCH MSG3 transmission For OOK-based LP-WUS, the required resource reported is 0.72~4.32 MHz*Symbol/bit For FSK-based LP-WUS, the required resource reported is 4.32 MHz*Symbol/bit (one source) For OFDM-based LP-WUS, the required resource reported is 0.62~4.36 MHz*Symbol/bit Note the above OFDM symbol assumes subcarrier spacing 30kHz In general, it is much more challenging for LP-WUS to reach comparable MIL as legacy PDCCH with AL16/AL8, more resources occupancy and/or coverage enhancement techniques for LP-WUS transmission would be required to reach such challenging MIL target.
Proposal 3: Coverage target should be comparable with PUSCH MSG3 performance

## Slide 5: LP-WUS for Activation/Deactivation
Since the LP-WUS/LP-SS functionality is similar to paging, at least paging-related information should be contained, such as UE-ID, UE group ID and sub-group ID
Based on TR 38.869, several potential activation and deactivation of LP-WUS monitoring method are proposed
In IDLE/INACTIVE mode, the available UE specific signaling is mainly paging, and the utilization of available system information signaling will not have UE monitoring flexibility. Hence, activation/deactivation of LP-WUS monitoring based on signaling is not appropriate
For IDLE/INACTIVE mode
Proposal 4: Specify procedures to allow UE paging monitoring triggered by LP-WUS in IDEL/INACTIVE mode, and prioritize monitoring behavior based on UE implementation or preconfigured criteria
For CONNECTED mode
Meanwhile, some potential activation/deactivation methods for the CONNECTED mode are also proposed
Some LP-WUS monitoring functionalities such as PDCCH monitoring and similar functionality as R16 DCP are identified
Corresponding procedures to allow UE MR PDCCH monitoring triggered by LP-WUS can be specified
Proposal 5: Specify procedures to allow UE PDCCH monitoring triggered by LP-WUS in CONNECTED mode

## Slide 6: RRM measurement
For IDLE/INACTIVE mode
In IDLE/INACTIVE mode, RRM relaxation and offloading to WUR can be both supported in the serving cell to avoid the frequent trigger of the MR part
RRM measurement offloading to WUR for neighbor cell measurement is difficult to perform
For CONNECTED mode
In CONNECTED mode, since the MR part has been waken up, RRM measurement can be performed on the MR part, which is not necessary for offloading to WUR
The RRM relaxation for the CONNECTED mode can be considered
Proposal 6: RRM measurement relaxation and offloading to WUR can be both specified in serving cell measurement for IDLE/INACTIVE mode
Proposal 7: RRM measurement relaxation can be specified in serving cell measurement for CONNECTED mode

## Slide 7: Potential Rel-19 WID Scope
Specify a unified LP-WUS design for both IDLE/INACTIVE and CONNECTED mode usage
  OOK-1 and/or OOK-4 based LP-WUS is supported for envelope detection LP-WUR
    Flat spectrum scheme is designed for further potential normative work
    Central part repetition scheme should also be supported
  Harmonized design can be also considered
  The generation procedure should be based on existing hardware from gNB transmitter perspective
The coverage performance target for LP-WUS should be comparable to PUSCH MSG3 channel
For IDLE/INACTIVE mode
  Specify necessary procedures to allow UE MR paging monitoring triggered by LP-WUS
    Activate/Deactivate the LP-WUS monitor
  Specify necessary procedure to allow UE RRM measurement
    Consider both RRM measurement relaxation and offloading to LP-WUR for serving cell
For CONNECTED mode
  Specify necessary procedures to allow UE MR PDCCH monitoring triggered by LP-WUS
    Activate/Deactivate the LP-WUS monitor
  Specify necessary procedure to allow UE RRM measurement
    Consider RRM measurement relaxation for serving cell

## Slide 8: Thank You!