## Slide 1
Views on Rel-19 AI/ML for Mobility
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda item: 9.1.2.4
TDoc number: RP-233620

## Slide 2: Use cases
Use cases for Rel-19 study on AI/ML for Mobility:
  Type of Mobility:
    L3-based Mobility (e.g. L3-based handover, CHO)
    L1/L2 based Mobility (LTM)
  Our considerations:
  Both L3-based Mobility and LTM are important in commercial deployment, for L3-based handover and LTM, mobility is triggered based on the measurement results received from the UE. AI-Mobility can be considered to facilitate network selection of target cell/beam.
  For CHO, AI-Mobility can be considered to facilitate network selection of candidate target cells. However, after CHO candidates are configured to the UE, it is up to the UE to select the final target cell/beam based on UE’s evaluation of triggering conditions. If AI is used to select target candidate cell for CHO execution, Mobility performance may degrade because it is out of network’s control.
  The study of AI-Mobility should focus on L3-based handover and LTM for which target cell/beam selection is still within network’s control.
  Proposal 1: Both L3-based Mobility and LTM are considered in the study of Rel-19 AI/ML for Mobility.
  Proposal 2: Focus on the scenario in which handover target cell/beam is determined by the network. AI based target cell/beam selection for CHO execution is down-prioritized.

## Slide 3: AI/ML based L3 Mobility
  Our considerations:
  AI-based L3 Mobility should focus on how to leverage the AI/ML predicted RRM measurement results in L3 based mobility procedure. For measurement prediction, we think both intra-RAT(intra-freq/inter-freq) measurements and inter-RAT measurements should be considered.
  With AI-based RRM measurement prediction (e.g. use intra-freq measurement results to predict inter-freq/inter-RAT measurement results), UE’s measurement effort can be reduced, UE throughput can also be improved if measurement gap can be avoid. In addition, with AI-based target cell prediction, handover failure/Ping-Pong rate can be avoid, so better handover robustness can be achieved.
  Considering network has better knowledge of the coverage information of serving and neighbor cells, including the mobility history of the UE, it makes more sense to maintain a per-cell trained model at network side. So, we think network based solution should be prioritized in AI-based L3 Mobility.
  For performance metrics, can consider: UE measurement power consumption, prediction accuracy, handover latency, handover failure rate, Ping-Pong rate, UE throughput.
  Potential handover failure, RLF should be considered as part of RRM measurement prediction and target cell prediction, individual study on this is not needed.
  Proposal 3: The study of AI/ML based L3 mobility should focus on:
  Study the RRM measurement prediction (e.g. intra/inter-frequency, inter-RAT) for L3 mobility, focus on cell level RRM measurement results prediction (RAN2)
  Identify performance metrics for AI/ML based L3 mobility, and evaluate the benefits of AI/ML based L3 mobility (RAN2)
    Performance metrics can include e.g. UE measurement power consumption, prediction accuracy, handover latency, handover failure rate, Ping-Pong rate, UE throughput;
  Study the signaling requirements (e.g. capability indication, assistant information, configuration and control procedures) and assess potential specification impact (RAN2)
  Network-sided solution should be highly prioritized in the study.

## Slide 4: AI/ML based LTM
  Our considerations:
  Besides LTM candidate configuration (which is based on L3 RRM measurements), LTM cell switch is performed based on L1-level inter-cell beam measurements. In order to significantly reduce mobility latency, the cost of frequent intra/inter-cell L1 measurement and scheduling restriction (for inter-frequency) is paid for both by the NW and the UE sides.
  With advanced ML algorithm, AI based LTM becomes an emerging enabler for the inference of inter-cell beam measurements (involving intra-/inter-frequency and/or spatial-domain measurement compression, and/or temporal domain beam/cell switching prediction). Some detailed evaluation on FR2 high/medium mobility can be found in our companion contribution [1]
    In our views, based on historical data, LTM-AI model can be trained (gNB-specific) in NW, and then, after receiving lists of LTM-related reports (FFS: format refinement (e.g. overhead reduction) and extra parameter(s) (e.g. arrival of time)), the prediction of beam/cell switching can be performed. In such case, advanced application timing for cell switching command may be considered.
  Proposal 4: The study of AI/ML based LTM should focus on:
  Study the L1 inter-cell beam measurements prediction (e.g. intra/inter-frequency) for LTM(RAN1, RAN2)
  Study evaluation methodology (EVM) (e.g. metrics), and identify performance gains by AI/ML based LTM (RAN1, RAN2)
  Study the signaling requirements (e.g. report format, configuration and control procedures, capability indication, and assistant information) and assess potential specification impact (RAN1, RAN2)
[1] RWS-210481, Enhancements on predictable mobility for beam management, ZTE, Sanechips

## Slide 5: LCM framework
  Our considerations:
  Aim to use unified LCM framework for AI/ML for air interface and AI/ML based Mobility.
  Considering life cycle management has been studied for both AI-RAN and AI-PHY in Rel-18, to avoid overlapping, AI based Mobility should only study the new requirements on LCM (e.g. mobility specific LCM procedure and parameters).
  Proposal 5: The study of AI/ML based Mobility should focus on mobility specific LCM procedure and parameters, the conclusions in Rel-18 AI/ML study should be used as a baseline.

## Slide 6: Summary of Proposals
  Proposal 1: Both L3-based Mobility and LTM are considered in the study of Rel-19 AI/ML for Mobility.
  Proposal 2: Focus on the scenario in which handover target cell/beam is determined by the network. AI based target cell/beam selection for CHO execution is down-prioritized.
  Proposal 3: The study of AI/ML based L3 mobility should focus on:
  Study the RRM measurement prediction (e.g. intra/inter-frequency, inter-RAT) for L3 mobility, focus on cell level RRM measurement results prediction (RAN2)
  Identify performance metrics for AI/ML based L3 mobility, and evaluate the benefits of AI/ML based L3 mobility (RAN2)
    Performance metrics can include e.g. UE measurement power consumption, prediction accuracy, handover latency, handover failure rate, Ping-Pong rate, UE throughput;
  Study the signaling requirements (e.g. capability indication, assistant information, configuration and control procedures) and assess potential specification impact (RAN2)
  Network-sided solution should be highly prioritized in the study.
  Proposal 4: The study of AI/ML based LTM should focus on:
  Study the L1 inter-cell beam measurements prediction (e.g. intra/inter-frequency) for LTM(RAN1, RAN2)
  Study evaluation methodology (EVM) (e.g. metrics), and identify performance gains by AI/ML based LTM (RAN1, RAN2)
  Study the signaling requirements (e.g. report format, configuration and control procedures, capability indication, and assistant information) and assess potential specification impact (RAN1, RAN2)
  Proposal 5: The study of AI/ML based Mobility should focus on mobility specific LCM procedure and parameters, the conclusions in Rel-18 AI/ML study should be used as a baseline.

## Slide 7: Proposed objectives
Proposed objectives:
  Mobility use cases:
    L3-based Mobility, focus on L3-based handover which target cell is determined by the network. AI based target cell/beam selection for CHO execution is down-prioritized;
    L1/L2 based Mobility (LTM).
  RRM measurement prediction:
    Study L3 cell level measurement results prediction (e.g. intra/inter-frequency and inter-RAT) for L3 based Mobility, prioritize network-sided model (RAN2)
    Study L1 beam level measurement results prediction (e.g. intra/inter-frequency) for LTM (RAN1, RAN2)
  Performance evaluation:
    Identify performance metrics for AI based L3 mobility, and evaluate the benefits of AI/ML based L3 mobility (RAN2)
    Identify performance metrics for AI based LTM, and evaluate the benefits of AI/ML based LTM (RAN1)
      Performance metrics can include, e.g. UE measurement power consumption, prediction accuracy, handover/LTM latency, handover/LTM failure rate, Ping-Pong rate, UE throughput.
  Assess potential specification impact:
    Study mobility specific LCM procedure and parameters, LCM framework concluded in AI/ML for air interface is taken as a baseline (RAN2/RAN1/RAN3)

## Slide 8: Thank You！