## Slide 1: Views on Demodulation/RRM Topics for Rel-19
NTT DOCOMO, INC., Fujitsu
3GPP TSG RAN #102
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.4.3
Document for: Discussion
RP-233752

## Slide 2: Overview
In last RAN#101, we proposed several topics to be introduced as Rel-19 items and received comments from companies
With consideration of these comments, we brush-up our proposals with clear motivation and possible objectives
The list of proposals for Demod/RRM topic are as follows:
  Performance requirements of MMSE-IRC receiver for NR BS
  FR2 RRM delay reduction enhancements
  HO with PSCell requirements for new scenarios

## Slide 3: Performance requirements of MMSE-IRC receiver for NR BS
Motivation
  According to the changing of mobile communication and expansion of rich context services, e.g. video streaming, uplink traffic has been becoming more important factor for mobile service
  As same as LTE situation, the expansion of NR makes inter-cell interference more severe than when NR service was started
  Moreover, if existing network deployment is designed based on non-HPUE, inter-cell interference from HPUE may cause significant degradation on uplink
  In addition, for multi-vendor architecture, it is difficult to ensure the minimum performance as a whole network from operator point of view, and also it is difficult for new vendor to implement MMSE-IRC receiver with satisfied performance for these network
  Based on above analysis, demodulation performance requirements of MMSE-IRC receiver for NR BS is necessary even if in this later stage

## Slide 4: Performance requirements of MMSE-IRC receiver for NR BS
Possible objectives
  Identify target deployment scenarios and agree on relevant network parameters
    At least homogeneous deployment (macro cell only) should be considered
    Heterogeneous deployment (co-channel between macro cell and low power node) can be deprioritized
    FR2 is not necessary because of its high propagation loss characteristics
  Study applicability of inter-cell interference modelling methodology and other side conditions identified during LTE study, and link-level simulation to evaluate gain of MMSE-IRC over baseline receiver (MMSE receiver)
    Conduct system-level simulation if necessary to determine the inter-cell interference modelling methodology and other side conditions
  NR BS MMSE-IRC receiver shall be assumed as the reference receiver structure for specifying the requirements.
    Demodulation RS based MMSE-IRC receiver can be considered as baseline, and practical and realizable implementation should be taken into account.
  Specify the enhanced demodulation performance requirements for verification of BS receiver’s ability on inter-cell interference suppression.
    For PUSCH, specify enhanced demodulation performance requirements based on the reference receiver.
    For PUCCH, with lower priority, determine whether to specify enhanced demodulation performance requirements based on the reference receiver.
  Specify the enhanced conformance test requirements.

## Slide 5: FR2-1 RRM delay reduction enhancements
Motivation
  During previous releases, FR2-1 RRM delay reduction related topic has been discussed and limited enhancements was specified, e.g. fast SCell activation in Rel-17, SCell activation delay reduction in Rel-18
  Other FR2-1 RRM delay than SCell activation related also take long time in several cases and it may cause inconvenience to operate FR2-1 in commercial network
  For example, BFD evaluation at least takes 800ms and CBD evaluation at least takes 480ms, thus totally more than 1s to prepare beam change in non-DRX mode
  These “seconds order” delay can be problematic even if low mobility assumption

## Slide 6: FR2-1 RRM delay reduction enhancements
Possible objectives
  Identify the possible delay reducible requirements
    Cell selection/re-selection in IDLE/INACTIVE state
    Handover delay
    Radio Link Monitoring
    SCell activation delay
    Link Recovery Procedure
    Intra-frequency measurement
    Inter-frequency measurement
    L1-RSRP measurement
    L1-SINR measurement
  Study applicability of delay reduction methodologies identified previous releases (e.g. fast beam sweeping, multi panel utilization, A-TRS utilization), and also investigate new delay reduction methodologies if necessary
  Specify if needed, reference signal enhancement and/or signaling enhancement for the UE to meet the enhanced delay requirements (RAN2 involved)

## Slide 7: HO with PSCell requirements for new scenarios
Motivation
  In order to fully utilize HO with PSCell in commercial network, the dropped scenarios should be specified and the workload may not be high
  Especially NR-SA to NR-DC (FR1+FR2) is higher priority considering real network deployment
Possible objectives
  Study the applicability of existing requirements for new scenario
  Study UE behavior for HO with PSCell, if any
    Existing requirements for HO and PSCell addition as baseline
    Timeline and interaction between HO and PSCell addition
  Specify RRM requirements for HO with PSCell based on agreed UE behavior