## Slide 1
Agenda item: 9.3.1.1
Source: Samsung, CMCC, MediaTek, Ericsson, Huawei, HiSilicon, NTT DOCOMO,
NTT CORPORATION, ZTE, OPPO, vivo, CableLabs, CATT, China Telecom,
China Unicom, Deutsche Telekom, DISH Network, ETRI, Fraunhofer IIS,
Fraunhofer HHI, Futurewei, Google, HONOR, Interdigital, KDDI, KT Corporation,
Kyocera, LG Electronics, LG Uplus, NEC, New H3C, NICT, Sharp, SK Telecom, Sony,
Tejas Networks, Verizon, Vodafone, Xiaomi
Title: On the scope for Rel-19 NR MIMO Ph5
Document for: Discussion and Decision
3GPP TSG RAN Meeting #105 RP-241774
Melbourne, Australia, September 9-12, 2024

## Slide 2
Background
Rel-19 NR MIMO Ph5 WI has progressed very well and is on track
In RAN#104, the following 3 topics were brought up as candidates of “scope expansion” for Rel-19 MIMO Ph5 WI:
  SRS port grouping for TDD low-complexity 6/8RX receiver
  2TA without CoresetPoolIdx association for asymmetric DL sTRP/UL mTRP
  3T6R SRS antenna switching
The above 3 topics, combined together, add marginal amount of work in RAN1 and other responsible WGs (RAN2, RAN4)
  Also demonstrated in RAN1 to offer benefits in pertinent deployment scenarios and use cases

## Slide 3
Proposal
For Rel-19 NR MIMO Ph5 WI, specify the following 3 features without any TU modification in RAN1, RAN2, and RAN4
  SRS port grouping for TDD low-complexity 6/8RX receiver
  2TA without CoresetPoolIdx association for asymmetric DL sTRP/UL mTRP
  3T6R SRS antenna switching
Discuss the specific objectives and revise the WID accordingly in RAN#105
Commence the work starting from RAN1#118bis (October 2024) per RAN#104 guidance

## Slide 4
References
Simulation results demonstrating necessity of SRS port grouping for low complexity receiver:
[1] R1-2405871, On 128 CSI-RS ports and UE reporting enhancement, Huawei, HiSilicon
[2] R1-2407262, Views on Rel-19 CSI enhancements, Samsung
Simulation results demonstrating necessity of 2TA for asymmetric DL sTRP/UL mTRP:
[3] R1-2406031, Discussion on enhancements for asymmetric DL sTRP/UL mTRP scenarios, ZTE Corporation, Sanechips, China Telecom
[4] R1-2406647, Views on Rel-19 asymmetric DL sTRP/UL mTRP scenarios, Samsung
[5] R1-2406928, Discussion on enhancement for asymmetric DL sTRP/UL mTRP scenarios, NTT DOCOMO, INC.

## Slide 5
Example WID revision
RAN1:
Specify enhancement to facilitate UE-initiated/event-driven beam management for reducing overhead and/or latency, assuming the unified TCI while leveraging (as much as possible) legacy CSI measurement and reporting configuration frameworks, targeting FR2 and sTRP with intra- and inter-cell beam management
  UL signaling content(s) (and procedure(s) as required) for UE-initiated/event-driven beam reporting facilitating fast beam switching
  UL signaling medium/container considering the UE-initiated/event-driven nature of the UL transmission, designed primarily for the purpose of beam reporting
Specify CSI support for up to 128 CSI-RS ports, targeting FR1
  Type-I codebook refinement supporting up to a total of 128 CSI-RS ports across all resources, assuming legacy CSI-RS resources (with up to 32 CSI-RS ports per resource), based on extension of legacy codebooks
  Type-II codebook refinement supporting up to a total of 128 CSI-RS ports across all resources, assuming legacy CSI-RS resources (with up to 32 CSI-RS ports per resource), based on extension of legacy codebooks, without modifying any codebook parameter other than introducing additional values for the number of ports codebook parameter(s)
  Extension of CRI(s)-based CSI reporting (CQI/PMI/RI calculated per CRI for ≥1 CRIs) for hybrid beamforming supporting up to a total of 128 CSI-RS ports across all resources, with up to 32 CSI-RS ports per resource, without new codebook design
  Specify SRS port grouping and codeword association to the two segments of receive antennas for the 6/8Rx low complexity receiver supporting up to 6/8-layers, with legacy codebook and legacy codeword-to-layer mapping
3. Specify UE reporting enhancement for CJT deployments under non-ideal synchronization and backhaul, targeting FR1, both FDD and TDD
    Inter-TRP time misalignment and frequency/phase offset measurement and reporting, assuming legacy CSI-RS design, with stand-alone aperiodic reporting on PUSCH
4. Specify non-coherent UL codebook to facilitate 3-antenna-port codebook-based transmissions, and enhancement(s) to enable 3T6R SRS antenna switching, without enhancement on UL full power transmission and without enhancement on SRS resource
Note: UL full power transmission mode 1 and 2 are not supported.
5. Specify enhancement for asymmetric DL sTRP/UL mTRP deployment scenarios, assuming intra-band intra-DU non-co-located mTRP scenarios, without changing existing cell definition or defining a new cell (e.g. UL-only cell), assuming the Rel-17/18 unified TCI framework and fully reusing the legacy QCL/UL spatial relation rules, targeting FR1 and FR2
  Two closed-loop PC adjustment states for SRS, both separate from PUSCH; and pathloss offset configurations for pathloss calculation to UL TRP(s), when the pathloss RS is from DL sTRP.
  Extending Rel-18 M-DCI-based 2TA toward UL TRP(s) and DL sTRP without using CoresetPoolIndex, while assuming legacy PRACH resources