## Slide 1: Mandatory proposal for Rel-17 CRS-IM
3GPP TSG RAN Meeting #105
Melbourne, Australia, September 9-12, 2024
RP-241811
KDDI corporation, China Telecom

## Slide 2
DSS interference issue
NR
NR/LTE ※mod3=0
NR/LTE ※mod3=1
LTE CRS
interference
NR
NR/LTE ※mod3=0
NR/LTE ※mod3=0
PCI Mod3 matched
rateMatching functionality works
LTE CRS
interference
PCI Mod3 unmatched
rateMatching functionality does not work
Rel-17 CRS-IM works for mitigating NR throughput degradation in Mod3 unmatched case.

## Slide 3
KDDI Testbed Trial for DSS Interference Issue
 | No neighbor cell |  |  | Neighbor cell (mod3 matched) |  |  | Neighbor cell (mod3 unmatched) |  | 
 | THP [Mbps] | Avg MCS | Avg RANK | THP [Mbps] | Avg MCS | Avg RANK | THP [Mbps] | Avg MCS | Avg RANK
A(Rel-16) | ２６０Mbps | 23.2 | 4 | ２３８Mbps | 23.8 | 4 | ６０Mbps | 8.3 | 3.9
B(Rel-16) | ２52Mbps | 23 | 4 | ２３０Mbps | 23 | 4 | １５7Mbps | 16 | 4
C(Rel-15) | ２46Mbps | 23.4 | 4 | １７３Mbps | 23.6 | 3 | ３7Mbps | 8 | 2.8
mod3=1
mod3=2
mod3=0
Mod3
unmatched
Band：n3(DSS with CRS-RM) BW 20M SCS 15MHz 4T4R
Serving: n3 SS-RSRP-80dBm
Neighbor: B3 RSRP-80dBm(non load)
mod3=1
mod3=2
mod3=0
Mod3
matched
With some UEs, NR throughput degradation was critical in mode3 unmatched case. The inability to mitigate NR throughput degradation caused by LTE CRS interference from adjacent cells is hindering the deployment of DSS infrastructure.

## Slide 4
Rel-17 Minimum requirements for CRS-IM (FDD)

## Slide 5
Proposals
Proposal1: RAN agree to confirm a significant throughput degradation without cancelation feature.
Proposal2: RAN agree to check the status of UE implementation regarding Rel-17 CRS-IM feature, “crs-IM-DSS-15kHzSCS-r17”.
Proposal3: RAN agree to discuss from which release to make Rel-17 CRS-IM feature mandatory.
  Option1: from Rel-18 and beyond
  Option2: from Rel-19 and beyond
Proposal4: RAN agree to discuss which band(s) the feature should be mandatory for.

## Slide 6
CR(text proposal) for TS38.306
supportedCRS-InterfMitigation-r17 Indicates whether the UE supports CRS interference mitigation (CRS-IM) in both DSS and non-DSS scenarios with overlapping spectrum for LTE and NR, which is defined in TS 38.101-4 [18]. The capability signalling contains the following: - crs-IM-DSS-15kHzSCS-r17 indicates whether the UE supports neighboring LTE cell CRS-IM in DSS scenario with NR 15 kHz SCS. UE can indicate support of this capability on the CC(s) in a band only if the UE indicates support of rateMatchingLTE-CRS on that band. - crs-IM-nonDSS-15kHzSCS-r17 indicates whether the UE supports neighboring LTE cell CRS-IM in non-DSS and 15 kHz NR SCS scenario, without the assistance of network signalling on LTE channel bandwidth. - crs-IM-nonDSS-NWA-15kHzSCS-r17 indicates whether the UE supports neighboring LTE cell CRS-IM in non-DSS and 15 kHz NR SCS scenario, with the assistance of network signalling on LTE channel bandwidth. - crs-IM-nonDSS-30kHzSCS-r17 indicates whether the UE supports neighboring LTE cell CRS-IM in non-DSS and 30 kHz NR SCS scenario, without the assistance of network signalling on LTE channel bandwidth. - crs-IM-nonDSS-NWA-30kHzSCS-r17 indicates whether the UE supports neighboring LTE cell CRS-IM in non-DSS and 30 kHz NR SCS scenario, with the assistance of network signalling on LTE channel bandwidth. For the UE supporting the capability of crs-IM-DSS-15kHzSCS-r17, the UE can perform CRS-IM without the assistant configuration information of neighbour LTE cells when RateMatchPatternLTE-CRS is configured for the serving cell, and if lte-NeighCellsCRS-Assumptions-r17 is not configured. For the UE supporting the capability of crs-IM-nonDSS-15kHzSCS-r17, the UE can perform CRS-IM without the assistant configuration information of neighbour LTE cells with 15 kHz SCS when RateMatchPatternLTE-CRS is not configured for the serving cell, and if MeasObjectEUTRA is configured, the configured measurement gaps overlap with neighbour LTE cell PBCH position and lte-NeighCellsCRS-Assumptions-r17 is not configured. For the UE supporting the capabilities of crs-IM-nonDSS-30kHzSCS-r17, the UE can perform CRS-IM without the assistant configuration information of neighbour LTE cells with 30 kHz SCS when RateMatchPatternLTE-CRS is not configured for the serving cell, and if MeasObjectEUTRA is configured, the configured measurement gaps overlap with neighbour LTE cell PBCH position and lte-NeighCellsCRS-Assumptions-r17 is not configured. For UEs supporting rateMatchingLTE-CRS for n1/n3/n5/n18, "crs-IM-DSS-15kHzSCS-r17 is mandatory with capability signaling NOTE 1: In the DSS scenario, serving and neighboring cells are both operating with dynamic spectrum sharing (DSS) of NR and LTE. NOTE 2: In the non-DSS scenario, serving cell is operating in NR, and neighboring cells are operating in LTE. | FSPC | No | No | FR1 only