## Slide 1
3GPP TSG RAN #105 RP-241817
Melbourne, Australia, September 9th – 12th, 2024
Agenda Item: 9.1.2
Source: vivo, China Broadnet, NTT DOCOMO, INC., China Telecom, China Unicom, CMCC, Vodafone, Charter, TCL, Spreadtrum, Lenovo, CATT, NEC, Motorola Mobility, CableLabs, Qualcomm Incorporated
Title: Rel-19 MUSIM enhancements work item
Document for: For discussion

## Slide 2
Background
Contributions support:
Operators support: including CMCC, China Telecom, China Unicom, China Broadnet, NTT docomo, Vodafone, Verizon, Charter, CableLabs
Summary in RP-232627

## Slide 3
MUSIM-Gap enhancements
Motivation: For the periodic/short time activities in NW B, a finer granularity MUSIM gap in NW A is more suitable:
R17 per UE MUSIM gap causes data interruption in NW A
R18 MUSIM capability switching causes the related resources release with data throughput loss in NW A
Potential objectives:
  Specify the request/configuration of a finer granularity MUSIM gap (e.g. per CG, per FR, per CC) [RAN2]
Specify new RRM requirement for the finer granularity MUSIM gap [RAN4]
R19: A finer granularity MUSIM Gap

## Slide 4
MUSIM-Optimization for same operator
Motivation:
Based on vivo statistics in China, 34% of dual USIM phones have the USIMs from the same operator.
It is beneficial for the network to know two UEs are in the same device, many network side optimizations are possible by implementation, e.g., common RRM / mobility (e.g., handover to the same gNB/Cell at same time), and network-based UE capability sharing between two USIMs.
Potential objectives:
Case 1: The UE of one USIM informs the gNB the UE and cell identity (e.g., C-RNTI, PCI) of another USIM in the same gNB. [RAN2]
Case 2: The UE of one USIM indicates to the gNB it prefers to connect to a specific cell (e.g., cell ID), such that two USIMs are in the same cell. [RAN2]
Note1: The gNB shall verify that the USIM A and USIM B are physical co-located in the same terminal device [coordination with SA may be needed].
Note 2: The enhancement can also apply to RAN sharing case if any.

## Slide 5
TU allocation
Proposed TU :
RAN2 core part: Total 3TUs (0.5TU per meeting)
RAN4 core part: Total 2.5TUs(0.5TU per meeting, start after one RAN2 meeting)
RAN4 Perf part: Total 0.75TUs(0.25 TU per meeting, start from Q4 2025)