## Slide 1
Views on the scenarios for Ambient IoT in NR
3GPP TSG RAN Meeting #105 RP-241944
Melbourne, Australia, September 9-12, 2024
Agenda: 9.2.2
Source: CMCC, Huawei, ZTE, China Telecom, China Unicom, xiaomi, CATT
Notes: 党的二十大报告44次提到科技，55次提到创新，36次提到人才。刚刚高总也提到了，党中央和国家，对中央企业勇担国家战略科技力量，强化企业创新主体地位的要求之高史无前例。

## Slide 2
Background
  RAN2 company contributions to extend the Ambient IoT study item scope to temporarily out of coverage intermediate UE in RAN2#127 meeting. (R2-2406652)
  Agreements of RAN2:
  Will support in-coverage and study cases for reader “temporarily” out of connection (e.g. RLF, HO). May consider extendibility to future “temporarily” out of coverage case with full NW control of resources (if possible).
  Further discussion:
  As per RAN2 online discussion and chairman notes, lots of companies share their concerns on that case, including CMCC, Huawei, Ericsson, ZTE, LG, Intel, Samsung and so on. They thought the out of coverage is out of scope and should not be considered.

## Slide 3
Investigation of RAN approved SID scope (RP-240826)
Deployment Scenarios with the following characteristics, referenced to the tables in Clause 4.2.2 of TR 38.848:
Deployment scenario 1 with Topology 1
  Basestation and coexistence characteristics: Micro-cell, co-site
Deployment scenario 2 with Topology 2 and UE as intermediate node, under network control
  Basestation and coexistence characteristics: Macro-cell, co-site
  The location of intermediate node is indoor
FR1 licensed spectrum in FDD.
Spectrum deployment in-band to NR, in guard-band to LTE/NR, in standalone band(s).
Traffic types DO-DTT, DT, with focus on rUC1 (indoor inventory) and rUC4 (indoor command).
From RAN#104, the study will assess whether the harmonized air interface design (per bullet ‘A’ above) can address the DO-A (Device-originated autonomous) use case, only to identify which part(s) of the harmonized air interface design (per bullet ‘A’ above) is/are not sufficient for the DO-A use case.
Related Observations
As per the SID, the intermediated UE in topology 2 is always under network control and stay indoor.
For both topology, the FR1 licensed spectrum in FDD is used for D2R and R2D link.
Only indoor scenarios are considered in the SI scope.
Observation 1:
RAN WGs should NOT work on topology scenarios other than Topology 1 and 2 in Rel 19.
RAN WGs should NOT work on scenarios other than indoor scenario for Ambient IoT in Rel 19.
Discussion (1)

## Slide 4
  Our views are as follows:
  The scenario that UE reader is temporarily out of coverage is topology 4, which is not in the scope of study item, considering the workload is already high in RAN, we should not further extend the SI scope for additional scenarios.
  How to handle radio link failure, HO or inactive/idle mode intermediate UE (i.e., out-of-connection) is open to discuss in RAN2.
  Observation 2
  - Intermediate UE out-of-coverage scenario is topology 4 and should NOT be included in the SI scope of Rel 19.
  Observation 3
  RAN Ambient-IoT SI is full loaded and should NOT be extended to include additional scope.
  Sidelink may use ITS spectrums for out-of-coverage services. However, for licensed spectrum, it is always under network control and in-coverage usage from operators’ perspective.
  Observation 4
  License spectrum should restrict to under network control and in-coverage usage.
Discussion (2)

## Slide 5
Observations and Proposal
Observation 1:
RAN WGs should NOT work on topology scenarios other than Topology 1 and 2 in Rel 19.
RAN WGs should NOT work on scenarios other than indoor scenario for Ambient IoT in Rel 19.
  Observation 2：
  Intermediate UE out-of-coverage scenario is topology 4 and should NOT be included in the SI scope of Rel 19.
  Observation 3：
  RAN Ambient-IoT SI is full loaded and should NOT be extended to include additional scope.
  Observation 4：
  License spectrum should restrict to under network control and in-coverage usage.
  Proposal 1:
  Rel-19 Ambient SI does not include UE reader (temporarily) out of coverage scenario.

## Slide 6
  Thank you
Notes: 党的二十大报告44次提到科技，55次提到创新，36次提到人才。刚刚高总也提到了，党中央和国家，对中央企业勇担国家战略科技力量，强化企业创新主体地位的要求之高史无前例。