## Slide 1
Check point for OTA testability related to AI/ML
Agenda: 9.2.8
Source: Samsung
Document for : Discussion and decision
RP-241986

## Slide 2
Background
  According to latest WID for FR2 OTA SI in RP-241158, there is a check point on AI/ML testability in this meeting
  It is dependent on the core part progress on AI/ML beam management
Note: check in RAN#105 regarding whether or not to study OTA testability related aspects such as beam management as related to AI/ML

## Slide 3
AI-BM scenarios
  Channel model is not determined
  Test setup needs more input
  Observation 1: further investigation and convergence on AI-BM scenario aspects in core session are needed for channel model selection and hence decide test setup accordingly.
Issue 2-3: Channel models
Agreement: Further discuss and down-select the following options considering TE feasibility
Option 2: TDL
Option 5: simplified CDL
  CDL channel model with a small number of clusters. CDL simplification needs to be further discussed
Issue 2-4: Test setup needs
Issues listed below to be further investigated in order to determine the capabilities of the test equipment:
set B Tx beams; set A Tx beams
      number of beams transmitted simultaneously
      overall number of beams transmitted during the test
AoA
AoD
UE rotation during the test
Other aspects can also be considered
R4-2414323
R4-2414323

## Slide 4
AI-BM algorithm
  Open issues related with DUT AI algorithm which impact testability
    AI input is only RSRP or not
    Whether UE implementation related aspect considered or not
    Whether UE knows its Rx beam paired with the predicted gNB Tx beam
  Observation 2: further investigation and convergence on AI-BM algorithm aspects in core session are needed before starting AI-BM testability work
Issue 2-8: Beam prediction and TCI state related issues
Proposals
  Option 1: Tx beam prediction does not imply that UE knows the best UE Rx beam to receive the predicted beam
    TCI state for the predicted beam is unknown unless it has been explicitly measured within 1280ms
  Option 2: UE knows the Rx beam paired with the predicted Tx beam
    FFS whether the TCI state associated with a predicted Tx beam is known or unknown
  Option 3: UE knows the Rx beam paired with the predicted Tx beam
    TCI state should be considered known , FFS whether side conditions for known TCI state should be modified (relaxed) for this case
  Option 6: others
R4-2412831

## Slide 5
Observations and Proposals
  Observation 1: further investigation and convergence on AI-BM scenario aspects in core session are needed for channel model selection and hence decide test setup accordingly.
  Observation 2: further investigation and convergence on AI-BM algorithm aspects in core session are needed before starting AI-BM testability work
  We are supportive to include AI/ML testability into FR2 OTA SI, but suggest delay to December meeting.
Proposal：postpone the check point of including AI/ML testability into FR2 OTA SI from RAN#105 to RAN#106