## Slide 1
Huawei, HiSilicon
Checkpoint on study objectives of AI/ML for air interface
3GPP TSG RAN#105 RP-242036
Melbourne, Australia, 9-12 September, 2024
Agenda Item: 9.3.1.3

## Slide 2
Contents
Background
Views on CSI feedback enhancement
Views on model identification and model transfer/delivery
Views on CN/OAM/OTT collection of UE-sided model training data
Views on the testability and interoperability
Summary of proposals

## Slide 3
Background
The WID on AI/ML for NR Air Interface was approved in RAN#102 with the following study objectives:

## Slide 4
Views on CSI feedback enhancement – CSI prediction
Summaries of study status
  Performance
  Benchmark: non-AI/ML based CSI prediction
  Metric: Mean UPT
  Results: 0%~7.8% gain from 7 sources
  Other evaluation aspects are also studied, including channel estimation error/phase discontinuity (higher gain is observed), and generalization
  Other aspects
  Potential specification impact on performance monitoring are studied
  RAN1 conclusion: Study of CSI prediction has been completed and performance improvement is observed with increased complexity
Huawei views
  Observation 1: Performance gain for CSI prediction is limited. However, standard effort can be small, if the signaling/mechanism for LCM of AI/ML based BM-Case 2 and CSI enhancement for mobility in Rel-18 MIMO can be reused as much as possible.
  Proposal 1: Converting CSI prediction (UE-sided model) to normative work can be considered, if specification impact is minimized.

## Slide 5
Views on CSI feedback enhancement – CSI compression
Summaries of study status
Huawei views
  Study status of RAN1
  Performance
  Temporal domain cases: 6 sources show up to ~29% UPT gain at high RU and rank 2 for Case 2 (using past CSI for compression) on top of Rel-16 eTypeII CB, and 2 sources show up to ~22% UPT gain at high RU and rank 2 for Case 3 (using future CSI for compression) on top of Rel-18 eTypeII CB.
  Localized model: 1 source shows up to ~1.2% UPT gain at high RU with FTP traffic, 1 source shows up to ~15.2% UPT gain at high RU with full buffer.
  Complexity/overhead: Complexity for temporal domain cases are plotted, but no particular study/conclusion on complexity reduction methods.
  Inter-vendor training collaboration
  4 candidate options (Option 1/3/4/5), including their sub-options of 3a-1/3a-2/3a-3/3b/4-1/4-2/4-3/5a-1/5a-2/5a-3, are studied with still quite large amount of remaining issues to be further studied in order to conclude on the feasibility, e.g. the 10 big issues identified and listed in the agreements from RAN1#118 (not a full list).
  Other aspects: Candidate monitoring methods are studied, with no conclusion on the feasibility of any of them.
  RAN1 recommendation: Extend the study of the AI/ML CSI compression based on RAN1 understanding that the study is not completed.
  Study status of other WGs
  RAN2: No particular study on CSI compression in RAN2.
  RAN4: Candidate testing options for two-sided model are studied, yet the current progress is not able to justify any of the options.
  Observation 2
  Study on CSI compression is not complete in all the relevant WGs, with large amount of issues to be further studied even for feasibility.
  Long study phase is expected in order to complete the study and conclude on aspects, including at least feasibility, complexity and testability/interoperability.
  Proposal 2: Extend the study of AI/ML based CSI compression to the end of Rel-19.

## Slide 6
Views on model identification and model transfer/delivery
Summaries of study status
  Study status of RAN1
  Model identification
  5 model identification options are discussed in RAN1, and example procedures are provided for MI-Option 1 (data collection based) and MI-Option 2 (dataset delivery based). However, no conclusion on either necessity or feasibility of the options yet, e.g.,
    For MI-Option 1, there is substitute solution without model identification.
    For MI-Option 2 and MI-option 3, the feasibility is coupled with the feasibility of inter-vendor training collaboration of two-sided models.
  Model transfer/delivery
  Cases y/z1/z2/z3/z4/z5 are studied in RAN1, and conclude to deprioritize Case z2 at least for UE-sided model, Case z3, and Case z5.
  It is concluded in RAN1 that model transfer is needed at least for some (e.g., Option 3b) of inter-vendor training collaboration option(s) of CSI compression using two-sided model (if supported). However, it depends on further study of the feasibility/necessity of the inter-vendor training collaboration options.
  RAN1 recommendation : Extend the study of the model identification, and model transfer/model delivery based on RAN1 understanding the study is not completed.
  Study of other WGs
  RAN2 has not conducted corresponding study on model identification details or model transfer/delivery solutions in Rel-19.
Huawei Views
  Observation 3: The study of model identification and model transfer/delivery is not complete in all the relevant WGs, and the feasibility/necessity is coupled with two-sided model (i.e. CSI compression).
  Proposal 3: Extend the study of model identification and model transfer/delivery to the end of Rel-19.

## Slide 7
Views on CN/OAM/OTT collection of UE-sided model training data
Summaries of study status
  Study status of RAN2
  Options 1a/1b/2/3 for CN/OAM/OTT collection of UE-sided model training data are discussed in RAN2, with the result of the analysis captured in Table 7.2.1.3.2-1 in clause 7.2.1.3.2 in TR 38.843.
  The study of option 1a is complete and there is no 3GPP specification impact for option 1a.
  For option 1b/2/3, RAN2 either cannot reach consensus or has not concluded on some aspects, e.g.,
  For Option 1b, RAN2 cannot reach consensus on the level of possible MNO controllability and visibility without input from SA groups.
  For option 2/3, RAN2 cannot reach consensus on the feasibility of UP tunnel, and has not concluded on the need for partial and no visibility options.
  RAN2 cannot conclude on the feasibility of option 1b/2/3, since some of the aspects is out of RAN2 scope, e.g. the potential involvement of NF or other higher layers entities/functionalities and the impact on OTT sever.
  RAN2 has not reached consensus on the need of MNO control over data collection.
  RAN2 has not discussed the exact data content for option 1b/2/3 for each potential use case.
  Study status of other WGs
  No discussion on Options 1b/2/3 in other WGs.
Huawei views
  Observation 4
  The study of option 1a is complete and it can already fully support training data collection for UE-sided model, while necessity/feasibility of option 1b/2/3 is not justified.
  It is unclear whether consensus can be achieved or not in Rel-19 even with further study.
  Proposal 4: For training data collection of UE-sided model, recommend not to convert any option from option 1b/2/3 to normative work in Rel-19.

## Slide 8
Views on the testability and interoperability
Summaries of study status
Huawei views
  Observation 5
  The study of testability and interoperability for both one-sided models and two-sided models are not completed.
  Much less remaining open issues for one-sided model than that for two-sided model, and the feasibility of two-sided model itself depends on further study of other WGs.
  Proposal 5: Extend the study of testability and interoperability to the end of R19.
RAN4 SI AI/ML | Progress till RAN4 #112 | List of main open issues
Testing goal | It is agreed to verify whether the minimum performance of AI/ML functionality/feature can be achieved | Whether and how many different test configurations/parameters are used for tests
Test dataset | Use synthetic channels as the default assumption for conformance requirements/test. | Conduct an analysis for each use case to determine the reliability of using synthetic channels for test data in evaluating models trained on real data.
Feasibility verification of potential testing options | For Option 3 1st round of simulation results collection for checking the feasibility of testing option 3 was performed, however SGCS divergency in range of [0.69,0.79] was observed; Refined simulation parameters are identified, however still struggling for alignment of simulation results in terms of SGCS For Option4 Sub-options (4a/4b/4c) are identified. | For Option 3 To verify the feasibility, at least the following need further study: Performance alignment of the test decoder Framework to share dataset/model among companies Criteria of selecting one or more decoder Performance alignment using companies’ individual encoder Criteria of feasibility For Option 4 Necessity and feasibility study for identified sub-options
General Aspects
Two-sided Model specific
Test metric | Potential test metrics of BM/Positioning are discussed but not concluded yet, since it depends progress of other WGs | Testability and interoperability need to be concluded
One-sided Model specific

## Slide 9
Summary of proposals
For the study of CSI prediction,
  Proposal 1: Converting CSI prediction (UE-sided model) to normative work can be considered, if specification impact is minimized.
For the study of CSI compression,
  Proposal 2: Extend the study of AI/ML based CSI compression to the end of Rel-19.
For the study of model identification and model transfer/delivery,
  Proposal 3: Extend the study of model identification and model transfer/delivery to the end of Rel-19.
For the study of CN/OAM/OTT collection of UE-sided model training data,
  Proposal 4: For training data collection of UE-sided model, recommend not to convert any option from option 1b/2/3 to normative work in Rel-19.
For the study of testability and interoperability,
  Proposal 5: Extend the study of testability and interoperability to the end of R19.