## Slide 1
Introduction of BDS B2b
in A-GNSS in Rel-19
CAICT, CATT, CMCC, China Telecom, China Unicom, CBN, Huawei, Honor, OPPO, Xiaomi, Spreadtrum, ZTE, ASR, H3C, Intel, MediaTek Inc., Qualcomm, China broadnet, Hisilicon, vivo, Ericsson, Swifts, Apple, Nokia, Nokia Shanghai Bell, Reliance Jio, Lenovo, Samsung, IIRC, ADINNO INC.
RP-242044
3GPP TSG RAN Meeting #105
Melbourne, Australia, Sep. 9-12, 2024

## Slide 2
B1I signal(V3.0), B1C signal(V1.0), B2a signal(V1.0) and B3I signal(V1.0) of BeiDou Navigation Satellite System (BDS) have been supported in 3GPP in Rel-17.
BeiDou Navigation Satellite System
Signal In Space Interface Control Document
Open Service Signal B2b (Version 1.0) has been
published by China Satellite Navigation Office,
in August, 2020.
Introduction
Reference : China Satellite Navigation Office, http://www.beidou.gov.cn/xt/gfxz/202008/P020230516558683155109.pdf

## Slide 3
The main reasons that B2b signal should be supported in A-GNSS in Rel-19 are:
B2b signal offers the open global navigation service on B2 frequency and also broadcasts PPP-B2b signals, which can enhance the spectrum compatibility of UE and would reduce UE complexity;
B2b signal can provide A-GNSS four-frequency compatible interoperation capability;
Higher accuracy of A-BDS with dual/multi frequencies on B1, B2 or B3.
Higher processing efficiency with triple frequencies on B1, B2 and B3, by reducing the initial time for ambiguity fixed.
Motivation
Proposal 1: B2b signal should be introduced in A-GNSS in 4G and 5G as well as B1C, B2a etc.

## Slide 4
How to handle?
How to support B2b signal in both 4G and 5G in Rel-19:
  A small WI for supporting BDS B2b signal can be led by RAN2.
    The work load is small, can be finished in no more than 9 months;
    Multiple working groups involved：
      RAN2 (core part), RAN4 (performance part).

## Slide 5
Proposals
Proposal 1: B2b signal should be introduced in A-GNSS in 4G and 5G in Rel-19.
Proposal 2: RAN is kindly requested to discuss and decide how to support BDS B2b signal in both 4G and 5G in Rel-19. The following WF is preferred:
  A small WI for supporting BDS B2b signal can be led by RAN2 .

## Slide 6: Objectives and specifications impacted
Objectives：
  Specify A-BDS enhancements in Rel-19, including :
    Supporting new signal of BDS B2b in A-GNSS for both 4G and 5G [RAN2, RAN4];
    Specify corresponding assistant information in dedicated signaling [RAN2].
Specifications:
Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |  |  | 
TS/TR No. | Description of change | Target completion plenary# | Remarks
TS37.355 | Support BDS B2b signal in A-GNSS, define corresponding assistant data for B2b, and add reference of B2b. | Main CR. RAN#108 | No more than 0.5 TU for each RAN2 meeting. Total <2 TUs for RAN2 are needed. Total 0.5 TU for RAN4 is needed.
TS36.305 | Add corresponding references of B2b. | Small CR. RAN#108 | 
TS38.305 | Add corresponding references of B2b. | Small CR. RAN#108 | 
TS36.171 | Add corresponding references of B2b and define corresponding requirements if needed. | Small CR. RAN#109 | 
TS38.171 | Add corresponding references of B2b and define corresponding requirements if needed. | Small CR. RAN#109 | 
Note: Currently no new posSibType is identified to be defined for B2b. So there is no impact on 36.331/38.331/36.455 and 38.455. |  |  | 

## Slide 7
THANK YOU