## Slide 1: Discussion on RAN4 scope for AI mobility
3GPP TSG RAN Meeting #105 RP-242095
Melbourne, Australia, September 9-12, 2024
Agenda Item: 9.2.5
Source: Xiaomi
Document for: Discussion

## Slide 2: Background: SID (RP-234055)
<<<Focus on testability and NOTE2, check-point for RAN4 scope/work, other part omitted>>>
Evaluate testability, interoperability, and impacts on RRM requirements and performance [RAN4]
NOTE 1: RAN1/3 work can be triggered via LS
NOTE 2: RAN4 scope/work can be defined and confirmed by RAN#105 after some RAN2 discussions (within the RAN4 pre-allocated TUs)
NOTE 3: To avoid duplicate study with “AI/ML for NG-RAN” led by RAN3
NOTE 4: Two-sided model is not included

## Slide 3: Use case: RRM Measurement Prediction
Observation:
  For sub-cased 1, L1 beam-level measurement result(s) is predicted based on measured L1 beam-level measurement result(s). Then Cell-level measurement result(s) will be further obtained based on predicted L1 beam-level measurement result(s).
    RAN4 to study L1 beam-level measurement result(s) prediction requirement, e.g. measurement delay, prediction delay, prediction accuracy, etc.
    RAN4 to study Cell-level measurement result(s) prediction requirement, e.g. measurement delay, prediction delay, prediction accuracy, etc.
  For Sub-use case 2, Cell-level measurement result(s) is predicted based on measured Cell-level measurement result(s).
    RAN4 to study Cell-level measurement result(s) prediction requirement, e.g. measurement delay, prediction delay, prediction accuracy, etc.
  For Sub-use case 3, Cell-level measurement result(s) is predicted based on L1 beam-level measurement result(s).
    RAN4 to study Cell-level measurement result(s) prediction requirement, e.g. measurement delay, prediction delay, prediction accuracy. Etc.
Proposal:
  RAN4 to study RRM requirement for potential L1 beam-level measurement result(s) prediction procedure and/or Cell-level measurement result(s) prediction procedure.

## Slide 4: Use case: RLF Prediction
  RAN2 defines two types of prediction for RLF. i.e. direct and indirect.
  Indirect RLF prediction will have RAN4 impact. In indirect RLF prediction, RLF is derived based on predicted SINR of PCell measurement result(s).
Proposal:
    RAN4 to study SINR prediction related requirement for indirect prediction case.

## Slide 5
Thanks！