## Slide 1: Views on RAN4 scope of Rel-19 AI/ML for mobility in NR
CATT
3GPP TSG RAN Meeting #105
Melbourne, Australia, September 9-12, 2024
Agenda item: 9.2.5
RP-242136

## Slide 2: Background
According to the SID[1], all work is led by RAN2, and RAN4 is advised to start evaluations from RAN4#112bis:
  Evaluate testability and interoperability
  Evaluate impacts on RRM requirements and performance
Considering RAN4 work scope will be defined and confirmed in RAN#105, we will present our views on the specific RAN4 work scope in this contribution.
RAN2 progress till RAN#105 is briefly summarized:
  Case 1: RRM measurement prediction
    Completed the 1st round of performance evaluation
  Case 2: Measurement event prediction
    Deprioritized
  Case 3: RLF/HO prediction
    RLF prediction: Completed the initial discussion on simulation assumptions
    HO prediction: Deprioritized
[1] RP-234055, Study on Artificial Intelligence (AI)/Machine Learning (ML) for mobility in NR, RAN#102.

## Slide 3: Discussion
Based on the summary, it is observed that RAN2 progress is limited, especially in measurement event prediction and RLF/HO prediction. Therefore it is too early for RAN4 to start evaluations for Case 2 and 3.
Observation 1: It is too early for RAN4 to access testability, interoperability and RRM impacts of measurement event prediction and RLF/HO prediction.
For RRM measurement prediction, discussions on testability and interoperability will largely overlap with the ongoing discussions on beam management in Rel-19 AI/ML air interface WI. To avoid duplicated efforts, we believe that agreements from those discussions can be reused for Case 1 in AI/ML for mobility in NR SI.
Observation 2: Discussions on testability and interoperability of Case 1 are similar to the ongoing discussions for BM in Rel-19 AI/ML air interface.

## Slide 4: Discussion
Regarding the impacts of Case 1 on RRM requirements, we do not see a strong motivation to start RAN4 evaluations in the October meeting. Given that one-sided models are used and existing measurement quantities and reporting schemes are assumed in RAN2, RAN4 workload on RRM impacts should be manageable and can start during the WI stage.
Observation 3: RAN4 workload of Case 1 is manageable, considering existing measurement quantities and reporting schemes are assumed in RAN2.
Therefore RAN4 study work, if any, can start after RAN2 have made sufficient progress, or can be triggered by RAN2 LS if RAN2 identify any issues that need to be addressed by RAN4.
Based on the observations and above analysis, we have the following proposal:
Proposal 1: Postpone the checkpoint of RAN4 work till RAN#106.

## Slide 5: Conclusion
Observation 1: It is too early for RAN4 to access testability, interoperability and RRM impacts of measurement event prediction and RLF/HO prediction.
Observation 2: Discussions on testability and interoperability of Case 1 are similar to the ongoing discussions for BM in Rel-19 AI/ML air interface.
Observation 3: RAN4 workload of Case 1 is manageable, considering existing measurement quantities and reporting schemes are assumed in RAN2.
Proposal 1: Postpone the checkpoint of RAN4 work till RAN#106.

## Slide 6
Notes: 万物互联，无限沟通
Universal Connectivity, Infinite Communication.