## Slide 1: Remaining gaps in IoT NTN for Rel-19
Source: Inmarsat, Viasat, Echostar, Novamint, Sateliot
3GPP TSG RAN #105
September 9-13th, 2024, Melbourne Australia
Agenda: 9.1.2 - Proposals led by RAN2
TDOC: RP-242142
For: decision
Public

## Slide 2: General Mindset (yes, you’ve seen this before )
NTN is a reality now, with networks being deployed as we speak.
Initial focus of deployments and products has been NB-IoT NTN in FR1, but systems will evolve in time
NB-IoT NTN devices are reaching the market TODAY, (some even before the Release 17 and 18 work has been fully finalized)
NB-IoT NTN was slightly rushed to market with a shorter Work Item phase in R17, this achieved the proposed goal of meeting market demand, but meant some aspects were missed.
We must focus on:
  Features that ensure better system efficiency based on learnings from field
  Features that facilitate deployment and ROI
Release 19 is likely the last chance to improve what’s missing before too many products are already on the market.

## Slide 3: Discussed in RAN#102
Key Remaining aspects for IoT NTN:
Network-Controlled/Steered Anchor-to-Anchor Carrier Switching [RAN2]
Inter-RAT mobility between TN (NR, LTE) and IoT NTN (Idle and Connected mode) [RAN2]
5GC Support for IoT NTN [RAN3, RAN2]
Efficient Multicast Delivery via SC-PTM [RAN2]

## Slide 4: Network-Controlled/Steered Anchor-to-Anchor Carrier Switching for NB-IoT
Rationale/Background:
Satellite and satellite beam coverage areas are very large, with different beam sizes and very likely include multiple NB-IoT NTN carriers in the same footprint
There are situations in which the network may need to move UE between NB-IoT NTN carriers for load-balancing or frequency management purposes
There are situations in which the network may need to offload UE between beams for mobility, coverage, frequency or load-balancing purposes
NB-IoT does not support CONNECTED_MODE mobility or any kind of Network-controlled mobility or load-balancing
A combination of multiple NB-IoT NTN Anchor and Non-anchor carriers may be deployed within any given satellite beam coverage area
NTN operators may have a constraint of being able to deploy only Anchor carriers in adjacent beams or within the same beam
Moreover, it is likely expected that additional Non-Anchor carriers associated with a given Anchor carrier are only deployed within the same beam, and that adjacent beams will mostly be associated with different Anchor carriers

## Slide 5: Network-Controlled/Steered Anchor-to-Anchor Carrier Switching for NB-IoT
Proposal 1: Revise the current IoT_NTN_Ph3 WID, to include the following objectives:
Identify and specify NB-IoT enhancements to support an efficient mechanism for Network-controlled or steered Anchor-to-Anchor and non-anchor-to-Anchor carrier switching for UE, beyond one-off RRC based re-direction [RAN2]
  Including after initial attach and in Connected Mode
  Note : No impact on connected measurements
  Note: How carriers are mapped to same or different satellite beams is left to an Operator’s deployment considerations

## Slide 6: Inter-RAT mobility between TN (NR, LTE) and IoT NTN
Despite the extensive work on Mobility aspects for NTN, many buildings blocks in TN-NTN mobility are still missing
TN-NTN Mobility has been (or is being) almost fully addressed for NR NTN (except mobility from E-UTRA, which is currently being addressed).
Some aspects have been ported to/from IoT NTN – but mostly limited to NTN-NTN
Chiefly, Mobility from E-UTRA TN and NR TN to IoT NTN is not yet fully specified
A number of UE will be developed with full LTE and NR TN support, but only IoT NTN support
Proposal 2: Revise the current IoT_NTN_Ph3 WID to include the following objective:
Specify missing aspects to support TN-NTN inter-RAT mobility towards IoT NTN (eMTC, NB-IoT)
  to support Idle mode mobility via Cell Reselection from E-UTRA TN and IoT NTN
  to support Idle mode mobility via Cell Reselection from NR TN and IoT NTN
  to support Connected mode mobility via Handover (HO) and Conditional Handover (CHO) from E-UTRA TN and IoT NTN
  to support Connected mode mobility via Handover (HO) and Conditional Handover (CHO) from NR TN and IoT NTN

## Slide 7: 5GC Support for IoT NTN
IoT NTN currently only specified for 4G (EPS)
Lack of appetite for further carryover of 4G System in the 6G era
Need a path forward for IoT NTN for 5G towards 6G
NB-IoT and eMTC are already supported by 5GC for TN
Minimal work required to complete the spec and include NTN
Proposal 3: Revise the current IoT_NTN_Ph3 WID to include specification of 5GC support for IoT NTN
  Address remaining gaps in overall 5GC support for CIoT (NB-IoT, eMTC) – e.g. MT-EDT, etc.
  Liaison with SA2 as required

## Slide 8: Efficient Multicast Delivery for IoT NTN
Rationale:
Satellite is by nature a broadcast medium, that can quickly reach very large coverage areas even when terrestrial networks are down.
Radio resource density per km^2 of NTN systems is much, much smaller than TN
Delivery of same data to a very large UE population in the same area via Unicast is not scalable (resource requirement scales with the number of UE, which for NTN with large coverage areas per-cell is simply not viable!)
With Multicast/Broadast, service delivery becomes more and more efficient with more and more UE are targeted!
Use Cases include (but not limited):
Firmware and configuration delivery (for IIoT, Automotive, etc)
Emergency broadcast messaging (e.g. EW4All)
Public safety communications (e.g. such as first responders, emergency services, disaster response teams) and Other Group Communications: media and news network teams exchanging information during a news coverage event, private citizens within a closed communications group.
  Services will include group messaging, group data and file sharing, group PTT voice, etc.
We think making Multicast/Broadcast work well on IoT NTN is a key aspect and a very low hanging fruit which can significantly improve the addressable market and quality of services provided via NTN
Source: https://www.un.org/en/climatechange/early-warnings-for-all

## Slide 9: Efficient Multicast Delivery for IoT NTN
Proposal 4: Revise the current IoT_NTN_Ph3 WID, to include the following objectives:
Identify and specify enhancement to current SC-PTM implementation with reduced signalling overhead and more flexible resource allocation, to improve efficiency and delivery times. [RAN2]
  Reduction of requirements for periodic service announcements (and corresponding UE monitoring requirement), i.e. only when data is actually available via on-demand paging
  Network-directed service delivery (removal of mandatory UE-driven joining requirement)
  e.g. semi-persistent scheduling, more flexible packet size and TBS
  Emergency broadcast message with priority – entire cell or sub-set of the UE in a cell
Assumptions:
  No impact to physical layer channels
  Re-use wherever possible mechanisms currently being defined for MBS in NR NTN

## Slide 10: Thank you!