## Slide 1: NR_AIML_Air Rapporteurs' inputs for Discussion
AI: 9.3.1.3
Qualcomm, CAICT, Ericsson
RP-242226
3GPP TSG RAN#105
Melbourne, Australia
September 9-12, 2024

## Slide 2: Outline
Study objectives in NR_AIML_Air with checkpoints in RAN#105
Summary of relevant open issues in SR (RP-241910) requiring discussion & RAN guidance
Rapporteurs’ recommendations

## Slide 3: Study Objectives in NR_AIML_Air (1/3) with checkpoints in RAN#105 [WID in RP-240774]
CSI feedback enhancement [RAN1]:
  For CSI compression (two-sided model), further study ways to:
    Improve trade-off between performance and complexity/overhead
      e.g., considering extending the spatial/frequency compression to spatial/temporal/frequency compression, cell/site specific models, CSI compression plus prediction (compared to Rel-18 non-AI/ML based approach), etc.
    Alleviate/resolve issues related to inter-vendor training collaboration.
    while addressing other aspects requiring further study/conclusion as captured in the conclusions section of the TR 38.843.
  For CSI prediction (one-sided model), further study performance gain over Rel-18 non-AI/ML based approach and associated complexity, while addressing other aspects requiring further study/conclusion as captured in the conclusions section of the TR 38.843 (e.g., cell/site specific model could be considered to improve performance gain).
Study objectives with corresponding checkpoints in RAN#105 (Sept ’24):

## Slide 4: Study Objectives in NR_AIML_Air (2/3) with checkpoints in RAN#105 [WID in RP-240774]
Necessity and details of model Identification concept and procedure in the context of LCM [RAN2/RAN1]
CN/OAM/OTT collection of UE-sided model training data [RAN2/RAN1]:
  For the FS_NR_AIML_Air study use cases, identify the corresponding contents of UE data collection
  Analyse the UE data collection mechanisms identified during the FS_NR_AIML_Air (TR 38.843 section 7.2.1.3.2) study along with the implications and limitations of each of the methods
Model transfer/delivery [RAN2/RAN1]:
  Determine whether there is a need to consider standardised solutions for transferring/delivering AI/ML model(s) considering at least the solutions identified during the FS_NR_AIML_Air study

## Slide 5: Study Objectives in NR_AIML_Air (3/3) with checkpoints in RAN#105 [WID in RP-240774]
Testability and interoperability [RAN4]:
  Finalize the testing framework and procedure for one-sided models and further analyse the various testing options for two-sided models, in collaboration with RAN1, and including at least:
    Relation to legacy requirements
    Performance monitoring and LCM aspects considering use-case specifics
    Generalization aspects
    Static/non-static scenarios/conditions and propagation conditions for testing (e.g., CDL, field data, etc.)
    UE processing capability and limitations
    Post-deployment validation due to model change/drift
  RAN5 aspects related to testability and interoperability to be addressed on a request basis
NOTE: offline training is assumed for the purpose of this project.
NOTE: the outcome of the study objectives should be captured in TR 38.843 for future reference.
NOTE: Coordination with SA/SA WGs of the ongoing study/work as it may relate to their required work.

## Slide 6: Remaining Open Issues from Status Report
RAN1:
  […]
  Decide how to proceed with the CSI prediction study: continue the study, start normative work or stop.
  Extend study on CSI compression
  Extend study on other aspects of AI/ML model and data with RAN1 impact
RAN2:
  […]
  Related to the topic of UE-side data collection, it should be decided how to proceed considering the RAN2 analysis captured in TP for TR 38.843 in R2-2407807. The decision could be whether to continue the study in RAN, whether to start or not a normative work in RAN, whether to involve SA WGs in the discussion
[SR in RP-241910]

## Slide 7: Remaining Open Issues from Status Report
RAN4:
General aspects
  Post deployment handling
  AI/ML model performance
  Generalization
  LCM handling
Testability and interoperability issues for beam management
  Metrics/KPIs for BM
  RSRP Prediction accuracy
  Reported measurements and ground truth related issues
  Channel models
  Test setup needs
  OTA Test setup for beam management
  Measurement error impact
  UE reporting for network side models
  Beam prediction and TCI state related issues
  UE side beam prediction requirements impact
Testability and interoperability issues for positioning accuracy enhancement
  Requirements for case 1/2a/2b/3a/3b
  Requirements for measurements and reported metrics/values
  KPIs
Testability and interoperability issues for CSI compression and CSI prediction
  CSI Prediction Accuracy metrics
  Testing options for 2-sided model
  Reference/test encoder/decoder
  Option 3 for 2-sided model
  Option 4 for 2-sided model
  Comparison table
[SR in RP-241910]

## Slide 8: CSI Prediction (RAN1)
Agreement
From RAN1 perspective, study of CSI prediction has been completed and performance improvement is observed with increased complexity.
Rapporteurs’ observation:
  Majority of companies would like to proceed to normative phase
  No consensus in RAN1 for moving to normative phase
    Modest gains and possibility for allegedly achieving most of the gains by implementation means observed as main reasons for not recommending normative work
  More studies not expected to change the landscape
Rapporteurs’ recommendation:
  Proposal 1: Move CSI prediction to normative phase with well-defined scope (to be discussed in RAN#105).

## Slide 9: CSI Compression (RAN1)
Rapporteurs’ observation:
  Good progress made in Q1/Q2/Q3 to better understand the trade-off between performance and complexity/overhead, and the ways to alleviate/resolve issues related to inter-vendor training collaboration
Rapporteurs’ recommendation:
  Proposal 2: Extend the CSI compression study objective one additional quarter as recommended by RAN1.
Agreement
RAN1 is recommending extending the study of the AI/ML CSI compression based on RAN1 understanding the study on CSI compression is not completed.

## Slide 10: Model identif, Model transfer/Model delivery
Agreement
RAN1 is recommending extending the study of the Model identification, and Model transfer/Model delivery based on RAN1 understanding the study is not completed.
Rapporteurs’ observation:
  Good progress made in Q1/Q2/Q3 to better understand the utility and necessity of model identification and model transfer/delivery
Rapporteurs’ recommendation:
  Proposal 3: Extend the Model identification, and Model transfer/Model delivery one additional quarter as recommended by RAN1.

## Slide 11: UE-side data collection (RAN2)
Rapporteurs’ observation:
  RAN2 has continued the discussion on the topic of UE side data collection for UE-side model training and agreed on TP for TR 38.843 on this topic (R2-2407807) where multiple options are identified and analyzed.
  More discussions on this topic in RAN2 not expected to be valuable
Rapporteurs’ recommendation:
  Proposal 4: Inform SA & SA WGs of RAN2 analysis on UE-side data collection for them to take it into consideration in their work.

## Slide 12: Testability and Interoperability
Rapporteur’s observation:
  Good progress made in Q2/Q3 on testability aspects
    Continued discussions on testability of two-sided models are needed
    Beam management OTA test setup requires attention
    Early RAN5 involvement may be desirable
Rapporteur’s recommendation:
  Proposal 5: Extend the testability and interoperability study objective one more quarter. Discuss how to proceed with Beam management OTA test setup. Discuss whether and how to involve RAN5 in this project.

## Slide 13: Thank you