## Slide 1: Way Forward on Additional Study for AI/ML for Air Interface
Source: AT&T
Agenda Item: 9.3.1.3
RP-242228
3GPP RAN#105
Melbourne , Australia, Sept 9–12, 2024

## Slide 2: CSI Prediction
Observation 1: CSI prediction study in RAN1 considered limited specification impact related to data collection and performance monitoring
Observation 2: CSI prediction evaluations in RAN1 showed small mean UPT gain (0% to 7.8%) dependent on the traffic model.
Observation 3: CSI prediction evaluations in RAN1 showed moderate gains for 5% UE UPT (3.8% to 20.7%) dependent on traffic model.
Observation 4: RAN1 conducted a limited number of generalization studies on aspects other than UE speed. The generalization studies showed that the model does not generalize well as we increase the number of speeds in the training data set.
Observation 5: AI/ML model for CSI prediction requires site specific models to perform well in practical settings, due to poor generalization performance over multiple aspects
Observation 6: RAN1 showed limited results on solutions to improve performance for 20ms CSI-RS periodicity.
Observation 7: Additional specification impact is required for techniques used to improve AI/ML model performance for 20ms CSI-RS periodicity
Based on the above observations, the CSI prediction use case provides gains only for high mobility users at the cell edge. Furthermore, a generalized model will have poor performance in practical settings.
Proposal 1: RAN to conclude that the study for CSI prediction is complete, based on RAN1 agreement.
Proposal 2: RAN to conclude that CSI prediction use case is not recommended for further normative work.
RP-242228

## Slide 3: CSI Compression
Observation 8: CSI compression is the only 2-sided AI/ML use case.
Observation 9: Inter-vendor collaboration, model identification, model transfer/delivery are critical topics that need to be studied in Rel-19.
Observation 10: CSI compression evaluations in RAN1 showed moderate to high gains for mean UE UPT dependent on traffic model, RU utilization and rank.
Observation 11: CSI compression evaluations in RAN1 showed high gains for 5% UE UPT dependent on traffic model, RU utilization and rank.
Based on the above observations, we propose the following:
Proposal 3: RAN to extend the study of the AI/ML CSI compression.
RP-242228

## Slide 4: Other aspects of AI/ML model and data
Observation 12: LCM aspects related to Model Identification and procedures, and Model transfer/delivery are still not fully studied.
Observation 13: General framework of AI/ML models continues to be developed alongside the different AI/ML use cases as we get more clarity regarding the requirements of different use cases.
Based on the above observations, we propose the following:
Proposal 4: RAN to extend the study of the general framework aspects for AI/ML models, e.g., Model Identification/procedures, Model transfer and delivery.
RP-242228

## Slide 5: Summary
RAN Plenary to agree the following WI updates for “NR_AIML_air”:
Proposal 1: RAN to conclude that the study for CSI prediction is complete, based on RAN1 agreement.
Proposal 2: RAN to conclude that CSI prediction use case is not recommended for further normative work.
Proposal 3: RAN to extend the study of the AI/ML CSI compression.
Proposal 4: RAN to extend the study of the general framework aspects for AI/ML models, e.g., Model Identification/procedures, Model transfer and delivery.
RP-242228

## Slide 6: References
3GPP TR 38.843 “Study on Artificial Intelligence (AI)/Machine Learning (ML) for NR air interface,” Rel-18.
R1-2407478 Session notes for 9.1 (AI/ML for NR Air Interface), Ad-Hoc Chair (CMCC)
RP-240774, Revised WID on Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface, Qualcomm.
R1-2407341, Summary #4 of CSI prediction
R1-2407495, Draft summary of Additional study on AI/ML for NR air interface: CSI compression
R1-2407499, Summary of Evaluation Results for Additional study on AI/ML for NR air interface: CSI compression
R1-2407305, Summary#4 for other aspects of AI/ML model and data
R1-2407520, TPs to capture the outputs of 9.1.3.3