## Slide 1: LGE views on Rel-20 AIML Mobility

## Slide 2: Progress of Rel-19 AIML Mobility SI
Ongoing work in Rel-19 AIML Mobility SI
  Two main goals for AIML mobility use cases
    1st goal: measurement reduction
    2nd goal: handover performance improvement
  Three use cases under evaluations
    1) RRM prediction
      Prediction of L3 cell level measurement results
      Prediction of L3 beam level measurement results
    2) Measurement event prediction
      Prediction of event satisfaction for event A1-A5 (A3 as starting point)
      The RRM prediction results are used for measurement event prediction, i.e., indirect prediction is baseline.
      Output:
        Probability of event occurrence within a time window (direct)
        Expected occurrence time of a measurement event satisfaction (indirect)
    3) RLF prediction
      Direct RLF prediction (RLF prediction directly based on actual measurements of PCell quality)
      Indirect RLF prediction (RLF prediction based on predicted on PCell quality)
      Output:
        Probability of RLF within a time window (direct)
        Expected occurrence time of RLF (indirect)
scenario number | Priority | Evaluation scenario | Target study goal | Methodology
1 | Low | FR1 to FR1 intra-frequency temporal domain case A | 2nd goal | TBD
2 | High | FR1 to FR1 intra-frequency temporal domain case B | 1st goal | Intra-cell
3 | High | FR1 to FR1 inter-frequency frequency domain | 1st goal | Inter-cell
4 | High | FR2 to FR2 intra-frequency temporal domain case A | 2nd goal | Intra-cell
5 | Low | FR2 to FR2 intra-frequency temporal domain case B | 1st goal | TBD
6 | Middle | FR2 to FR2 intra-frequency spatial domain | 1st goal | Intra-cell
Scenarios for RRM prediction in TR 38.744

## Slide 3: Justification of Rel-20 AIML Mobility WI
Our observations from the simulation results
  AIML based RRM prediction can predict RSRP with acceptable accuracy in several use cases including time domain prediction, spatial domain prediction, and frequency domain prediction.
  AIML based RRM prediction can outperform non-AI approaches in time domain prediction. The performance difference is larger with longer prediction window.
  AIML based RRM prediction can provide measurement reduction gain, and meaningful measurement reduction gain is achieved in intra-frequency intra-cell prediction (spatial domain prediction) and inter-frequency RRM prediction (frequency domain prediction).
  Generalization performance needs further investigation due to insufficient simulation results.
Tentative conclusion from the observations
  The acceptable accuracy of AIML based RRM prediction reported so far implicitly shows that, if the AIML based RRM prediction capabilities are employed in existing relevant procedures, both measurement reduction gain and handover performance improvement can be achieved in several cases.
In our view,
  Gains from AIML mobility are observed from the initial simulation results of Rel-19 AIML mobility SI. This justifies Rel-20 AIML mobility WI.
  Once AIML mobility features are introduced in Rel-20, these features can be the baseline for AI-empowered 6G RRM and mobility from 6G day1. To promote success of 6G, normative work on AIML mobility in Rel-20 should be incentivized.

## Slide 4: Potential Scope of AIML Mobility WI
Use cases for normative work
  Work scope should be strictly limited to use cases well studied in Rel-19 AIML Mobility SI, in order to mange the normative work with minimal uncertainty.
  That is, normative work should only address the use cases of RRM prediction, Measurement report event prediction, and RLF prediction, as specified in TR 38.744.
Procedures for AIML mobility
  Modification/extension of existing procedures should be the prioritized, whenever possible, instead of specifying entirely new procedures.
    For RRM prediction and event prediction, existing measurement and measurement reporting procedures in TS 38.331 can be extended.
    For RLF prediction, existing RLF declaration and failure reporting procedures in TS 38.331 can be extended.
Other core functionalities to support AIML mobility
  To address different UE capabilities related to AIML mobility, UE capability signaling should be extended
  To address generalization of AI models/functionalities, applicable functionality reporting procedure, being introduced in Rel-19 AIML PHY, can be extended.

## Slide 5: Potential Scope of AIML Mobility WI
RRM prediction use case
  RAN2 procedures (network configuration and UE behaviors) on AI-based RRM measurement reduction
    Spatial domain and frequency domain prediction are focused to achieve measurement reduction.
  RAN4 requirements on RRM measurements with AI-based measurement reduction
Event prediction use case
  Specify RAN2 procedures (network configuration and UE behaviors) to support AI-based measurement report event prediction
    Existing measurement report procedure is extended.
    Event A1 to A5 are considered
    Temporal prediction is focused to achieve handover performance improvement.
  Both direct and indirect predictions are supported.
    Prediction of expected occurrence time of measurement event satisfaction (indirect)
    Prediction of probability of measurement event satisfaction within time window (direct)
RLF prediction use case
  Specify RAN2 procedures (network configuration and UE behaviors) to support AI-based RLF prediction and avoidance.
    Existing RLF declaration procedure and failure reporting procedure are extended.
  Both direct and indirect predictions are supported
    Prediction of expected RLF occurrence time (indirect)
    Prediction of RLF probability within time window (direct)
  RAN4 requirements on RLF prediction

## Slide 6: Potential Scope of Rel-20 AIML Mobility WI
Other functionalities required to support AIML mobility use cases
  LCM for AIML mobility use cases (R2)
    Inference performance monitoring
    Fallback to non-AIML based functionalities
  Capability signaling and updates for AIML mobility use cases (R2)
    Extension of capability signaling
    Extension of functionality applicability reporting
  Data collection for AIML mobility use cases (R2)
    Data collection for UE sided model training
    Data collection for NW sided model training

## Slide 7: Summary
Justification of Rel-20 AIML mobility WI
  Gains from AIML mobility are observed from the initial simulation results of Rel-19 AIML mobility SI. This justifies Rel-20 AIML mobility WI.
  Once AIML mobility features are introduced in Rel-20, these features can be the baseline for AI-empowered 6G RRM and mobility from 6G day1. To promote success of 6G, normative work on AIML mobility in Rel-20 should be incentivized.
Preferred work scope
  Extend existing procedures for AIML mobility use cases (R2)
    Extend RRM measurement procedures to support RRM prediction, with the focus on spatial domain and frequency domain prediction, to achieve measurement reduction.
    Extend measurement report procedures to support MR event prediction for event A1~A5, with the focus on temporal prediction, to achieve handover performance improvement.
    Extend RLF and failure reporting procedure to support RLF prediction and RLF avoidance.
  LCM for AIML mobility use cases (R2)
    Inference performance monitoring
    Fallback to non-AIML based functionalities
  Procedures for capability signaling and updates for AIML mobility use cases (R2)
    Extension of capability signaling
    Extension of functionality applicability reporting
  Data collection for AIML mobility use cases (R2)
    Data collection for UE sided model training
    Data collection for NW sided model training
  Performance requirements for RRM prediction and RLF prediction (R4)