## Slide 1: Motivation for a new work item on low band carrier aggregation via switching in Rel-19
3GPP TSG RAN Meeting #106
Madrid, Spain, December 9-12, 2024
Agenda Item 9.1.4
Source: AT&T, Anterix, Apple, Bell Mobility, Boost Mobile Network, BT plc, Ericsson, Google, HiSilicon, Huawei, Murata, Nokia, OPPO, Qorvo, Qualcomm, Samsung, Skyworks Solutions Inc., Sony, Southern Linc, TELUS, vivo, ZTE
RP-242532

## Slide 2: Motivation
Low-bands carry significant traffic volumes in MNO networks both in urban and rural markets.
Considering n29 is DL only band, n29 capacity is completely lost in low-bands only coverage areas
Today’s low band challenge:
The amount of mid-band spectrum an operator holds is typically 10-20 times greater than their low-band spectrum holdings.
Mid-band spectrum is more effective closer to cell sites, while low-band spectrum propagates farther, making it more useful at greater distances from sites.
Low-band spectrum carries significant traffic volumes in urban (indoor) and rural areas, leading to congestion that severely degrades customer experience.
This issue is exacerbated by the fact that low-band SDL bands, which reach most poor coverage areas, cannot be paired with an UL, rendering them useless.
Utilization of SDL bands via Low-Low band CA, where one low band serves as an SDL, could potentially solve this problem. However, this solution doesn't exist due to OEM challenges in supporting it.
B29 is widely deployed in Canada and the USA but is underutilized
  Bell and TELUS together have nationwide access to 10 MHz of MBS – DL only (n29) in 700MHz spectrum.
  Band 29 reaches 83% of Canada’s pop.
We would like to propose a solution that enables SDL utilization via a version of low-low CA with minimal impact to the devices
85% of traffic in urban
50% of traffic in rural
15% of traffic in urban
50% of traffic in rural
Mid-bands
Low-bands

## Slide 3: Proposed low-low CA solution
Device needs to support inter-carrier scheduling: UE monitors FDD DL PDCCH DCI, which has both FDD and SDL scheduling
Device switches back to FDD duplexer after SDL scheduled transmission interval is finished
TTI :
TTI :
FDD band
Tx
Rx
SDL band
Rx
Transceiver
TTI :
Tx
Rx
Rx
Transceiver
Tx
Rx
Rx
Transceiver
FDD band
SDL band
FDD band
SDL band

## Slide 4: Scenarios where this solution would be useful

## Slide 5: Observations
Observation 1:Band n29 falls within the duplex gap of band n12 and leaves 1 MHz for the filter stopband between n12 UL and n29 DL. With current duplexer technology, a solution based on traditional carrier aggregation architecture does not seem feasible.
Observation 2:Band n106 UL is separated from band n26 DL by 2 MHz. With current duplexer technology, a solution based on traditional carrier aggregation architecture does not seem feasible.
Observation 3:Band n67 DL overlaps with band n28 UL. With current duplexer technology, a solution based on traditional carrier aggregation architecture does not seem feasible.
Observation 4:In the case of aggregating n5 with n29 via a single antenna, optimization of radiated performance in both bands simultaneously can be challenging due to their separation in frequency, while a potential design choice to implement additional antenna elements to support these combinations may carry cost and RF architecture complexity impacts in terms of additional components and volume in the form factor.
Observation 5:In the case of aggregating n14 with n29, a solution based on switching the n14 and n29 carriers is useful to consider.
Observation 6:In the case of aggregating n29 with n71 via a single antenna, optimization of radiated performance in both bands simultaneously can be challenging due to their separation in frequency, while a potential design choice to implement additional antenna elements to support these combinations may carry cost and RF architecture complexity impacts in terms of additional components and volume in the form factor.

## Slide 6: Proposals
Considering that 3GPP has already specified the Tx Switching suite of features (with components and enhancements adopted in Rel-16 through Rel-18), it is useful for 3GPP to consider the application of this framework to the listed scenarios.
Proposal 1: An enhancement of the 3GPP specification is needed to enable LB+LB carrier aggregation based on switching.
Recognizing that this work item has impact on the RAN1 working group, the proposed objectives strive to minimize the impact on the physical layer procedures and are intended to implement the minimum useful functionality, from the operators’ perspective. Additionally, the operators have prioritized the suggested effort on the proposed band combination with one example band combination (CA_n5A-n29A) to be completed as part of the proposed work item and the remaining combinations to be handled via the band combination basket work item approach.
Proposal 2: The proposed objectives are provided in RP-242478 and are intended for approval.