## Slide 1
3GPP TSG RAN #106 RP-242627
Madrid, Spain, December 9-12, 2024
Agenda Item: 15.2
Source: vivo, CMCC, KT Corp., Spreadtrum, Viasat, Inmarsat, Verizon, NTT DOCOMO
Title: Support of voice call over GEO satellite based on NB-IOT in 5G-A Rel-20
Document for: Discussion & Decision

## Slide 2
Voice over GEO satellite based on NB-IOT(RAN2 led, WI)
Motivation:
    Satellite direct communication as a complement to terrestrial network coverage, provides communication service to everyone, everywhere, at anytime, bringing new values and opportunities to various market segments including IoT and smartphones.
    GEO satellite has its advantage to provide global coverage for low data rate services. Using of existing GEO satellites can enable rapid deployment to provide SMS and voice services. This feature is necessary for operators to increase their productivity and usage of GEO satellite.
    There are smartphone products in market supporting GEO satellite direct communication for SMS and low rate voice call for emergency services. Although the market acceptance of such products has been good, they are based on proprietary solutions which are not preferred from cost perspective and cannot provide consistent user performance.
    3GPP has been working on IoT-NTN since Rel-17 targeting direct communication over satellites. However, it was designed for IoT device/services thus the current solution cannot enable voice call over GEO satellites.
    In SA1#108 meeting, a new WID (S1-244772) on Satellite access has been agreed. One of Objectives is using the consolidated requirements(i.e., data rate and call setup time) captured in TR 22.887 as baseline to support IMS voice call using GEO satellite access.

## Slide 3
Voice over GEO satellite based on NB-IOT(RAN2 led, WI)
NB-IoT and GEO satellite are assumed due to the consideration of available satellite resource and coverage
Consider the following objectives as starting point:
    Enhancement 1: Support of dedicated RB for GBR IMS voice call for NB-IoT (RAN2)
      In NB-IoT, only Non-GBR service is supported. Guaranteed bit rate is required to support an reliable IMS voice quality.
      Support of voice service includes radio bearer configuration, establishment.
    Enhancement 2: Protocol overhead reduction for voice packets (RAN2)
      Due to coverage limitation, only low rate codec is considered for GEO scenario, as pointed in SA1 TR.
      ROHC (Robust Header Compression) can be used to reduce or optimize protocol overhead for IMS voice packets.
      Consider additional protocol overhead reduction if feasible and beneficial.
    Enhancement 3：Support of semi-persistent scheduling for NB-IoT in DL and UL (RAN2/RAN1)
      Voice packets are periodic, semi-persistent scheduling (SPS) is more preferable to reduce the scheduling overhead and delay. However, it is currently not supported for NB-IoT data transmission.
    Potential enhancement 4 (pending on RAN4 Rel-19 progress)：High power UEs for NB-IoT based IoT-NTN (RAN4)
      High power class is generally needed to achieve the coverage target for GEO satellite. However, up to 26dBm UE power class is supported for NB-IoT based IoT-NTN in Rel-19. Support of >26dBm power class is dependent on further RAN4 progress in Rel-19.
      Support of >26dBm UE power class for NB-IoT based IoT-NTN for handheld devices (if not available in Rel-19)