## Slide 1: On LR and MR operating in different bands in release 19
3GPP TSG RAN Meeting #106 RP-242656
Madrid, Spain, 9-12 December 2024
Source: Vodafone, Vivo,
Huawei, HiSilicon
Agenda Item: 9.3.1.4

## Slide 2: Problem statement and current status – RAN2
RAN1 has sent an LS in R1-2407559 asking for impact. Summary R1-2407507:
RAN2 sent a reply LS in R2-2410957:
1 Overall description In RAN1, the common understanding is that UE may not support LP-WUS reception on all the bands supported by the UE. RAN1 respectfully asks RAN2 and RAN4 to check if there is any issue and specification support needed for IDLE/INACTIVE UEs.
Answer: State of discussions in RAN WG2: During RAN WG2 discussions, many companies raised concerns that if LP-Receivers support only subset of the bands supported by the main receiver and if LP-WUS, Paging and RACH are executed in the LP-WUS bands it might lead to overload of these bands if the NW set the LP-WUS frequency as a higher priority. This will impact user performance and decrease the utilisation of higher frequency bands. In order to ensure the LP-WUS capable UEs are camping on the band LR implemented, the NW would need to offload LP capable UEs to LR band. On the other hand if the NW operator does not offload the UEs to the band LP receiver supports, only a subset of UEs would profit from LP-WUS feature. Some companies do not see that overload problem would occur as the NW implementation can control the offload of the UEs to the lower bands in dedicated way. In regards to the overload problem, RAN WG2 has not finished evaluations and would need to study the solutions more.

## Slide 3: Problem statement and current status – RAN4
RAN1 has sent an LS in R1-2407559 asking for impact. Summary R1-2407507:
RAN4 was not able to converge to the contents of the reply in RAN4#113. Several options for the reply were captured in the WF R4-2420100 (Issue 1-1-8).
However, RAN4 RRM has achieved the following agreements in RAN4#112-bis in the WF R4-2416861 (Issue 1-1-8):
1 Overall description In RAN1, the common understanding is that UE may not support LP-WUS reception on all the bands supported by the UE. RAN1 respectfully asks RAN2 and RAN4 to check if there is any issue and specification support needed for IDLE/INACTIVE UEs.
From Rel-19 RAN4 RRM requirement of MR offloading and relaxation perspective, RAN4 assumed LR and MR are operating on the same carrier frequency as baseline. FFS for the case of MR and LR working on different carrier frequencies if it is supported in RAN1/2.

## Slide 4: Scenarios (Solutions 1 and 3 can be considered as part of Solution 2)
Scenarios |  | Overload on LR band | Limited Usage of LP-WUS | Expected specification efforts
Intra-Frequency | Solution 1: MR is prioritized (via SIBs) to camp on the same band as LR (System information, Paging, RACH on LR band) | Yes | No | Mainly in RAN2 since same carrier frequency is assumed in RAN4 as baseline. Frequency priority configured for LP-WUS capable UE in SIB
 | Solution 2: MR is prioritized to camp on the same band as LR (System information, Paging on LR band; and RACH on another MR band based on reselection criteria) | No | No | Mainly in RAN2 since same carrier frequency is assumed in RAN4 as baseline Frequency priority configured for LP-WUS capable UE in SIB or dedicated signalling. UE needs to perform cell reselection following the legacy frequency priority after waking up.
 | Solution 3: MR is not prioritized to camp on the same band as LR but can be redirected via dedicated signalling depending on LR band load (up to gNB implementation) | Highly dependent on the awareness of load in LR band by the gNB | Dependent on LR band load | Mainly in RAN2 since same carrier frequency is assumed in RAN4 as baseline Frequency priority configured for LP-WUS capable UE in dedicated signalling.
 | No solution- MR is not prioritized to camp on the same band as LR (i.e. the UE would only use LP-WUS whenever it was already camped on LR band) | Dependent on LR band load | Yes | No specification impact is expected but very limited usage of LP-WUS procedures
Inter-Frequency | Solution: 4- MR (SI/Paging/RACH) is camped on a different band than LR. LR can wake up MR on the band it is camped on | No | FFS | LP-WUS - Paging offset design in RAN1/RAN2. Entry/exit conditions in RAN2/RAN4. Validity of measurements in RAN4 as LR and MR are operating in different frequencies. Note: Might be applicable for co-located case only. Non co-located case is FFS.

## Slide 5: Way forward
RAN Plenary should provide guidance to the working groups on how to proceed on this issue.
Proposal RAN Plenary to task RAN WGs RAN1, RAN2 and RAN4 to continue discussion to address the operator concerns associated to the UE may not supporting LP-WUS reception on all the bands supported by the MR (e.g. overload and/or limited usage of LP-WUS) It is proposed to focus on solution 2 and 4 and downselect one of them. RAN Plenary Checkpoint in RAN#107 for final decisions on normative in Rel-19. Note: Solutions 1 and 3 can be considered as part of solution 2.

## Slide 6: Thank you