## Slide 1
Mobility Enhancements for Rel-20
Apple
  3GPP TSG RAN #106
  Madrid, Spain, December 9 - 12, 2024
  Source: Apple
  Agenda Item: 15.2
  RP-242792

## Slide 2
Background
Mobility has been integral part of NR features
  Since the first, every release has a WI for improving some aspect of mobility
    Rel-15: Basic mobility (as in LTE) including INACTIVE state. Addition of beam management.
    Rel-16: CHO, intra-SN mobility - towards mobility robustness, DAPS - towards “0”ms interruption time.
    Rel-17: SCG Deactivation, inter-SN mobility enhancements. RACH-less for some features
    Rel-18: Intra-CU LTM, further SN mobility enhancements (for eg CHO+SN), RACH-less for more features
    Rel-19: Inter-CU LTM, conditional intra-CU LTM

## Slide 3
Some Observations…
RAN views that robustness in mobility and reducing latency are important topics
  Every release added some optimizations/procedures to address/optimize the above!
However, adoption of these features paints a slightly different story
  In terms of deployment, there is little to none for any of the Rel-16/Rel-17/Rel-18 features
    Rel-16 CHO and some other aspects are now being considered in some part of the world
    DC aspects (for eg SN mobility improvements) through the earlier releases have no adoption interest!
  Nevertheless, LTM brought renewed interest from operators
    Reduction in latency, effective spectrum usage, improved KPIs/call performance etc – among other reasons
    Rel-19 LTM additions expand the usable scope of LTM
      Inter-CU (expands the deployable options)
      Conditional LTM (increases robustness)

## Slide 4
Release-20 guiding principles for Mobility
Release 20 would likely be the last (if not significant) NR-A release
  For mobility, we should focus on aspects that “appeal” more in terms of commercial deployment, while ensuring that latency/robustness is addressed.
  With 6G study as part of the WG workload, it is “OK” to narrow the scope of mobility objectives – to only those that add to the usefulness in terms of practical deployment.
Focus on LTM
  Lower layer mobility with LTM is the main mobility feature that fits the bill.
  It would be important to “selectively” choose improvements on the LTM feature

## Slide 5
Dissecting Rel-19/18 LTM
Dissecting Rel-18/19 LTM :
  LTM was introduced in Rel-18, but was quite narrow in scope in terms deployability (limited to a CU)
    Still brings reductions in latency with L2/L1 level signaling and neighbor beam handling
  Inter-CU from Rel-19 closes the loop on the using wide-spread L2 mobility practically, expanding to CU-CU mobility.
    Additional enhancements in mobility robustness (with conditional LTM) and latency reduction (early CSI acquisition etc.,)
    However, there are still some aspects of inter-CU LTM that are not part of Rel-19
    Inter-CU LTM in both MCG and SCG
    Conditional LTM is limited to intra-CU alone.
What needs to be enhanced:
  Expanding “robustness” aspect across CUs
    Rel-16 CHO addressed mobility robustness, but had adaption issue with one of the reasons being NW inter-CU effort
      Inter-CU LTM already lays the framework for this pre-requisite inter-CU framework
      Closes the loop on specifying C-LTM for all types of deployment (intra and inter-CU)
  Security of L2 signaling
    Currently LTM uses unsecure MAC CE
    SA3 has/continues to have discussion on L2 security in Rel-19. But with limited time left, Rel-19 is not envisioned to have any enhancements to address this.

## Slide 6
Release-20 Mobility Enhancements - Proposal
Based on the guiding principle we mentioned earlier, we propose the following LTM improvements:
  A R20 WI on further LTM enhancements as part of Mobility Enhancements:
    Specify Conditional LTM for inter-CU.
    Specify procedures and signaling to make LTM L2 signaling secure, in colloboration with SA3.
    NOTE: Do not automatically add aspects that were not possible in Rel-19 LTM.
      For eg: We do not see the need to handle inter-CU LTM in both MCG and SCG at the same time.