## Slide 1: Consideration on AI/ML topics in 5G-A Rel-20
Agenda item: 15.2
Source: CATT
3GPP TSG RAN Meeting #106 RP-243124
Madrid, Spain, 9th -12th December, 2024

## Slide 2
AI/ML in air interface
AI/ML for mobility
AI for NG-RAN
Summary

## Slide 3: AI/ML in air interface

## Slide 4: AI/ML in air interface
General view: AI/ML is ‘add-on optimization’ for 5G-A. 1~2 use cases with the clear benefit/interest can be moved forward.
Motivation
  Continuation of Rel-18&19 study in 5G-A
  Improve CSI compression performance better than ever
  Warm-up of supporting two-sided model use case in 6G
Main objectives
  Specification support of LCM for CSI compression
  Data collection
    Support high resolution data collection at NW
  Training
    Prioritize NW-first training without offline collaboration
    Prefer Option 3a-1/3b and Option 4-1
  Inference and CSI report
  Performance monitoring
    At least support NW-side monitoring to monitor end-to-end performance
Use case 1: CSI compression
UE
AI/ML encoder
gNB
AI/ML decoder
CSI feedback
Inference, monitoring…
Training collaboration
UE-side server
NW-side
  *Note: Support of this use case depends on the final outcome of Rel-19 study.

## Slide 5: AI/ML in air interface
General view: AI/ML is ‘add-on optimization’ for 5G-A. 1~2 use cases with the clear benefit/interest can be moved forward.
  Motivation
Evolution of Rel-19 AI/ML based beam management
Further improve NW energy/resource saving
Further reduce UE measurement complexity and latency
  Main objectives
  Support LCM for inter-frequency/cell DL Tx beam prediction
  Focus on inter-frequency CA case, with Set B beams in FR1 and Set A beams in FR2
  Support prediction in spatial domain, and/or time domain
  Support both UE-side and NW-side model
  *Note1: Support of this use case depends on the TU availability.
  *Note2: A study phase may be considered to identify the gain and additional specification impact based on Rel-19 AI/ML-based BM.
Use case 2: Inter-frequency/cell beam management
UE
gNB
FR2
FR1
No. | Evaluation scenario combination | Measure | Predict
1 | FR1 to FR1 intra-frequency temporal domain case A | FR1 | FR1
2 | FR1 to FR1 intra-frequency temporal domain case B | FR1 | FR1
3 | FR1 to FR1 inter-frequency frequency domain | FR1 | FR1
4 | FR2 to FR2 intra-frequency temporal domain case A | FR2 | FR2
5 | FR2 to FR2 intra-frequency temporal domain case B | FR2 | FR2
6 | FR2 to FR2 intra-frequency spatial domain | FR2 | FR2
Current RAN2 use cases focus on prediction in the same FR

## Slide 6: AI/ML for mobility

## Slide 7: AI/ML for mobility
Use cases:
  RRM measurement prediction
    For scenarios, 3 out of the 6 scenarios were agreed as high priority:
      Case 2: FR1 to FR1 intra-frequency temporal domain case B
      Case 3: FR1 to FR1 inter-frequency frequency domain
      Case 4: FR2 to FR2 intra-frequency temporal domain case A
    Baseline simulation assumption has been agreed including the following aspects: channel model, UE trajectory, UE speed, RRC parameters .etc.
    Simulation results from companies shows that the RSRP difference between AI and non-AI are acceptable.
  Measurement event prediction
    Baseline simulation assumption has been agreed
    Simulation results from Feb. 2025
  RLF/HO failure prediction
    RLF prediction
      Baseline simulation assumption has been agreed
      Simulation results from Apr. 2025?
    HOF prediction
      Down prioritized, no subsequent simulations/evaluations
      Generalization study:
    Reuse the evaluation methodology in TR38.843
    Simulation assumptions under Email discussion
Rel-19 SI Progress
General view: AI/ML for mobility in NR is moved to WI in R20.

## Slide 8: AI/ML for mobility
Study other potential use cases (e.g. LTM):
  Simulation assumption of RRM measurement prediction is reused: Simulation result:
General view: AI/ML for mobility in NR is moved to WI in R20.
Rel-20 New use case
Observation: The RSRP difference is acceptable for LTM beam level prediction.
Simulation parameters |  | CATT
Simulation assumptions | UE trajectory option | Option 1 in TR38.843 section 6.3.1
 | UE trajectory boundary processing option | Circle-bouncing model
 | UE speed (Km/h) | 90
 | spatial consistency option | Procedure A in TR38.901
 | Number of TX beams | 32
 | Number of RX beams | 4
 | Observation window | 240ms
 | Prediction window | 80ms
AI/ML model input/output | Model input | L1 Beam level RSRP of all cells
 | Model output | L1 Beam level RSRP of all cells
AI/ML model description | Model type | LSTM

## Slide 9: AI/ML for mobility
Motivation:
  The application of AI/ML techniques to NR mobility has been studied in FS_NR_AIML_Mob
  Use cases studied in R19 could provide good gains. E.g. Regarding RRM measurement prediction:
    For FR1 to FR1 temporal domain prediction with goal of reducing measurement overhead, HO performance of AI predication does not deteriorate obviously
    For FR2 to FR2 temporal domain prediction with goal of enhancing HO performance, AI predication in advance could achieve high prediction accuracy
    For FR1 to FR1 frequency domain prediction with goal of reducing measurement overhead, AI predication could achieve high prediction accuracy
  At least RRM measurement prediction use case can proceed into normative work
  Objectives:
  Provide specification support for RRM measurement prediction [/ Measurement event prediction/ RLF prediction] [RAN2, RAN3, RAN4]
    Signaling and protocol aspects (Uu, Xn) of data collection for training/inference/monitoring
    Mobility related applicability interaction and training/inference/monitoring configuration
    Maximum reuse the LCM raised in AI/ML for NR Air Interface, the impact of generalization can be considered
  [Study objective for LTM prediction] [RAN2, RAN4]
    Use part of sub use case 1 (to predict beam level results) as a starting point
    Mainly based on theoretical analysis with limited simulation work
  [R19 leftover] [RAN2, RAN4]
    Simulation of RLF prediction
General view: AI/ML for mobility in NR is moved to WI in R20.
Rel-20 WID

## Slide 10: AI for NG-RAN

## Slide 11: AI for NG-RAN
Motivation:
  To support optimized NG-based handover with AI/ML means which has already been supported for Xn-based handover
  To support mitigating handover to a “wrong” target node and predicting UE trajectory beyond one target node
  To support AI/ML-based LTM
Objective:
  Signalling design to support AI/ML-based NG handover
  Signalling design to support multi-hop UE trajectory collection after given handover
  Signalling design to provide “feedback” information to the gNB-DU
Mobility Optimization
General view: Mobility optimization, energy saving and QoE can be considered to be studied and specified in R20.

## Slide 12: AI for NG-RAN
Motivation:
  Maximise UE’s QoE by AI/ML means and RAN’s experience
Objective:
  Signalling design for AI/ML based QoE optimization in RAN side
Motivation:
  Optimizing NES features with AI/ML for better performance
Objective:
  Finer granularity of Energy Cost
  Using AI/ML means to optimize beam-level ES
Energy Saving
QoE
General view: Mobility optimization, energy saving and QoE can be considered to be studied and specified in R20.

## Slide 13: Summary

## Slide 14: Summary
  AI/ML in air interface：
  Proposal 1: For AI/ML in air interface in 5G-A Rel-20, ‘very surprising new use case’ with huge study effort should be avoided.
  Proposal 2: For 5G-A Rel-20, the following use cases are considered to be specified for AI/ML in air interface :
CSI compression, contingent on the final outcome of Rel-19 study;
Inter-frequency/cell beam management, contingent on the TU availability.
  AI/ML for mobility：
  Proposal 3: Suggest to have a Normative work of AI/ML for mobility in R20:
  At least the use case of RRM measurement prediction can be specified;
  May consider LTM prediction as a study phase, which mainly based on theoretical analysis with limited simulation work.
  AI for NG-RAN：
  Proposal 4: For 5G-A Rel-20, the following aspects are considered to be studied and specified in AI/ML for NG-RAN:
  Enhancement on mobility, including AI-based NG handover, multi-hop UE trajectory prediction and feedback, and AI-based LTM;
  Enhancement on Network Energy Saving (NES), including finer granularity of EC and beam-level NES;
  AI-based QoE optimisation.