## Slide 1: Viasat-Inmarsat Release 20 priorities 5GAdvanced Workshop
Viasat, Inmarsat, Ligado Networks, Thuraya
Omnispace, Terrestar Solutions Inc.
3GPP TSG RAN #106
December 9-12th, 2024, Madrid, Spain
Agenda: 15.1
TDOC: RP-243188
For: discussion

## Slide 2: IMS Voice over GEO in IoT-NTN
Justification
  Messaging and Emergency services (NB-IoT) over GEO is already here today and operational
  FR1 GEO satellites are already operational
  There are lots of “holes” in terrestrial coverage, areas that have limited or no coverage from the TN networks that can be filled by NTN coverage
Business Need
  The business need is for a seamless calling experience for the end user.
    The end user needs to use his/her phone like usual
Areas that need to be investigated/improved
  Low rate codecs, maybe latency adaptive codecs
  QoS that will allow good quality voice calling
  Service continuity between TN and NTN networks
  Mobility between TN and NTN networks
  Call Setup (SIP signaling improvement)
  Paging

## Slide 3: Position free UE IoT-NTN and NR-NTN
Justification
  GNSS receiver is sometimes the weak link in a IoT-NTN system
  Some IoT NTN devices may not be smartphones with GNSS receivers
  Security considerations may prevent the smartphone from using GNSS
  GNSS signals are known to be spoofed/tricked
Areas that need to be investigated/improved
  Define UE positioning method for Idle and Connected modes
  PRACH enhancements
  Frequency Corrections
  Timing correction and Doppler issues
  Enhancements to closed loop timing and frequency corrections
  Other considerations

## Slide 4: RAN full support for IoT services and deployment
Justification
  As defined in Rel 17, an MSS operator with both NB and NR service offerings
    needs to have an ePC AND 5GC
    Needs to have an eNB (for the NB-IoT/eMTC) and gNB (for NR)
  This duplication is expensive, and for satellites with thousands of spotbeams very operationally inefficient
  Limited MSS spectrum will need to be bifurcated – leading to more inefficiency
Areas to be addressed
  NB-IoT and eMTC shall be fully incorporated into the gNB and RAN such that the NB-IoT channel scan either be in band or guard band and eMTC channels can be incorporated in band as part of the 5G NR channel.
  NB-IoT and eMTC shall be supported by the 5GC

## Slide 5: MIMO for NR-NTN
Justification
  Optimal precoding matrices for NTN
    Current MIMO codebooks in 3GPP assume rectangular arrays
    Satellite arrays are may not be rectangular
    Codebooks for different geometry need to be investigated
  Some NR-NTN devices may be bigger than a smartphone (non-smartphone use case)
    Thus allowing multiple antennas over a bigger area
  The Land Mobile Satellite (LMS) channel needs to be investigated for multipath and potential MIMO use
  Multi satellite systems
Areas that need to be investigated/improved
  CSI-RS based training
  LMS channel and its use with multipath
  Optimal precoding matrices for satellites
  Multi satellite MIMO
Impacted areas
  RAN 1,2, possibly other areas

## Slide 6: Thank You!