## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Seonggu Shim
Status Report for RAN WG3
3GPP TSG RAN #107, Incheon, Korea
Mar 12th – 14th, 2025
RP-250007

## Slide 2: Executive Summary
Total 692 Tdocs at submission deadline (excluding LSin received from other groups) in Q1
  12% LSs and related documents
  16% Maintenance: Rel-18 & earlier
  72% Documents to Rel-19 WIs
Updated endorsed guidelines for f2f meeting with 1-way remote access: R3-250003
TR30.531 Work Plan and Working Procedures - RAN WG3 was updated and approved in R3-250756
RAN3#127 | Feb 17th – 21st, 2025 Athens, GRC
RAN #107 | Mar 12th – 14th, 2025 Incheon, KR

## Slide 3: Tdoc submitted to RAN3
In R19, the total number of contributions around 640 (less than R18) for each RAN3 meeting seems reasonable, quota rule works well.
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: Overview of RAN3-led Rel-19 NR SI/WIs
UID | Name (acronym) | Acronym | Target completion | Old % (the same as in WI/SI SR) | WID | New % | Change or comments
1021092 | Data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) Phase 4 WI | NR_ENDC_SON_MDT_Ph4-Core | 25/09/2025 | 50% | WID: RP-234038 | 60% | LS to RAN2 on SON for Network Slicing in R3-250914
1050124 | New WID: Enhancements for Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN | NR_AIML_NGRAN_enh-Core | 25/09/2025 | 30% | WID: RP-242385 | 50% | LS to SA5 on Continuous MDT in R3-250891
1051125 | New WID on additional topological enhancements for NR | NR_WAB_5GFemto-Core | 25/09/2025 | 30% | WID: RP-243009 | 60% Note: WAB 50%, Femto 70% | LS to SA2 on Additional ULI for UEs served by WAB-nodes in R3-250901 Reply LS to SA2 on Support of Location Service Involving WAB-Nodes in R3-250902 LS on security verification related to NR Femtos to SA3 in R3-250822
1020083 | Study on enhancements for Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN SI | FS_NR_AIML_NGRAN_enh | 25/09/2024 | 80% | WID: RP-240323 | 100% | 
1020082 | Study on additional topological enhancements for NR SI | FS_NR_WAB_5GFemto | 25/09/2024 | 70% | WID: RP-240319 | 100% | 
WI: Black SI: Blue
Completed WI/SI: Red

## Slide 6: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-250008, which includes:
  30 CRs were agreed in Q1.
    2 Rel-16: 2 Cat.F CRs
    7 Rel-17: 5 Cat.F CRs, 2 Cat.A CRs
    21 Rel-18: 14 Cat.F CRs, 7 Cat.A CRs
      0 Non-Backwards-Compatible (NBC) CRs
        (Here is how 3GPP works with NBC changes)
    0 TEIxx Cat.B/F CRs with TEI identifier
  4 endorsed draftCRs to RAN2 specs.

## Slide 7: Experience for GTW Usage in f2f meeting
RAN3 has 1 main meeting room and 1 breakout room in RAN3#127 (1-way remote access).
In general, the number of remote participants for main session is quite limited, less than 8. The audio device test for remote access was performed before daily session starts.
MCC and IT support during the meeting are sufficient.

## Slide 8: R19 SON/MDT WI
Progress in the last quarter
MRO for LTM:
For UHI and ping-pong avoidance:
    CU can adjust the candidate Cell list for LTM based on UHI.
    DU should be able to resolve LTM ping-pong based on information over F1.
Network based or UE based solution for LTM candidate cell list?
  Network based solution is used for LTM candidate cell list.
MRO for CHO with Candidate SCG(s):
    In case of too late CHO execution, reusing Handover Report message from the last serving MN to the relevant candidate MN.
    New message is defined for the serving MN to forward the SCGFailureInformation to the respective MN which should perform the optimization.
MRO for S-CPAC:
The forwarding mechanism in BLCR for TS37.340 need to be refined.
New stage-2 definition referring to CHO with candidate SCG is needed. Detail under checking.
MRO for Intra-NTN:
For Time based CHO:
    Existing timers can be reused to identify when RLF happens with 100ms accuracy.
    No need to identify whether RLF happens before or after T1 for time-based CHO.
For Location based CHO:
  Revert the WA: There is no need to report any other info in the RLF report for the location based CHO.
  For earth moving case, the accuracy and complexity issue of the network-based solution is acknowledged.

## Slide 9: R19 SON/MDT WI
Progress in the last quarter
Slice-based Cell Reselection Enhancement:
  The UE is unable to find suitable cell in the frequency corresponding to the prioritized NSAG, UE falls back to legacy Cell reselection procedure.
MHI Enhancement for SCG Deactivation/Activation:
Wait for RAN2 progress on whether to use absolute time or relative time to express SCG activated time.
Impacts and dependencies on other WGs
LS to RAN2 on the Slice-based Cell Reselection.
Other important info
N/A

## Slide 10: R19 AI RAN WI
Progress in the last quarter
Network Slicing
Introduce Slice Measurement Initiation Result IE to indicate the predicted radio resource status per slice or predicted slice available capacity cannot be initiated.
UE performance per S-NSSAI defined in SA5 can be referred in RAN3 which can be used as the feedback.
Coverage and Capacity Optimization
Add Future Coverage Modification Notification List IE and Future Coverage Modification Cause IE properly in F1AP.
Value 0 for Future Cell Coverage State IE is needed for inactive cell.
Continuous MDT Collection:
RAN3 assumes a solution for continuous MDT should minimise impacts on the current Management Based MDT framework. And send the LS to SA5 for seeking the guidance on possible solutions for Continuous MDT collection.
Split Architecture:
Packet delay measured for UE Performance feedback is sent from CU-UP (the delay in DU side is aggregated in the CU-UP) to the CU-CP in the case of CP-UP split architecture.
Packet delay measured for UE Performance feedback is sent from DU to CU via DDDS in the case of CU-DU split architecture.
Impacts and dependencies on other WGs
LS to SA5 on possible solutions for Continuous MDT collection.
Other important info
N/A

## Slide 11: R19 additional topological enhancement WI
Progress in the last quarter
WAB:
Include Additional ULI into the User Location Information IE in TS 38.413. Additional ULI contains a CGI and a TAI. In case of WAB-MT connects via NTN, the Additional ULI is determined based on WAB-node geo-location. The latter applies to intra PLMN and inter PLMN cases.
Support and capture the two-logical-gNB solution for UE’s AMF change in 38.401.
Capture in Stage 2 that, in case IPsec tunnel mode is used to protect WAB-gNB’s traffic, MobIKE can be used to avoid the change of inner IP address.
For WAB deployments, the legacy mechanism can be reused for PCI collision avoidance. PCI space can be partitioned by allocating a range of PCIs to WAB cells.
Update the definition of mobile TRP in TS 38.305 to capture the case when the TRP belongs to a WAB-node. Capture in TS38.305 the WAB-MT UE ID as part of assistance data
RAN3 to introduce in TS38.455 a new IE to indicate the UE ID of the WAB-MT in the TRP Information IE.
Capture in TS38.401 that NG connection(s) removal for a WAB-gNB is supported.
NR Femto:
Considering that NAT is an IP router functionality, and that IP routers are part of the transport network, NAT does not need to be mentioned in the stage 2 description of the NR Femto GW.
To avoid routing ambiguities, a TAI used in a NR Femto GW shall not be reused in another NR Femto GW.
Reuse the Global gNB ID to identify the NR femto node.
Send an LS(R3-250822) to SA3 to check verification aspects with respect to NR Femto GW architecture.
Impacts and dependencies on other WGs
Expect reply LS from SA3 on NR Femto.
Reply LS is sent to SA2 on Support of Location Service Involving WAB-Nodes.
LS is sent to SA2 on Additional ULI for UEs served by WAB-nodes.

## Slide 12: R19 Mobility Enh WI
Progress in the last quarter
For the network Semi-Persistent CSI-RS coordination, source gNB-DU/source gNB triggers the activation/deactivation of the CSI-RS transmission in the candidate cell.For the activation/deactivation procedure, a class 1 procedure is needed from the source gNB-DU/source gNB. FFS for reusing existing one or a new one.
The candidate gNB-CU responds the full SSB Time/Frequency Configuration (in SSB Information IE) of candidate cells to the source gNB-CU in the Handover Request ACK message.
The source gNB-CU sends the pair of (gNB ID, new ID of early RACH configuration resource (to be further discussed)) to the candidate gNB-CU to request early RACH configuration.
WA: Introduce a new non-UE associated class 2 procedure on Xn, namely TA information Transfer message, to transfer the TA information from the candidate gNB-CU to the source gNB-CU.
RAN3 agree the following scenarios to support LTM with NR-DC:
  1.SN initiated inter-CU SCG LTM without MCG changes (high priority)
  2.Inter-CU MCG LTM without SN release
  3.Inter-CU MCG LTM with SN release
  4.Inter-CU MCG LTM with SN addition
The CU decides to configure C-LTM.
The CU determines which type of C-LTM to initiate: L1 event-triggered C-LTM or L3 event-triggered C-LTM.
Reuse the current LTM preparation procedure (i.e. UE Context Setup/Modification procedure) for DU to generate the C-LTM L1 execution condition.
Impacts and dependencies on other WGs
N/A

## Slide 13: R19 NR NTN WI
Progress in the last quarter
MBS broadcast service:
  Encode the Intended MBS service area as OCT STRING which refers to RAN2 spec.
Regenerative payload:
  Clarify the concerns mentioned in the incoming LS without any change on RAN3 previous agreements.
Impacts and dependencies on other WGs
  Reply LS to SA2 and SA5 on OAM requirements to support regenerative payload transport links.
Other important info
  N/A

## Slide 14: R19 IoT NTN WI
Progress in the last quarter
  Introduce stage 2 description of Store and Forward operation.
    Introduce stage 2 description of full eNB as regenerative payload.
    Introduce the S1 Removal procedure.
Impacts and dependencies on other WGs
  N/A
Other important info
  N/A

## Slide 15: R19 Ambient IoT WI
Progress in the last quarter
RAN3 agrees to support both the direct and indirect options for the A-IoT RAN node to communicate with AIoTF in Topology 1.
WA: Take Option1 (Including AIoTF information in NGAP).
WA: The AIoT RAN node may only provide the AIoT radio.
AIoTF obtain the AIoT RAN information via OAM configuration. The AIoT RAN information includes supported AIoT area, served reader ID list.
AIoT RAN node receives the requested service area information (encoded as area and/or reader ID list) from AIoT CN.
The location of reader is FFS.
FFS on whether signaling is needed, further discussion on the detail information and necessity.
The A-IoT RAN node always sends the AIoT device’s location at reader ID granularity to the AIoTF in Inventory Report.
AIoT RAN node sends the Inventory Report aggregated per Reader.
“Global gNB ID + Reader index” is used to uniquely identify the Reader globally.
FFS whether only Reader index or “Global gNB ID + Reader index” is sent in Inventory Report.
Impacts and dependencies on other WGs
LS R3-250905 is sent to SA2 and SA5, RAN3 would like to inform SA2 and SA5 about the RAN3 progress related to Architecture and OAM aspects.
Other important info
N/A

## Slide 16
Progress in the last quarter
  On-demand SIB1 for UEs:
  It is agreed that after Cell A gNB has received and accepted the UL WUS Configuration request from the NES Cell gNB, it broadcasts in SIBx at the first opportunity.
  It is agreed from the signalling point of view, in UL WUS Configuration Provision Request (naming to be further discussed) from NES Cell gNB to Cell A gNB, one option is “start with UL WUS Configuration”. This codepoint/choice is used to trigger Cell A to broadcast UL WUS configuration in SIBx.
  It is agreed that NES Cell gNB can “stop” (naming to be further discussed) Cell A to broadcast UL WUS configuration.
  Others:
  There is no consensus in RAN3 on the usage of this energy saving indication in this meeting, making the decision in next meeting and provide reply LS to SA2.
Impacts and dependencies on other WGs
  N/A
Other important info
  N/A
R19 Network ES WI

## Slide 17
Progress in the last quarter
R3-250841/R3-250913/R3-250838/R3-250839 were endorsed as BL CRs for support of R19 LP-WUS.
R3-250840(TP to TS 38.413 on support of LP-WUS) was agreed, and to be merged into R3-250930 as BL CR.
Impacts and dependencies on other WGs
For the following issues, including Extended UE Identity Index, the maximum value of CN subgroup ID, Emergency call back, the terminology of ”LP-WUS”, the LP-WUS node capability need more inputs from other WGs.
Other important info
N/A
R19 LP-WUS WI

## Slide 18: R19 Duplex WI
Progress in the last quarter
SBFD time and frequency configuration in Served Cell Information IE is agreed to be exchanged in F1 and Xn interface via a container.
For exchange of SSB info over Xn, nothing to be done, already supported in RAN3 spec.
For exchange of strongest DL beam information over Xn, SSB info is defined as SSB-Index INTEGER (0..63), NZP CSI-RS info is defined as NZP CSI-RS Resource Indicator INTEGER (1..64).
To define CLI-mitigation request as an optional IE.
Impacts and dependencies on other WGs
LS to RAN2 to design the detailed IE for SBFD time and frequency configuration.
Other important info
N/A

## Slide 19: R19 AI PHY WI
Progress in the last quarter
The LMF starts a NRPPa transaction. The gNB determines that data collection is needed.
For case 3a, it should be possible to collect data in both an “opportunistic” (gNB collects available data from ongoing positioning sessions) and “proactive” (gNB triggers data collection at the LMF, e.g., which may trigger positioning) manner.
For case 3a, it should be possible for the gNB to collect data for both served and non-served UEs.
WA: For case 3a data collection, Part A is known internally by the gNB and is not necessarily signalled outside the gNB.
Impacts and dependencies on other WGs
The details of the related measurements are still pending and subject to further discussion in RAN1.
Reply the LS to SA2 on AI/ML assisted positioning (case 3b) on Editor note’s issue.
Other important info
N/A

## Slide 20: R19 SL Relay WI
Progress in the last quarter
RAN3 agrees to support the Multi-hop relay in CU-DU split architecture.
RAN3 can work on the new signaling flow for multi-hop relay for the purpose of Initial Access procedure based on the existing procedures in TS 38.401.
The existing F1AP UE Context Setup and UE Context Modification procedure can be used as a baseline to establish the PC5/Uu Relay RLC channel(s) for relaying of Remote UE’s SRB/DRB.
For the initial UL RRC transfer message, the gNB-DU informs the gNB-CU of the multi-hop relay related information including at least gNB-DU UE F1AP ID of the Last Relay UE and Remote UE Local ID.
R3-250226/R3-250526/R3-250256 about authorization for multi-hop relay were agreed. R3-250878 about multi-hop remote UE initial access procedure was agreed.
Impacts and dependencies on other WGs
Whether intermediate relay in RRC_IDLE/INACTIVE is supported or not and multi-hop path switch configuration may depend on RAN2 progress.
Other important info
N/A

## Slide 21: TEI Corrections
Progress in the last quarter
Multiple Xn Setup
  The handling of duplicated Xn Setup procedures towards the same Xn-C interface instance is not covered by current specs, and is left to implementation, there is no consensus on how to standardize this in 5G.
X2/Xn exchange of signalling TNL addresses for signalling transport establishment
  The group confirms that there is an issue as there is no unambiguous IE/Information the target node could take to return the correct TNL address.
L3 measurements based LTM over F1
  RAN3 analyzed and compared all the solutions on the table on L3 measurements based LTM over F1, no consensus achieved for split gNB architecture, LS in R3-250879 to inform other WGs (RAN2, cc RAN4, RAN) that F1 support for L3 measurement based LTM will not be specified in Release 18.
AI/ML for NG-RAN
  Clarify the description of predicted UE trajectory over Handover Request Message.
  Clarify the signalling of Data Collection Update message.
Positioning
  Stage 3 correction for clarification on Positioning Assistance Information Control Procedure.

## Slide 22: TEI Corrections
Progress in the last quarter
SON/MDT
  Clarification on the description of the UE History Information.
  Stage 3 correction on propagation for MDT Configuration.
  Stage 2 and Stage 3 correction on DL LBT Failure Information.
IAB
  Stage 2 correction to 38.423 on (non-)F1-Terminating IAB-donor UE XnAP ID in IAB procedures.
UAV
  Discuss UAV related information(e.g. altitude) reporting from RAN to CN based on SA2 progress and provide feedback LS to SA2.
XR
  Discuss XR UL bit rate control and available data rate based on input information from other WGs and provide reply LSs.
Per-Packet QoS monitoring
  To be discussed in future release based on the per-packet delay monitoring requirement confirmed and to be discussed with a proper WI framework.

## Slide 23: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and organizing social events during the meetings!
  Thanks Athanasios, Anna’s kind help to find the nice local restraurant for RAN3 social event!
  Thanks Jiajun’s great efforts to organize the basketball match with RAN2！
Seonggu (RAN WG3 Secretary)
  For impressive hard work and continous support!
Sean, Jiren, Lixiang, Julien, Damiano...
  For moderating some tough email discussions and good support!
All Rapporteurs and moderators
  For their efforts to rapporteur updates and TEI corrections!
All RAN3 delegates
  For their positive, constructive and cooperative spirit and hard work!

## Slide 24: RAN3 Social Events in Athens
During the social event, we also celebrated our vice chair Gen’s birthday, thanks Seonggu bought the nice cake!
Notes: w

## Slide 25: RAN3vsRAN2 Basketball Match
The friendly match will be held in 7th, April, 2025.
Thanks for all the Participation and Sponsorship, ZTE、Nokia、Huawei、CAICT、TTA、Lenovo、CATT! The details can be found in R3-250757.
Welcome to watch the match and enjoy the beer party after the match!
Notes: w