## Slide 1: Views on Rel-20 mobility enhancements
Agenda Item: 15.2.8.1
Source: Fujitsu
Document for: Discussion
3GPP TSG RAN Meeting #107 RP-250132 Incheon, Korea, March 12-14, 2025

## Slide 2: Background
What we have done in Rel-18 and Rel-19 for Lower-layer Triggered Mobility (LTM):
Rel-18
LTM for intra-CU
SSB-based L1-RSRP measurement
L1 measurement reporting by gNB scheduled
Defining of RRM requirement (e.g., interruption time)
Timing Advance management for candidate cells
Rel-19
LTM for inter-CU
CSI-RS-based L1-RSRP measurement
Measurement reporting by event triggered reporting
CSI acquisition for the target cell
Conditional LTM for intra-CU

## Slide 3: Challenges in Rel-20
To strive for designing better LTM operation
Interference consideration by L1-SINR measurement
  L1-RSRP only may not well reflect the channel condition for LTM determination in NW side due to severe interference, especially for inter-frequency scenario.
Robustness against channel fluctuations
  High fluctuation of L1-RSRP / L1-SINR disturbs stable LTM operation with event triggered reporting
    Especially, the filtering should be discussed if L1-SINR is adopted
  Time-to-Trigger (TTT) itself has limited performance to avoid ping-pong issue in high channel fluctuation case
  For gNB scheduled reporting, the gNB can filter by itself based on periodically reported measurement results from UE. Hence, the support of NW configurable filter for the gNB scheduled is not needed.
Optimized network architecture for inter-CU LTM
  For Rel-19 inter-CU LTM cell switch, security handling method compromised in SA3 is not completely secure, i.e., the NCC (Next hop Chaining Counter) is transmitted by MAC CE without security protection
  Inter-CU LTM w/o RRC/PDCP anchor change can avoid security key update, but not supported due to time limitation in Rel-19 at RAN3

## Slide 4: L1-SINR measurement
L1-SINR measurement provides following benefits
  More comprehensive cell selection
    Possible to provide the interference information beyond RSRP, especially in inter-frequency scenario
    Prevents cell switch to the cell with high interference causing throughput drop
  Prevent ping-pong issue
    Cell switch decision based on interference leads to reduced unnecessary cell switch
Proposal 1: Specify L1-SINR measurement in Rel-20 Mobility enhancement

## Slide 5: Network configurable filtering
For event triggered reporting, TTT mechanism alone is insufficient for handling L1-RSRP/L1-SINR variance
  Difficult to set TTT duration
    Long TTT: Temporary signal dips reset timers  delaying LTM procedure
    Short TTT: Results in frequent ping-pong issue
  UE implementation-based filtering leads to inconsistent measurement variance across UEs
Network configurable filtering can provide
  Improved cell switch performance
    Significantly reduces ping-pong issues
    Provides clearer L1-RSRP/L1-SINR trends for more accurate LTM decision
    Consistent L1-RSRP/L1-SINR variance across UEs with different implementation for filtering
  Enabling network-specific optimization for different deployment scenarios
    Network operator can adapt filtering based on specific deployment characteristic
  Efficient implementation
    Minimal UE memory impact by first order IIR filter
    Complements existing TTT mechanism
  Filtering can be performed in MAC layer
Proposal 2: Specify the network configurable filtering for handling L1-RSRP/L1-SINR variance for the event triggered reporting in Rel-20 Mobility enhancement

## Slide 6: Inter-CU LTM w/o RRC/PDCP anchor change
CU2
UE
RRC+DRB
In Rel-19 Inter-CU LTM cell switch w/o RRC/PDCP anchor change is not supported
  Because of time limitation in Rel-19 at RAN3
  Technical study was not conducted
However, this architecture will be beneficial
  Security key update is not necessary
    Unprotected NCC transmission via MAC CE [1] can be avoided
    NW burden due to path switch procedure is reduced
    Data loss due to PDCP re-establishment is reduced
From NW vendor’s point of view, implementation impact of this architecture will be small
RRC+DRB
RLC
RLC
Cell switch
RRC/PDCP anchor remains in CU1
Proposal 3: Support inter-CU LTM without RRC/PDCP anchor change in Rel-20 Mobility enhancement
Inter-CU LTM w/o RRC/PDCP anchor change
DU2
CU1
DU1
CU2
DU2
CU1
DU1
UE
[1] S3-251124, Reply LS on security handling for inter-CU LTM in non-DC cases

## Slide 7: Conclusion
For Rel-20 Mobility enhancement, we propose followings
  Proposal 1: Specify L1-SINR measurement
  Proposal 2: Specify the network configurable filter for handling L1-RSRP/L1-SINR variance for the event triggered reporting
  Proposal 3: Support inter-CU LTM without RRC/PDCP anchor change

## Slide 8
Thank you