## Slide 1
Views on Rel-20 Ambient IoT
RP-250150
3GPP TSG RAN#107
Incheon, Korea, March 12th – 14th, 2025
Source: Ericsson
Agenda Item: 15.2.3

## Slide 2: Background
SA1 has specified service requirements for Ambient IoT (A-IoT) use cases in TS 22.369.
The Rel-18 RAN-plenary-level SI TR captures RAN design targets and required RAN functionalities (TR 38.848).
The Rel-19 RAN WG SI focused on a harmonized air-interface design to enable passive and active devices (Devices 1, 2a, 2b) to address a limited set of indoor use cases, including indoor inventory/command (TR 38.769).
The Rel-19 SI was converted into a Rel-19 WI (RP-243326) with a narrower scope, focusing on Device 1 and the deployment scenario and connectivity topology combination D1T1 (scenario D1T1-B).
RAN#106 agreed a way forward (RP-243280) with a Rel-20 workplan that includes Device 2 and D2T2 and a limited number of additional use cases, for which the details are to be discussed in a later RAN plenary meeting.

## Slide 3: RAN#106 agreed way forward for Rel-20 A-IoT
According to RP-243280, the workplan for Rel-20 includes the following:
  Includes D2T2
  Includes Device 2
  A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types in TR38.848 as a starting point.
  Note: work on D2T2, device 2 shall follow the Rel-19 study conclusions, and further down-selection of architecture options for topology 2 may be needed. For indoor use cases, deviations from Rel-19 study conclusion shall be well justified and agreed.
  Details to be discussed at a later RAN plenary meeting, including the need for study phase.
  Co-ordination with SA2/3 is expected.

## Slide 4: Device 2 support & D2T2 support
For D2T2, RAN plenary needs to decide which device types should be supported (Device 1 and/or 2a and/or 2b).
  If Device 1 or 2a is supported, it needs to be clarified which scenarios (D2T2-A1/A2/B) should be supported.
  It needs to be clarified whether the intermediate NR UE and A-IoT device can be guaranteed to be indoors. Otherwise, we in practice get D4T2 rather than D2T2, which would require further coexistence study for outdoor UE and/or device, increasing the required TU allocation at least for RAN4.
For Device 2 in D1T1, RAN plenary needs to decide whether to include Device 2a or 2b or both.
  If Device 2a is supported, it needs to be clarified if some other scenario than D1T1-B should be supported.
The SA2/SA3 impacts and dependencies are currently unclear and need to be revisited in June.
Definitions:
  Device types, deployment scenarios, and connectivity topologies are defined in TR 38.848 clause 4.
  Cases for combinations of deployment scenarios and connectivity topologies are defined in TR 38.769 clause 4.2.

## Slide 5: On additional use cases: Outdoor T1 solutions have not yet been studied
Several SA1 use cases would be best served by outdoor topology 1 (D4T1).
However, specification of outdoor T1 support would require a new SI on solutions for outdoor T1 support.
  The Rel-19 SI/WI solutions do not address the outdoor SA1 use cases.
  The Rel-19 SI/WI solutions are optimized for passive indoor solutions, makes it extremely challenging to achieve the required coverage and coexistence for outdoor use cases.
  Therefore, outdoor T1 would require a proper SI since it would necessitate a new air-interface design (different from Rel-19) with different targets for coverage, capacity, and coexistence.
  For RAN1, our initial TU estimate for SI+WI for outdoor T1 is 3 TUs per meeting (this is in addition to the number of TUs required for Device 2 support & D2T2 support).
If an SI+WI for outdoor T1 is included in Rel-20 on top of the WI scope on the previous slide (Device 2 support & T2 support), the total required TU allocation for Rel-20 A-IoT would be very large.

## Slide 6: On additional use cases: Challenges in adding outdoor T1 support in Rel-20
Challenges in adding outdoor T1 support in Rel-20:
  Coexistence with 6G
    The outdoor T1 solution should have good coexistence with 6G (e.g., from spectrum sharing and interference points of view), and 6G design is not yet known.
  Market fragmentation
    It needs to be better understood what use cases can be addressed by 6G before an outdoor T1 solution is specified, to avoid market fragmentation/confusion.
  Required TU allocation
    As mentioned on the previous slide, the total required TU allocation would be very large if the SI+WI for outdoor T1 is included in Rel-20 on top of the already agreed WI scope (Device 2 support & D2T2 support).
Considering the challenges in adding outdoor T1 support in the Rel-20 scope, it would be better to study and specify outdoor T1 in a later (6G) release.

## Slide 7: Proposals
Proposal 1:
  For Device 2 support and D2T2 support, clarification is needed for Rel-20 scoping regarding the following:
    For D2T2, what device types (1/2a/2b) and D2T2-x scenarios (x=A1/A2/B/C) to support
    For D2T2, whether and how the intermediate NR UE and device can be guaranteed to be indoors
      If not guaranteed, study of outdoor coexistence for UE and/or device is required.
    For Device 2 in D1T1, what device types (2a/2b) and D1T1-x scenarios (x=A1/A2/B/C) to support
Proposal 2:
  In Rel-20, focus on Device 2 support and D2T2 support, and address outdoor use cases in a later release.