## Slide 1: Proposed scope of Rel-20 Mobility

## Slide 2: LTM Overhead Reduction
Justification for reduction of L1 measurement/reporting overhead
  UE measurement burden is proportional to the number of beams across all candidate cells.
  Selective measurements among configured candidate cell beams can reduce UE measurement burden.
  In Rel-19 LTM, event triggered L1 measurement report are introduced but measurement reporting overhead may still be high, because:
    Network should still rely on periodic L1 reporting or more frequent event triggered L1 reporting for other decisions for LTM operations (e.g., candidate cell management, early DL/UL sync) because the events for L1 MR introduced in Rel-19 are only targeting cell switch decision.
    Based on per-beam L1 event evaluation, multiple L1 MRs can be successively triggered by different beams of the same candidate cell.
  Schemes to omit triggering non-essential measurement report can reduce measurement reporting overhead.
Proposed scope
  Reduction of candidate cell beam measurement overhead, by e.g.,
    Activation/deactivation of candidate cell beam measurements via MAC CE; and/or
    UE autonomous selective beam measurements via candidate cell selection/beam set selection
  Reduction of event triggered L1 measurement reporting overhead, by, e.g.,
    New events to facilitate candidate cell management and RACH-less LTM with minimal measurement reporting overhead.
    Reduction of successive but unnecessary L1 measurement report triggering

## Slide 3: LTM Overhead Reduction
Justification for reduction of early DL/UL synchronization overhead
  To enable RACH-less (C)LTM, network needs to keep receiving L1 measurement report to select a candidate cell eligible for triggering early DL/UL synchronization procedure, which increases UL/DL signaling overhead.
  UE autonomous triggering of early-TA RACH can reduce the UL/DL signaling overhead required to trigger early-RA RACH for (C)LTM.
  RACH-based early TA acquisition can cause the serving cell interruption.
  The use of UE-based TA acquisition eliminates the interruption but UE-based TA acquisition is currently applicable only in the limited case where serving cell and candidate cell are tightly synchronized.
  Extending applicable cases of UE-based TA acquisition can reduce the serving cell interruption caused by RACH to candidate cell.
Proposed scope
  Reduction of early UL synchronization overhead by, e.g.
    UE autonomous triggering early-TA RACH for (C)LTM
    Generalization of UE-based TA for less-synchronized candidate cell

## Slide 4: CLTM Specific Enhancements
Justification for CLTM specific enhancements
  In RACH-less CLTM or CFRA based CLTM, each candidate cell should keep reserving (UL) resources for CLTM, upon being prepared as CLTM candidate.
  This may often lead to no-show, where the candidate cell has to reserve the resources for long time without utilizing it.
  On-demand (or on-the-fly) network resource reservation can alleviate inefficient radio resource utilization due to no-show.
  In Rel-19 CLTM, only CG based approach was introduced for RACH-less CLTM.
  Inefficient radio resource utilization can occur because massive CG resources have to be configured for all beams associated with CLTM candidate cells.
  DG-based RACH-less CLTM cell switch can alleviate inefficient radio resource utilization due to massive CG resource configuration.
Proposed scope
  Minimization of network resource reservation for CFRA/RACH-less CLTM, by, e.g.
    UE indication for on-demand network resource reservation
  Support of DG based RACH-less CLTM cell switch

## Slide 5: Support of Intra-CU CLTM for DC Case
Justification for Support of intra-CU CLTM for DC case
  Due to limited time left, Rel-19 may not be envisioned to support intra-CU CLTM for DC case.
  It is important for 5G mobility feature to support DC case. So, CLTM is necessary to ready for DC case in 5G NR.
Proposed scope
  Intra-CU CLTM for DC case if not supported in Rel-19

## Slide 6: Summary
Justification of Rel-20 Mobility Enhancement WI (Ph5)
  Given the performance benefit and flexible network deployment options that LTM provides, we believe that LTM is a compelling candidate technology for 5G-Advanced and 6G. This motivates further enhancements of LTM in Rel-20, so as to provide differentiated mobility experiences for 5G-A and 6G users.
Preferred work scope (in decreasing priority order)
  LTM overhead reduction
    Reduction of candidate cell beam measurement overhead
    Reduction of event triggered L1 measurement reporting overhead
    Reduction of early UL synchronization overhead
  Conditional LTM specific enhancements
    Minimization of network resource reservation for CFRA/RACH-less CLTM
    Support of DG based RACH-less cell switch
  Supported scenario
    Intra-CU CLTM for DC case if not supported in Rel-19