## Slide 1: View on RAN4 R20 Agenda Item: 15.3 Source: OPPO Document for: Approval
3GPP TSG RAN#107
Incheon, Korea, March 12-14, 2025
RP-250165

## Slide 2: General view on RAN4 Rel-20
NR and 6G will be two parallel tracks in RAN4 R20. Time needs to be well balanced between R20 and 6G in RAN4, and 50% to 50% overall time split is preferred
  More time can be allocate to NR R20 in the beginning
  RAN4 6G works are expected to be increased in later R20
NR R20 needs to focus on real deployment demands
6G enhancements which is beneficial to 5G can also be considered in NR R20 if there is deployment demands

## Slide 3: Potential enhance areas in Rel-20
PC1.5 for 1CC in TN/NTN
SUL/NUL Tx switching period
Flexible CBW
Band combination simplification
MSD simplification if not introduced in R19
Fragment carrier from SID to WID
Tx switching for 3Tx UEs
power class 8 for FR2
RF
RRM
RedCap UE supporting RLM/BFD relaxation
Enhanced RRM requirements for NES
NTN CA/MIMO if feasible
Cross Area
SISO OTA
    More bands to be considered
    Continue XR, NTN OTA if not complete
Dynamic MIMO OTA if not complete in Rel-19
OTA/Test

## Slide 4: PC1.5 for single CC in TN/NTN
Motivation
  Case 1: TN 2Tx FDD PC1.5 in single CC
    TN FDD PC2 was introduced in Rel-17 with 1PA or 2PA architectures. And FDD PC2 is implemented mostly with 1PA architecture which makes possible in supporting FDD PC1.5 with 2Tx.
    In addition to power enhancements, PC1.5 with 2Tx can also provide gains in MIMO throughputs.
  Case 2: TN 3Tx PC1.5 in single CC
    3Layer PC3 and PC2 have been introduced in Rel-19.
    3Layer PC1.5 was also discussed in Rel-19, however, due to many restrictions in Rel-19 MIMO WI (e.g. not supporting TxD) introducing PC1.5 in Rel-19 becomes unnecessarily complex. Therefore, it is desired to introduced single CC 3Tx with PC1.5 in Rel-20 if not supported in Rel-19.
  Case 3: NR NTN PC1.5 in single CC
    NR NTN PC1.5 now only covers non-handheld UE in Rel-19, the handheld UE can be considered in Rel-20 with TxD.
  Case 4: IoT NTN PC1.5 in single CC
    IoT NTN PC1.5 up to now is not supported for both handheld and non-handheld UE.
    However, considering IoT NTN typically has small channel bandwidth and low PAPR, PC1.5 potentially can be supported with both 1PA or 2PA architectures by reusing current NR PAs. This makes PC1.5 is useful in increasing IoT NTN UL coverage, meanwhile keep the whole costs low.
Objectives
  Specify requirements for PC1.5 single CC with following cases
    TN FDD with 2Tx, e.g. AMPR and RSD
    TN TDD and FDD with 3Tx, e.g. MPR/AMPR and RSD
    NR NTN FDD with 2Tx, e.g. MPR/AMPR and RSD
    IoT NTN FDD with 1Tx and 2Tx, e.g. MPR/AMPR and RSD
PC/CC num | TN/NTN | FDD/TDD | Tx num | UE type
PC1.5 1CC cases | TN | FDD | 2T | Handheld and FWA
 | TN | FDD, TDD | 3T | Handheld and FWA
 | NR NTN | FDD | 2T | Handheld
 | IoT NTN | FDD | 1T/2T | Handheld and non-handheld UE

## Slide 5: SUL Tx switching period
Motivation
  Large amount of low price UEs on the market doesn’t support UL MIMO which can only enable one PA at a time.
  One power supplier is used for all the PAs in RFFE.
  Switch period is needed for this UE if want to support SUL band for coverage enhancement.
  However, now spec mandatory 0us switch period which mandates UE to implement two independent Tx chains with at least two power suppliers.
  To improve UL coverage with SUL for these low price UEs, non-zero switch period needs to be introduced.
Objectives
  Introduce Tx switch period (35us, 140us, 210us) for SUL+NUL band combination in Rel-20.
  Study how to enable this feature in early releases, e.g. from R16.
DC power supply
SUL band
NUL band

## Slide 6: Flexible CBW
Motivation
  Operators’ spectrum usually are not exactly the same as CBWs defined in RAN4
  In deployment, operators
    either use smaller CBW and waste spectrum,
    or use larger CBW but suffering interference,
    or use overlapping CA/CBW but it cannot be applied when the spectrum is not large enough (e.g. <10MHz)
  New CBW is requested from time to time but with many controversial debates
  An alternative approach is to introduce flexible CBWs, i.e. CBW is based on the spectrum that operators have in reality. No waste of any spectrum.
Objectives
  Study and specify guard bands and max transmission bandwidth for flexible CBWs in TN and NTN
  Investigate system parameter and RF requirement impacts, make necessary adjustment
  Investigate the impacts to RAN1 and RAN2
  Make sure UE test burden is within a reasonable level, e.g. only test the already defined CBWs (3/5/7/10…)
Range of bandwidth | Irregular spectrum hold by operators (MHz) | Applicable 3GPP CBW
<5MHz | 1, 2.4, 2.46, 2.49, 2.5, 2.51, 2.6, 3.4, 3.69, 3.7, 3.75, 3.8, 4, 4.2, 4.4, 4.6, 4.8, 4.9, 4.92 | No 3GPP CBW can be applied
[5MHz, 10MHz) | 5.03, 5.2, 5.4, 5.5, 5.6, 5.8, 6, 6.2, 6.25, 6.3, 6.4, 6.5, 6.6, 6.8, 7, 7.2, 7.5, 7.6, 7.8, 8, 8.2, 8.3, 8.4, 8.6, 8.8, 9, 9.1, 9.2, 9.3, 9.34, 9.6, 9.7, 9.8, 9.9 | 5MHz (Many spectrums are wasted !)
… | … | …
Min CBW
Max CBW
Freq
Any CBW between min and max can be supported

## Slide 7: Band / band combination simplification
Motivation
  NR has defined 70+ partially overlapping FR1 bands & tens of thousands of CA/DC/EN-DC band combinations caused very high complexity and cost of the network and UE.
  This trend is unsustainable in the future.
Objective
  Study the feasibility and how to harmonize band definition for new spectrum e.g. 6GHz, 7GHz and 8GHz
  Study the feasibility and how to harmonize the re-farming spectrums to form new large bands wherever feasible
  Study the feasibility of introducing “band group” based band combinations, e.g. Low band group + Mid/high band group
Fragmented bands in NR
Harmonized bands
New band X (1.5-2GHz)
New band Y (1.5-1.8GHz)
New band Z (1.8-2GHz)

## Slide 8: RedCap UE supporting RLM/BFD relaxation
Motivation
  The RLM/BFD relaxation has been defined as one of the power saving approaches for NR normal UE in R17.
  These features actually are also very useful for Redcap UE to further reduce the power consumption with the consideration of, e.g., CSI-RS and SSB based, 1Rx and 2Rx.
Objectives
  Specify RRM requirements for Redcap UE to support RLM/BFD relaxation
    Consider CSI-RS based and SSB based relaxation
    Consider both 1Rx and 2Rx

## Slide 9: Enhanced RRM requirements for NES
Motivation
  OD-SSB and always on-SSB can be configured with different periodicities and different carriers in RAN1.
  RAN4 is discussing this scenario under Rel-19 NES WI, however, due to time limitation if not be specified can be considered in Rel-20.
  To support the combined OD-SSB and always on-SSB based L3 measurement:
    One potential solution from time domain:
      NES cell configure multiple SMTCs on the same frequency, when OD-SSB and always on-SSB are not under the same periodicity
    The other potential solution from frequency domain:
      Use additional searcher or only measure one CC in a band when configured with multiple CCs to speed up OD-SSB based L3 measurements in multi-carrier operation.
Objectives
  Support multiple SMTCs in parallel for combined always on-SSB and OD-SSB based L3 measurement
  Support OD-SSB based fast L3 measurement with enhanced CSSF
  Specify corresponding RRM requirements, and if needed, introduce network configuration and UE capability
OD-SSB
AO-SSB
Case 2
Case 1
f1
f1
f2
t
t

## Slide 10: Thanks