## Slide 1: Scope discussion on Ambient IoT
Sources: Panasonic
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda: 9.3.1.7
TDOC: RP-250290
For: discussion

## Slide 2: Background
WG level discussion is ongoing for Ambient IoT. We think following points are worth to some discussion in RAN.
  Specification handling
  Target symbol rate (maximum M value)
  CP handling
  Counter handling

## Slide 3: Specification handling
To have one specification for each RAN1 and RAN2.
  For RAN1 specification, not to merge with 38.211/212/213/214/215 as the structure would be so different. In addition, separate specification could give the impression of independent generation.
  For RAN2 specification, not to merge with existing RAN2 specification as it would show independent MAC design.
  For RAN4 specification, “TS 38.xxx Ambient IoT Base Station (BS) and Carrier-Wave (CW) node radio transmission and reception” was agreed. We assume UE side spec would be specified as similar manner.

## Slide 4: Target symbol rate (maximum M value)
Device 1 should be competitive data rate with UHF RFID.
  Compared with device 2a/b in Rel.20, device 1 in Rel.19 should target a competitive bit rate with smaller coverage. Such design target differences would make distinct target markets.
  M=24 or higher should be target regardless of CP handling in order to be competitive with UHF RFID.

## Slide 5: CP handling
R2D is not required to be orthogonal to NR/LTE.
  Heated RAN1 discussion on how to handle CP.
    Higher symbol rate would be difficult depending on CP handling. Or it would increase the device complexity.
    How timing is acquisitioned with the existing of CP especially higher symbol rate is very difficult discussion.
  RAN4 agreed "to specify RAN4 RF requirements based on the assumption that NR UE is only outdoor in Rel-19".
  In any way, D2R and CW are not orthogonal. The guardband would be required regardless of orthogonality of R2D even if NR 15 kHz SCS and LTE are located in the same indoor.
    NR 30 kHz SCS or higher is always non orthogonal.

## Slide 6: Counter handling
How long and how accurate the counter can count should be guided from RAN e.g. 40ms with 0.5x10^5 ppm
  The accuracy and counter length determines the target design on the complexity.
  The counter clock accuracy after clock calibration should be 10^4 or 10^5 was discussed in RAN1#119.
    Either of the value would be reasonable but the views on complexity/power consumption trade off are different.
    We propose to take middle ground value of 0.5x10^5 as the compromise.
  D2R of TDMA of X>1 depends on the counter length in RAN1 discussion.
  The protocol design related to how long certain configuration are kept in the device depends on how long counter can be supported in the device.
    The order of 40ms would result +/-0.2ms order error with 0.5x10^5 clock.
    It can accommondate TBS of 1000 bits order in one round of R2D->D2R->R2D with M=8 and TDM of X=1.