## Slide 1
RP-250292
3GPP TSG RAN Meeting #107
Incheon, Korea, 12th to 14th March, 2025
Views on Scope for R20 “AI-ML for Air interface”
Agenda Item: 15.2.1
Source: Tejas Networks
Document for: Discussion

## Slide 2
Rel 19 considered the following topics in AI/ML for AI
  AI/ML based CSI compression and prediction
  AI/ML based Beam prediction
  AI-ML based Positioning Enhancements
5G-A Release 20 should focus on the following aspects of AI/ML for AI:
  CSI feedback enhancements phase 2
  Positioning enhancements phase 2
Introduction

## Slide 3
Views
on
Scope for R20
“AI-ML for Positioning Enhancement Phase-2”

## Slide 4
The release-19 of 3GPP studied the AI-ML for Positioning Enhancements but
  The studied was limited to timing information-based Positioning only,
  AI-ML techniques were not considered for training and inference of angle information,
  In Rel-19, the support for case-2a and case-2b is very limited so far.
    With only 2 more meetings remaining, its unlikely to see much progress on these cases.
The reporting of timing information being discussed in Rel-19 alone can’t meeting the positioning accuracy KPIs
  Target KPI:
    2D position error 20 cm for 90% of the users.
    Vertical position error 1.5m for 90% of the users.
The case-2a and case-2b should be discussed and the aspects related to AI-ML for Positioning Enhancement should be standardized.
Motivation
The impact of measurements beyond timing information (such as angle of arrival and departure, etc.) on positioning accuracy should be studied for “AI-ML for positioning enhancements”. Furthermore, the support of 3GPP standards should be extended for case-2a and case-2b.

## Slide 5
The performance of AI-ML-based positioning depends on the correlation between channel measurements collected from user equipment at different locations.
The more correlated and richer the channel measurements are, the easier it will be for the AI-ML model to make accurate inferences about the UE location and/or intermediate measurements (such as time of arrival, angle of arrival/departure, and the LoS/NLoS state).
Reporting channel measurements that include both time and angle information can offer better performance compared to using time alone.
Furthermore, it can reduce the number of TRPs required to achieve the positioning accuracy targets, resulting in reduced network overhead.
Angle and Time-based AI-ML Positioning Enhancements
AI-ML Model
AI-ML Model
PDP information based positioning
PADP information-based positioning

## Slide 6
Work Item for the “AI-ML for Positioning Enhancements Phase 2”:
  Extend the support for the Case-2a and Case-2b of AI-ML based Positioning,
  Based on angle measurements [A study to be performed, followed by the normative work in Release 20]
    For all the 5 AI-ML based positioning use-cases.
    Support for hybrid positioning schemes for AI-ML assisted positioning use-cases.
[RAN-1/2/3]AI-ML for Positioning Enhancement: Phase-2
Proposal
Reporting channel measurements that include both time and angle information can offer better performance compared to using time alone. Furthermore, it can reduce the number of TRPs required to achieve the positioning accuracy targets, resulting in reduced network overhead.
Observation

## Slide 7
Views
on
Scope for R20
“AI-ML for CSI feedback enhancement Phase 2”

## Slide 8
In Rel-19 WI for AI/ML over air interface, the following items were studied:
CSI feedback enhancement [RAN1]:
  For CSI compression (two-sided model), further study ways to:
    Improve trade-off between performance and complexity/overhead
      e.g., considering extending the spatial/frequency compression to spatial/temporal/frequency compression, cell/site specific models, CSI compression plus prediction (compared to Rel-18 non-AI/ML based approach), etc.
    Alleviate/resolve issues related to inter-vendor training collaboration.
while addressing other aspects requiring further study/conclusion as captured in the conclusions section of the TR 38.843.
Background

## Slide 9
The study showed:
  For improved tradeoff between performance and complexity:
    5 more sub-use cases are identified considering temporal aspects with more focus on case 2 and case 3
    Observation shows 20%~30% throughput gains can be achieved compared with legacy eType2 codebook.
  For resolving/alleviating issues related to inter-vendor training collaboration:
    5 major options (and a lot more sub-options) are studied and further consolidated into two major options
    Specification of model or model structure, potentially with model parameter exchange (option 3a-1/3b, Direction C)
    Dataset exchange (option 4-1)
  Scalable model structure with respect to number of Tx ports, CSI feedback payload size, bandwidth.
  Hardware allocation for CSI processing.
We support specification enhancement for AIML CSI compression with model structure specification and model parameter exchange for inter-vendor training collaborations in release - 20.

## Slide 10
Proposal 1: For 5G-A Rel-20 AIML based physical layer enhancements:
  Support specification enhancement for AI/ML based CSI compression with scalable model structure specification and model parameter exchange for inter-vendor training collaborations.
Proposal 2: We recommend work item objectives:
  Sub-use case 2/3, considering temporal aspects, should be completed in Rel-20.
  Option 3a-1/3b (Model/Parameter exchange) should be completed in Rel-20.
Proposal CSI compression