## Slide 1: Post-Deployment Views on AI/ML for the Air Interface
RP-250295
RAN#107
Agenda Item: 15.2.1
March 12th - 14th, 2025
VIAVI Solutions

## Slide 2: Post-Deployment Testing
Post-deployment testing is critical to the success of AI air interface techniques, but little progress has been made in addressing this challenge so far in 5G-A
The following agreements were reached in RAN4#112-bis:
  When operating in the field, two aspects of UE operation may impact performance:
    Update or fine tuning or addition/removal of models, if applicable, resulting in a change of functionality which may impact functionality performance
    Data drift / mismatch between the conditions encountered by the UE in the field and the training data, which may impact functionality performance
  For dealing with potential changes in performance of the functionalities, two options may be available. The options are not mutually exclusive:
    Option 1: Conduct the validation of a change in AI model/functionality before its deployment/activation in already deployed UEs
    Option 2: Using performance monitoring and LCM procedures
Both options are made up mostly of FFS items, as can be seen on the following slide

## Slide 3: Post-Deployment Testing
Options agreed in RAN4#112-bis
Option 1: Conduct the validation of a change in AI model/functionality before its deployment/activation in already deployed UEs
  Validation UE and the UE hardware in which the model is to be deployed/activated.
  FFS whether the validation takes place in the field (i.e., on each individual device) or in the lab conditions (i.e., per device type/model)
  FFS whether validation can be done at the device along with inference for another active functionality(ies)
  FFS on the feasibility
  FFS on one possibility for consideration for option 1 is to capture model input (and if needed other test data such as ground truth) during conformance testing. This stored data can later be used to validate new or updated models.
  Other aspects not precluded.
Option 2: Using performance monitoring and LCM procedures
  Performance monitoring will be designed in other groups
  RAN4 may consider the need and feasibility of requirements and tests to ensure consistency and accuracy of monitoring metrics or other monitoring related data sent from the UE and set requirements as feasible/needed.
  FFS on monitoring can be used for managing fallback, changes in functionality, model update/model switching/model transfer, if applicable
FFS: RAN4 needs to clarify whether changed functionalities that did not pass conformance testing are expected to be activated at the device

## Slide 4: Post-Deployment Testing
Updates from RAN4#114
Renaming of options:
  Option 1: Pre-activation functionality/model update testing
  Option 2: Post deployment management based on LCM
Still a long list of “further potential clarifications” and “significant issues”
Little to no more progress as time is prioritized for completing other work

## Slide 5: Post-Deployment Testing
Observation 1: There is still a significant lack of overall clarity on the most effective and feasible approach for ensuring AI interface techniques meet expected performance requirements post deployment – this needs to be robust and well understood for operators to have confidence in enabling any such techniques in a live network, and thus to ensure effort spent on specification work is not wasted.
Observation 2: We can continue to consider more use cases, but they will all ultimately face similar challenges. Adding more use cases for Release 20 will increase the workload and potentially be irrelevant if a robust solution cannot be established for post-deployment performance and test.
Proposal 1: Allocate sufficient time in Release 20 to further investigate and clarify the gaps for post-deployment testing of AI at the air interface to ensure a solid foundation before Release 21.
Proposal 2: Postpone or minimize the introduction of new use cases until Release 21, as suggested in RP-243292.