## Slide 1
Views on revised WID objective for 6 MIMO layers support
RP-250324
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda: 9.3.4.1
Source: Samsung, Apple, MediaTek
Document for : Discussion and decision

## Slide 2
Background and RAN4 Progress
6 layer feasibility study included in Rel-19 UE RF enhancement (NR_ENDC_RF_Ph4 WI):
  Under the objective of 6Rx for higher frequency band (>2.5GHz) targeting at support of handheld UE
  Support 4 MIMO layers at least, and study the gain and feasibility for 6 MIMO layer, according to WID:
Specify the core requirements to enable 6Rx for higher frequency bands (>2.5GHz) targeting at support of handheld UE for NR FR1 single carrier scenario
  Example bands: n41, n77/n78, n79, n104
  Support 4 MIMO layers at least, and study the gain and feasibility and if feasible, support 6 MIMO layers
  Specify the Rx requirements including reference sensitivity requirements for support 6Rx
    Note: the specified requirements can be applicable to both handheld UE and FWA devices
Status for 6 layer feasibility study till RAN4#114:
  After several meeting, RAN4 is still unable to conclude on a common set of simulation assumption to determine feasibility of 6 layer for handheld UE In Rel-19, as captured RAN4 chair notes:
  Agreement achieved in RAN4#114 as compromised WF [R4-2503014]:
RAN4 Chair to take note of the following in the meeting report:
- “RAN4 unable to conclude on a common set of simulation assumptions to determine feasibility of 6 layer for handheld UE In Rel-19”
Way Forward:
6-layer performance requirements will be only defined for FWA.
4-layer performance requirements will be defined and will apply to FWA and handheld UE devices.
The fact that 6-layer is only supported for FWA shall be explicitly captured at least in the RAN4 specifications.
Introduce 6 MIMO layers support as an optional feature only for FWA.

## Slide 3
Proposal 1: NR_ENDC_RF_Ph4 WID core and performance part objectives are revised to reflect RAN4 agreement:
  Revision to core part objective:
  Revision to performance part objective:
Proposal on Revised WID
6Rx for handheld and FWA UE [RAN4, RAN1]
Specify the core requirements to enable 6Rx for higher frequency bands (>2.5GHz) targeting at support of handheld UE for NR FR1 single carrier scenario
  Example bands: n41, n77/n78, n79, n104
  Support 4 MIMO layers at least, and study the gain and feasibility and if feasible, support 6 MIMO layers
  Introduce 6 MIMO layers support as an optional feature only for FWA.
    Note: The fact that 6-layer is only supported for FWA shall be explicitly captured at least in the RAN4 specifications.
  Specify the Rx requirements including reference sensitivity requirements for support 6Rx
    Note: the specified requirements can be applicable to both handheld UE and FWA devices
  Specify the requirements to support SRS antenna switching including t1r6, t2r6, t3r6, depending on UE capability
    RAN1 to study and specify, if necessary, SRS antenna switching to support 3T6R depending on UE capability.
      Note: RAN1 discussion starts from RAN1#118bis (Oct. 2024)
  Study the issue of insertion loss imbalance across SRS ports, and if justified, specify the corresponding solution.
6Rx for handheld and FWA UE
Specify the performance requirements to enable 6Rx on higher frequency bands (>2.5GHz) targeting at support of smartphone for NR FR1 single carrier scenario
  Investigate and if necessary, specify RLM test cases to support 6Rx
  Specify UE PDSCH demodulation performance and CSI requirements to support 6 Rx
    Support 4 MIMO layers at least, and follow the conclusion in core part for whether to support 6 MIMO layers
    6 MIMO layers performance requirements will be only defined for FWA.
    4 MIMO layers performance requirements will be defined and will apply to FWA and handheld UE devices.
  Specify the SDR requirements to support 6Rx