## Slide 1: Views on Rel-20 NG-RAN AI/ML Enhancements
RP-250332
Agenda : 15.2.6
RAN#107
Incheon, Korea
Mar 12-14,2025

## Slide 2
Background
In Release 18 AI/ML for NG-RAN WI, the following use cases were specified:
  AI/ML based Load Balancing
  AI/ML based Mobility Optimization
  AI/ML based Energy Savings
In Release 19 AI/ML for NG-RAN WI, the following new use cases and some leftovers from Rel-18 were addressed
  AI/ML based Network Slicing
  AI/ML based Coverage and Capacity Optimization
  Leftovers from Rel18 – AI/ML for NR-DC, AI/ML in Split gNB Architecture and Continuous MDT

## Slide 3
Objective | To enhance and optimize the LTM mobility using AI/ML techniques for improved performance
Motivation | AI/ML based LTM can provide following benefits – Optimized selection of LTM candidate cells Optimized trigger for early synchronization and Cell Switch Command Minimization of LTM reconfigurations/signaling overhead reduction
Proposal | Study and enhance intra and inter gNB LTM (including conditional LTM) with AI/ML for both split and non-split gNB
New Use Case – AI/ML based LTM

## Slide 4
Objective | Consider RAN1/2 AI/ML use cases on beam management and mobility optimization output as input for NG-RAN AI/ML Mobility Optimization (RAN3)
Motivation | Beam prediction from the UE and/or Network and RRM measurement prediction from the UE can be used for NG-RAN AI/ML based mobility optimization to select appropriate target cells and beams. AI/ML based Beam Management needs to be supported in Split gNB.
Proposal | Study and enhance NG-RAN AI/ML based Mobility optimization by taking beam and measurement predictions from UE and Network into account in disaggregated gNB. Study and support AI/ML based Beam Management in split gNB
Enhancement – Mobility Optimization taking UE Predictions into account

## Slide 5
Objective | To enhance and optimize Network Energy Savings with AI/ML
Motivation | AI/ML can be applied to enhance the Network energy savings for - Cell DTX/DRX Cell (de)Activation, sleep mode, OD-SSB, OD-SIB1 NES handovers
Proposal | Study and enhance AI/ML based Network Energy Savings for both split and non-split gNB
Enhancement – AI/ML based Network Energy Savings

## Slide 6
Summary Proposals
Proposal 1: Study and enhance intra and inter gNB LTM (including conditional LTM) with AI/ML for both split and non-split gNB
Proposal 2a:Study and enhance NG-RAN AI/ML based Mobility optimization by taking beam and measurement predictions from UE and Network into account in disaggregated gNB.
Proposal 2b:Study and support AI/ML based Beam Management in split gNB
Proposal 3: Study and enhance AI/ML based Network Energy Savings for both split and non-split gNB